## Slide 1: WF on UE capability on intraBandENDC-Support
Huawei, HiSilicon, []
R4-2103130
3GPP TSG-RAN WG4 #98-e
Jan 25 – Feb 05, 2021
Electronic meeting

## Slide 2: WF1: interpretation of intra-band EN-DC contiguous and non-contiguous Band combination
  RAN4 decide on the option in next meeting:
  Option 1: For intra-band ENDC, If LTE sub block is contiguous with NR sub block, it is contiguous EN-DC. Otherwise, it is non-contiguous. (If the channel spacing between LTE carrier and adjacent NR carrier are contiguous, i.e., the channel spacing is equal to or less than the nominal channel spacing of EN-DC channel spacing specified in TS 38.101-3)
      E.g. downlink DC_48A_(n)48AA is an intra-band contiguous EN-DC band combination
  Option 2: The entire LTE and NR spectrum are contiguous, i.e., all carriers are contiguously spaced. In other word, all the adjacent carriers including intra LTE carriers and intra NR carriers are contiguously spaced
    E.g. downlink DC_48A_(n)48AA is an intra-band non-contiguous EN-DC band combination
    Following issues can be considered on how to deal with the options:
    In TS 38.306, it is specified: An intra-band non-contiguous band combination is not considered to be a fallback band combination of an intra-band contiguous band combination.
    If UE indicate intrabandENDC-support as non-contiguous with LTE CA_48A-48A and NR ban n48A, does UE support both DC_48A_(n)48AA and DC_48A-48A_n48A? If not, how to distinguish DC_48A_(n)48AA and DC_48A-48A_n48A capability.
    If UE indicate intrabandENDC-support for both contiguous and non-contiguous together, does UE support all mixed case of contiguous and non-contiguous like DC_48A_(n)48AA?

## Slide 3: WF2: intraBandENDC-Support for DL and UL ambiguity
  FFS if IntraBandENDC-Support IE need to be indicated in UL and DL separately per band combination, following aspects can be considered:
    How to deal with the issue: there are several intra-band EN-DC parts with different support of contiguous/non-contiguous carriers.
      E.g. For DC_(n)48CA case, DL configuration could fall back to non-contiguous DC_48A-n48A, if UE indicate support IntraBandENDC-Support as both(contiguous and non-contiguous), gNB could configure DC_48C_n48A to the UE, while UE dose not support in fact.
    If Separately UL and DL indication on intraBandENDC-Support is needed, how to deal with Rel-15 signaling
    Can we Add limitation to solve the UL and DL ambiguity that: only both DL and UL including its fallback are contiguous, then the combination is contiguous. Otherwise, the combination is non-contiguous.
    Can we Add limitation to solve the UL and DL ambiguity that: For intra-band ENDC band combinations more than 2 CCs, if IntraBandENDC-Support indicated with default value(contiguous), only intra-band contiguous EN-DC UL configuration is allowed to configure to the UE.

## Slide 4: Reference
[1] R4-2102952, Email discussion summary for [98e][104] NR_NewRAT_UE_RF_Part_3, Huawei, HiSilicon, RAN4#98-e
[2] R4-2102559, Clarification of intra-bandENDC-Support, Nokia, RAN4#98-e
[3] R4-2102628, on UE capability for intra-band ENDC, Huawei, HiSilicon, RAN4#98-e