## Slide 1: WF on new per BC indication of the per-FR gap
CMCC
3GPP TSG-RAN WG4 Meeting # 98-e R4-2103168
Electronic Meeting, Jan. 25-Feb. 5, 2021

## Slide 2: Background: potential constraints for per UE indication of per-FR gap capability
Some companies indicate that for some UE implementation, the current per-UE based capability signaling will make the feature difficult for FR1+FR2 capable UE to support it because many different requirements associated to the feature shall be fulfilled even for the highest order of CA combination that can be supported by the UE
  For example, if UE is configured with the highest order CA combination it can support, per-FR MG capable UE may not be able to process both measurement on one band and control/data processing on the other band concurrently

## Slide 3: Background: Potential constraints for per UE indication of per-FR gap capability
  Some companies indicate that the requirements for some procedures that are not functionally related to measurements are dependent on per-FR gaps, which cause difficulty for UE to implement the per-FR gap feature.
  Some R15 and R16 features and RRM requirements are defined based on the gap capability (per-UE or per-FR), i.e. interruption requirements, parallel processing of BWP switching on multiple CCs and conditions for NR-DC multiple SCells activation requirements.
  If the UE wants to indicate the per-FR gap capability, it has to guarantee that it could fulfill the measurement requirements related to the gap capability and also the requirements mentioned above (i.e. interruptions, delay) under all cases.

## Slide 4: Way forward
Further discuss and identify the implementation constraints.
Further identify which requirements dependent on per-FR gaps cause burden in UE’s baseband complexity or difficulty for UE to implement the per-FR gap feature.
FFS on how to solve the constraints if any:
  Option 1: Keep the original per UE per-FR gap indication and add new Per BC indication for the per-FR gap capacity.
    So far, companies have not identified any compatibility issue in RAN4 by combining the original per-UE indication and the per-BC indication
  Option 2: Discuss in a case-by-case manner to check whether some requirements that were agreed to be introduced for per-FR gap capable UE cause some constraints. If so, RAN4 can discuss and investigate whether to revisit the previous agreement and the compatibility issues.

## Slide 5: Reference
R4-2101659, Discussion on per-FR gap capability, Huawei, HiSilicon.
R4-2014488, Overloading of the Per-FR gap capability, Qualcomm Incorporated