## Slide 1: Way forward on NC UL CA PC2 requirements
ZTE, [...]
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan – 5 Feb, 2021
R4-2103238
Agenda item: 11.2.2.5
Document for: Approval

## Slide 2: WF(1)
The following two points that were applied to PC2 intra-band contiguous UL CA, can be applied for PC2 intra-band NC UL CA:
  -No need to consider different power class configuration of each CC,
  -Adopt same UL/DL configuration and synchronized condition.

## Slide 3: WF(2)
P-MPR is available for the UE for SAR mitigation method
Duty cycle based SAR solution: Re-use the contiguous ULCA handling of MaxUplinkDutyCycle. The IE should be the same what is decided in contiguous UL CA for PC2.
  Some candidate options for IE as recommended by moderator:
    Option 1. Follow contiguous ULCA and use the same IE,
    Option 2. Develop NC UL CA dedicated
    Option 3. Use the single CC parameter
  - Agreement: Option3?

## Slide 4: WF(3)
Pcmax: re-use Pcmax from PC3 intra-band NC UL CA:
  Changes to 38.101-1, if any, are FFS
Fallback behavior: same fallback behavior as single carrier PC2. i.e. fallback to the corresponding PC3 intra-band non-contiguous CA in case of the dutycycle condition is not met.
Define +2/- 3 dB as tolerance for power class 2.
Emissions apply to the sum of antenna power
Spurious emissions, SEM and UE-to-UE co-ex same as PC3 NC UL CA
Same ACLR definition than for PC3 NC UL CA but with ACLR value at 31dB
In gap exceptions are FFS

## Slide 5: References
R4-2102185, ” Discussion on PC2 intra-band non-contiguous NR CA”, ZTE
R4-2102985, ”Email discussion summary for [98e][137] NR_RF_FR1_enh_Part_3” Qualcomm Inc.