## Slide 1: WF on system parameters and operating CBW in n14 for NR SL enhancement
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25th Jan. -05th Feb., 2021
Agenda item: 11.10.2
Document for: Approval
R4-2103242
CATT, AT&T…

## Slide 2: Background
In Rel-16 NR V2X WI, the principle of introducing CBW for NR V2X licensed bands was agreed:
  Channel bandwidths defined for NR V2X licensed band should be a subset of UE channel bandwidths for the same licensed band in NR.
In the 1st round, AT&T proposes the same principle agreed in LTE to be followed so that the UE can utilize 5 MHz or 10 MHz CBW for n14 SL.

## Slide 3: Issue 1-1-1: System parameters on CBW
  In 1st round, the following agreement is reached:
  Option 1: Follow same principle to decide the supported CBW in public safety and other SL operation. (See the principle in slide 2)

## Slide 4: Issue 1-2-2: CBW for SL operation
  Candidate options of CBW based on operator’s request
  Option 1: Only allow 10MHz CBW in n14.
  Option 2: Both 5MHz and 10MHz CBW in n14.
  Recommended WF
  Based on the candidate options, RAN4 further discuss on the supported CBW in n14.

## Slide 5: Issue 1-1-2: System parameters on Channel raster
  Candidate options of channel raster
  Option 1: 7.5 kHz shift will be considered in NR SL refarming bands (e.g. n14) to use LTE Uu/ProSe and NR SL operation in a spectrum sharing manner. If only NR SL operation is allowed, then NR Uu channel raster will be considered.
  Option 2: Regardless of sharing LTE prose/SL and NR SL, RAN4 firstly need to decide which channel raster will be considered for SL enh. operation
  Recommended WF
  Based on the candidate options (can be multiple choice), RAN4 further discuss the general principle for channel raster.

## Slide 6: Reference
[1] R4-2102990, Email discussion summary for [98e][142] NRSL_enh_part1, Moderator (LG Electronics), RAN4#98e
[2] R4-2100417, System parameters for newly introduced SL bands, CATT, RAN4#98e
[3] R4-2101857, Additional Information for SL Operation in NR Band n14, AT&T, FirstNet, RAN4#98e
[4] R4-2102342, Bandwidth for SL operating in n14, Ericsson, RAN4#98e