## Slide 1: WF on co-existence simulation assumptions for PC2 NR V2X
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25th Jan-05th Feb., 2021
Agenda item: 11.10.5
Document for: Approval
R4-2103251
CATT, LGE,…

## Slide 2: Background
In the 1st round, the following agreement is reached regarding ACLR for PC2 NR V2X in licensed band n38 (2570~2620MHz):
  ACLR should be determined based on co-existence simulation.
RAN4 has decided that there is no need to further study the adjacent channel co-existence for PC2 NR V2X in ITS band n47.
In Rel-16, the coexistence simulations for PC3 NR V2X in ITS band, FR1 FDD licensed band and FR1 TDD band have been performed and the methodology can be considered as baseline for PC2 NR V2X.
The co-existence simulation assumptions for PC2 NR V2X in licensed band n38 are captured in this WF based on RAN4 consensus.

## Slide 3: Adjacent channel coexistence scenarios
NR V2X operating frequency |  | Deployment scenarios (Aggressor-to-Victim)
FR1 | Scenario A: V2X service at licensed band where only NR SL is supported. (TDD: 2.6GHz) (2nd priority) | Case1: PC2 NR V2X UE-to- PC2 NR V2X UE Case2: PC2 NR V2X UE-to- PC3 NR V2X UE
 | Scenario B: V2X service at licensed bands where NR SL and NR Uu are supported. (TDD: 2.6GHz) (1st priority) | Case3: PC2 NR V2X UE-to-NR Uu BS Case4: NR Uu UE-to- PC2 NR V2X UE
  The potential adjacent channel coexistence scenarios in licensed band n38 are shown below:

## Slide 4: Layout model
  For Scenario A, the layout model specified for ITS band in TR 38.886 clause 5.2.1.1 can be reused.
  For Scenario B, the layout model specified for FR1 TDD band in TR 38.886 clause 5.2.3.1 can be reused.

## Slide 5: Simulation parameters for Scenario A
Parameter | Value | 
 | NR V2X UE (Aggressor) | NR V2X UE (Victim)
Tx power | 26dBm | 23dBm or 26dBm
Channel Bandwidth | 20MHz | 20MHz
Packet size | 1) 14 PRB (190 byte packet) for 15kHz SCS 2) Other options are not precluded | 1) 14 PRB (190 byte packet) for 15kHz SCS 2)Other options are not precluded
Traffic model | 1 transmission every 100ms 100ms message generation period Time instance of message generation is randomized among vehicles | 
Noise figure | 9dB | 9dB
Antenna pattern | Omni-directional with gain of 0 dBi | 
Sidelink Power control | The worst case of no power control is used | 
SINR-to-BLER mapping | As per link level performance model in TR 38.xxx Table A-x for 2.6GHz | As per link level performance model in TR 38.xxx Table A-x for 2.6GHz

## Slide 6: Simulation parameters for Scenario B
Parameter | Value |  | 
 | NR UE | NR BS | NR V2X UE
Max Tx power | 23dBm or 26dBm | NA | 26dBm
Channel Bandwidth | 20MHz | 20MHz | 20MHz
Packet size | 1) [32] PRB for 15kHz SCS 2)Other options are not precluded |  | 1) 14 PRB (190 byte packet) for 15kHz SCS 2)Other options are not precluded
Traffic model | Full buffer | Full buffer | Reference table 5.2.1.2-1
Noise figure | N/A | 5dB | 9dB
Antenna pattern | Omni-directional with gain of 0 dBi | Antenna pattern for FR1 Macro BS from TR 38.828 | Omni-directional with gain of 0 dBi
SINR-to-BLER mapping for NR V2X | NA | NA | As per link level performance model in TR 38.xxx Table A-x for 2.6GHz
SINR-to-rate mapping for NR | NA | As per link level performance model in TR 36.942 (Table A.2). α, attenuation = 0.4, SNIRMIN, dB = -10, SNIRMAX, dB = 22 (subclause 5.2.3.6 from TR 38.828). | NA

## Slide 7: ACLR and ACS for Scenario A
  1 step ACLR/ACS model
Parameter | Value | 
 | NR V2X UE (Aggressor PC2) | NR V2X UE (Victim PC3/PC2)
ACLR | 31 + X dB | 30dB/31dB + X dB
ACS | 27+ X dB | 27dB/27dB + X dB

## Slide 8: ACLR and ACS for Scenario B
  1 step ACLR/ACS model
Parameter | Value |  | 
 | NR UE (PC3/PC2) | NR BS | NR V2X UE (PC2)
ACLR | 30 dB/31 dB | NA | 31 + X dB
ACS | NA | 46 dB | 27 + X dB

## Slide 9: Power control
  For Scenario A, OLPC in TR36.786 can be reused or no power control is used.
  For scenario B, the power control specified for FR1 TDD band in TR 38.886 clause 5.2.3.4 can be reused.

## Slide 10: Reference
[1] R4-2102992, Email discussion summary for [98e][144] NRSL_enh_Part_3, Moderator (Huawei, HiSilicon), RAN4#98e
[2] R4-2101937, Discussion on n47 PC2 MPR simulation of Rel-17 SL enhancement, Huawei, HiSilicon, RAN4#98e
[3] R4-2100420, Discussion on PC2 for SL enhancement, CATT, RAN4#98e
[4] TR 38.886 V16.2.0, User Equipment (UE) radio transmission and reception