## Slide 1: WF on NTN RRM measurement requirements
Qualcomm Inc.
3GPP TSG-RAN4 Meeting #98-e
Electronic Meeting, 25th Jan. – 5th Feb., 2021
Agenda item: 11.8.4
R4-2103682
Document for: Discussion

## Slide 2: Background
Based on the 1st round of email discussion summary R4-2103476, proposals, conclusion, and observation are prepared for the 2nd round discussion.
Issue #6-10 of reference models is excluded since it is captured in RF session topics.

## Slide 3: General RRM requirements (Issue #6-1)
Proposal: The following RRM requirements are the candidates to be discussed for NTN RRM measurement. More items may be added pending on the progress in other WGs.
 | Parameter | Parameter Name
RRC IDLE /INACTIVE state | Cell Re-selection | UE measurement capability
 |  | Measurement and evaluation of serving cell
 |  | Measurements of intra-frequency NR cells
 |  | Measurements of inter-frequency NR cells
RRC CONNECTED state | Handover Parameters - NR Handover | NR Handover
 | RRC Connection Mobility Control | RRC Re-establishment
 |  | Random access
 |  | RRC Connection Release with Redirection
 | General measurement requirement | Measurement gap
 |  | UE Measurement capability
 | NR intra-frequency measurements | Requirements applicability
 | NR inter-frequency measurements | Requirements applicability
 | NR measurement accuracy requirements | Intra-frequency SS-RSRP/RSRQ/SINR accuracy, including absolute and relative accuracy
 |  | Inter-frequency SS-RSRP/RSRQ/SINR accuracy, including absolute and relative accuracy
 |  | SS-RSRP/RSRQ/SINR Measurement report mapping

## Slide 4: RRM procedures based on UE position (Issue #6-2/3)
Proposal: RAN4 shall consider requirements for A-GNSS in 38.171 as a starting point when defining requirements for further RRM procedures based on UE position. RAN4 needs to verify if existing A-GNSS requirements are sufficient for position/location based new procedures introduced by other working groups, if any. FFS on whether/how to consider following aspects:
  update period and accuracy of satellite/HAPS PVT
  lossy compression of PVT information
  time/frequency error propagation from feeder link(s)
Conclusion: How to configure SMTC and/or MG considering propagation delay information from satellite/HAPS is not in the scope of RAN4 unless requested otherwise by other working group(s), e.g. RAN2

## Slide 5: Measurements and Mobility (Issue #6-4/5/6)
Proposal: RAN4 to discuss measurement and mobility for the following scenarios
  Intra-NTN for both RRC Connected and Idle/Inactive modes with higher priority
    between GEO type satellites
    between LEO type satellites at the same altitude
      between earth fixed cells or between earth moving cells
      FFS: whether/which to prioritize
    depending on satellite/cell deployment topologies consider both scenarios where cells are within a satellite and belong to different satellites
    FFS: between HAPs
  between NTN and TN for RRC Inactive/Idle modes
  (note) not all possible mix of scenarios may be available

## Slide 6: Measurements and Mobility (Issue #6-4/5/6)
Proposal: For the existing mobility methodologies, RAN4 to study whether the existing requirements can be reused for NTN scenarios, e.g.
  S-criteria based cell (re)selection
  Time- or timer-based CHO
Proposal: For location-based mobility methodologies, RAN4 to discuss the following when relevant detailed procedures are provided by RAN2
  Cell (re)selection
  CHO

## Slide 7: Interruption/Measurement Gaps for GNSS Measurements (Issue #6-7)
Observation: FFS: whether interruptions or measurement gaps is expected for GNSS measurements during NTN operation.
  Companies are encouraged to investigate further and provide input if any technical issues are found. If any, RAN4 to discuss whether/how to define interruption and/or measurement gap for GNSS measurement in detail.
[information-only] Technical comment from Apple:
In RF discussion, the NTN GTW session agreed in RAN4#98e to work on both S- and L-band for the WI. We did not see big issue in terms of interference between GNSS and S-band, but L-band UL is very close to GNSS. So, we are not sure if there is a potential issue for that combination from IDC harmonic/emission interference perspective. If the IDC harmonic/emission interference exists and is not negligible, we may consider to protect GNSS measurement from aggressor NTN transmission. Secondly, this case is different from legacy NR, because NTN capable UE is mandatory to support GNSS measurement and also GNSS measurement is essential for NTN connection. We think all these IDC interference aspects have to be checked by RAN4 RF session, and we are also checking with our RF experts.
[Information-only] Technical comments from THALES
For exemplary L-band (see the GTW agreement from [98e][310]), NTN UE in-device coexistence study with GNSS may be required for this band.
Moreover, for the time being it is not clear the impact of interruption/measurement gaps on the UE capability to synchronize. It also depends on the type of constellation, the width and the type of cell (e.g. if Earth fixed cell or Earth moving cell).

## Slide 8: New SMTC and Measurement Gaps (Issue #6-8/9)
Proposal: RAN4 to study the following aspects for further discussion of (new) SMTC and Measurement Gap based requirements in NTN
  Propagation delay and/or reception power differences between cells
    between GEO type satellites
    between LEO type satellites at the same altitude
      between earth fixed cells or between earth moving cells
      FFS: whether/which to prioritize
    depending on satellite/cell deployment topologies consider both scenarios where cells are within a satellite and belong to different satellites
    FFS: between HAPs
    whether/how to account for delay propagation from feeder link is up to RAN1/RAN2 assumption/design
  Detailed requirements will be discussed when RAN2 solutions, if any, are provided
  FFS: whether/how to split detailed work between Rel-17 work items, NTN and MG enhancement