## Slide 1: Way forward on NR-U PRACH demodulation requirements
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, Jan. 25-Feb. 5, 2021
Agenda: 7.1.7.4.4
R4-2103808
Document for: Approval
Nokia, Nokia Shanghai Bell

## Slide 2: Background
Agreed WFs for in previous meetings
  RAN4 #96-e
    R4-2012611, Way Forward on NR-U BS demodulation requirements
    R4-2012610, Way Forward on NR-U UE demodulation requirements
  RAN4 #97-e
    R4-2017611, Email discussion summary for [97e][316] NR_unlic_Demod_BS
    R4-2017688, Way forward on NR-U BS demodulation requirements for general part and PUSCH
    R4-2017467, Way forward on PUCCH demodulation requirements
    R4-2017468, Way forward on PRACH demodulation requirements
Corresponding Email summary in RAN4#98-e
    R4-2103934 Email discussion summary for [98e][317] NR_unlic_Demod_BS
      The issues related to PRACH are:
        Issue 4-1-1: PRACH format
        Issue 4-1-2: Propagation conditions
        Issue 4-1-3: Ncs
        Issue 4-1-4: Time error tolerance for PRACH under AWGN and TDLC-300-100
        Issue 4-1-5: Time error tolerance for TDLA-30-10

## Slide 3: PRACH performance requirements
PRACH formats
  A2, B4, and C2
  Propagation conditions
    AWGN
    Fading channel TDLA30-10
  Frequency offset
    0 Hz for AWGN
    400 Hz for TDLA30-10
  Ncs
    164 for LRA=1151 and 190 for LRA=571

## Slide 4: PRACH performance requirements
Test scenario parameters
  Time error estimation tolerance
    Reuse the time error tolerance for Rel-15 PRACH performance requirements under AWGN
  Time error estimation tolerance for TDLA30-10
    0.67us for LRA=1151 and 0.41 us for LRA =571.
SCS | AWGN
15 kHz | 0.52 us
30 kHz | 0.26 us

## Slide 5: Declaration field for long PRACH
Create new declaration field for extended PRACH sequences in 38.141-1 which includes format, SCS, and LRA.
[D.111] | PRACH format with LRA = 1151 and LRA = 571 and SCS | Declaration of the supported PRACH format(s) as specified in TS 38.211 [17], i.e., format: A2, B4, C2. Declaration of the supported SCS(s) per supported PRACH format as specified in TS 38.211 [17], i.e., 15 kHz, 30 kHz or both.
[D.111] | PRACH format with LRA = 1151 and LRA = 571 and SCS | Declaration of the supported PRACH format(s) with LRA=1151 and LRA=571 as specified in TS 38.211 [17], i.e., format: A1, A2, A3, B4, C0, C2. Declaration of the supported SCS(s) per supported PRACH format, as specified in TS 38.211 [17], i.e., 15 kHz, 30 kHz or both, as well as sequence length other than LRA =139, i.e. LRA =1151 for 15 kHz SCS, and LRA =571 for 30 kHz SCS
Option 1
Option 2

## Slide 6: Applicability rules
Reuse the Rel-15 test applicability rules for different PRACH formats, i.e. Unless otherwise stated, PRACH test requirements shall apply only for each PRACH format declared to be supported (see [D.111] in table 4.6-1)
Applicability rules for different subcarrier spacings: Unless otherwise stated, for each PRACH format with LRA =1151 and LRA =571 declared to be supported, the tests shall apply only for the supported subcarrier spacing. If both 15kHz and 30kHz SCS are declared to be supported, the tests shall be done for 30kHz SCS. (see [D.111] in table 4.6-1).

## Slide 7: PRACH performance requirements
Consolidated parameter table
Parameter | Value
PRACH formats | A2, B4, C2
Antenna configuration | 1x2
Propagation conditions | AWGN and TDLA30-10
Frequency offset | 0 Hz for AWGN 400Hz for TDLA30-10
NCS | 164 for LRA = 1151 (15 kHz SCS) 190 for LRA = 571 (30 kHz SCS)
Test metric | false alarm probability ≤ 0.1% Probability of detection ≥ 99%
Time error estimation tolerance |  | 
SCS | AWGN | TDLA30-10
15 kHz | 0.52 us | 0.67 us
30 kHz | 0.26 us | 0.41 us