## Slide 1: WF on NR eMIMO demodulation and CSI requirements
Samsung
3GPP TSG-RAN WG4 Meeting #98-e
Electronic,25th Jan– 5th Feb 2021 Agenda Item: 7.9.4
R4-2103825 Document for: Approval

## Slide 2: Background
      Agreed WFs for demodulation requirements for NR eMIMO WI in previous meetings
        R4-2002419 WF on demodulation and CSI requirement for NR eMIMO, RAN4 #94-e
        R4-2002420 WF on PDSCH demodulation requirements based on multi-TRP transmission for NR eMIMO, RAN4 #94-e
        R4-2005529 WF on PDSCH demodulation requirement and general aspects for NR eMIMO, RAN4 #94e-Bis
        R4-2008813 WF for general and PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes(eMBB), RAN4 #95-e
        R4-2008814 WF for PDSCH requirements with Single-DCI based multi-TRP/Panel transmission schemes (URLLC), RAN4 #95-e
        R4-2008815 Simulation assumption for PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes, RAN4 #95-e
        R4-2008816, WF on PMI Reporting Test Cases with Rel-16 Type II Codebook, RAN4 #95-e
        R4-2012662, WF for general and PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes (eMBB), RAN4 #96-e
        R4-2012663, WF for PDSCH requirements with Single-DCI based multi-TRP/Panel transmission schemes (URLLC), RAN4 #96-e
        R4-2012664, Simulation assumption for PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes, RAN4 #96-e
        R4-2012761, WF on PMI Reporting Requirement for NR eMIMO, RAN4 #96-e
        R4-2017529, WF on NR eMIMO PDSCH requirement, RAN4 #97-e
        R4-2017530, Simulation assumption for PDSCH requirements with Single-DCI SDM scheme and Multi-DCI transmission schemes, RAN4 #97-e
        R4-2017531, WF on PMI reporting requirements for NR eMIMO, RAN4 #97-e

## Slide 3: PDSCH requirements

## Slide 4: Abbreviation of TRP in 38.104
Modify TRP to TRxP and add the abbreviation into sub clause 3.3 of 38.101-4 spec as ‘Transmission and Reception Point’

## Slide 5: FRC
FRC for single-DCI based FDM scheme A
  It’s RAN4 common understanding, TBS determination for FRC of single DCI based FDM scheme A based on full resource allocation BW
FRC for single-DCI based inter-slot TDM scheme
  Introduce new FRC for single-DCI based inter-slot TDM scheme with two TRS resources configuration every 20ms with additional note as
    Throughput is calculated under the assumption of repetition number 2
  Reference channel
    R.PDSCH.1-11.2 FDD: sDCI based Inter-slot TDM in FDD
    R.PDSCH.1-16.2 TDD: sDCI based Inter-slot TDM in TDD

## Slide 6: Test Parameters
Antenna port index for FDM scheme A
  {1000,1001} DMRS antenna port index for TCI state#1 and TCI state#2
Antenna port index for inter-slot TDM scheme
  {1000} DMRS antenna port index for TCI state#1 and TCI state#2
Note: For more details please refer to R4-2101449

## Slide 7: Requirement definition for 38.101-4
Introduce SNR requirements for the agreed test cases with following definition
  SNR= average of impairment results +extra margin
  Extra margin
    64 QAM : 0.8 dB
    16 QAM : 0.5 dB

## Slide 8: PDSCH requirement derive
Introduce SNR requirements with [] based on the simulation summary R4-2100903 submitted in RAN4#98-e meeting
Companies are encouraged to further align the results and update the simulation results in RAN4#98bis-e meeting
  In RAN4#98bis-e, for the test cases that the result span in ideal results among companies’ larger than [2.5]dB, RAN4 does not consider the farthest result(s) from the ideal AVERAGE value, until the span becomes within [2.5]dB. The final requirements are derived from AVERAGE impairment results with corresponding ideal results whose span is within [2.5]dB.
  Note: The threshold, [2.5]dB, can be discussed in RAN4#98bis-e meeting

## Slide 9: CSI requirements

## Slide 10: Enhanced Type II Test Setup
Introduce Rel-16 Type II codebook requirements with test metric as following PMI (eTypeII codebook)/Random PMI (Type I codebook)

## Slide 11: Test Parameters-I
Number of CSI-RS ports:
  16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  R = 1
Codebook parameter configuration
  paramCombination-r16: 6, with L =4, pν =1/2, β=1/2
Sub-band Size:
  4 for FDD with 15kHz SCS, 10MHz CBW
  8 for TDD with 30kHz SCS, 40MHz CBW
MIMO correlation
  XP Medium
Test point
  90% of TP

## Slide 12: Test Parameters-II
Channel Model
  TDLA30-5
MCS and Rank
  MCS 20 (64QAM Table), Rank 2
Beam-Steering Model
  How to specify beam steering model into specification.
    Same as specified in B.2.3B.4A of TS 36.101
Beam-Steering Approach
  Enable two independent beam directions applying the beam for both eType II and Type I cookbook simulation
  The remaining parameters will be same as for Rel-15 Type II codebook simulation assumptions in R4-2103846

## Slide 13: Gamma value
FDD
  16x2: [2.2]
  16x4: [2.2]
TDD
  16x2: [2.2]
  16x4: [2.2]
Introduce requirement with gamma value in [] based on simulation results summary R4-2100903 submitted in RAN4#98-e meeting .
Companies are encouraged to further align the results. Further update results and values in RAN4#98bis-e meeting not excluded