## Slide 1: WF for NTN General Part
Moderator, THALES

## Slide 2: Outline
Proposed way forward based on the outcomes of “Email discussion summary for [98e][310] NTN_Solutions_Part1”
See R4-2103948

## Slide 3: Content
Topic #1: Use Cases and Deployment Scenarios
Topic #2: RAN4 NTN Architecture
Topic #3: Proposed FR1 Exemplary Frequency band for NTN
Topic #4: Proposed Exemplary Frequency band outside FR1 (e.g. FR2 and/or outside FR1&FR2) for NTN NR based satellite networks
Topic #5: HAPS Frequency Bands
Topic #6: NTN UL frequency synchronization requirement

## Slide 4: Summary
List of proposals for each topics discussed
In “agreements” part
  Proposals with “green” comments are agreeable.
In “open issues” part
  Proposals with “purple” comments not agreeable.
  Proposals with “orange” comments not agreeable:
    If there is a GTW session and we could agree on some of them, this WF will be revised anyway;
    Please also note that the “orange” proposals were the results of “agreed with changes” comments.
  Proposals without any comment were not discussed.

## Slide 5
Agreements after 1st round
during GTW session
(1st of February 2021)

## Slide 6: Topic #2: RAN4 NTN Architecture – GTW Agreements
RAN4 shall define the corresponding RF requirements for service link between UE and satellite
From service link RF requirements aspect, candidate options for the components:
  Option 1: Satellite + feeder link + NTN-Gateway as a single entity
  Option 2: Satellite + feeder link + NTN-Gateway + gNB as a single entity
FFS whether RAN4 shall define RF requirements for the linkage between NTN-Gateway and gNB
  Companies are encouraged to further clarify and discuss the assumption of the linkage between NTN-Gateway and gNB

## Slide 7: Topic #3: Proposed FR1 Exemplary Frequency band for NTN – GTW Agreements
Include S-band, L-band as exemplary bands for FR1
  Using S-band frequency range i.e. 2GHz for co-existence simulation in FR1
At least one of above bands RF requirements completed, then Rel-17 NTN WI, RF requirements for FR1 can be considered as completed.

## Slide 8: Topic #4: Proposed Exemplary Frequency band outside FR1 (e.g. FR2 and/or outside FR1&FR2) for NTN NR based satellite networks – GTW Agreements
It’s FFS whether Ka bands can be introduced in the Rel-17 NTN WD as exemplary band with FR2 usage assumption pending on RAN-P decision.
Before RAN-plenary have clear guidance for Ka band treatment, no detailed discussion for RF requirements for Ka bands except the co-existence study
Considering 20GHz (DL) and 30GHz (UL) as frequency for FR2 NTN co-existence study purpose as 2nd priority before RAN-P have clear guidance

## Slide 9
Agreements after 2nd round of discussions

## Slide 10: Topic #1: Use Cases and Deployment Scenarios
  Coexistence system simulations are static type of simulations, UE mobility is modelled via a random distribution over the cells.
  Note: However, except from this coexistence system simulations, UE mobility SHALL be considered.
  No concern raised so far
Further continue discussion with respect to UE mobility assumptions in the RAN4 NTN coexistence studies.
  No concern raised so far
RAN4 shall investigate the ESIM use case as well as its architecture in the FSS spectrum identified by ITU.
  No concern raised so far

## Slide 11: Topic #1: Use Cases and Deployment Scenarios
For RAN4 NTN coexistence studies in FR1, handheld devices could be prioritized (to be further discussed in the NTN coexistence analysis).
  No concern raised so far
RAN4 shall use TN BS/UE ACLR and TN ACS as the ones specified in TS 38.104, 38.101-1 and 38.101-2 for NTN and TN coexistence studies.
  No concern raised so far

## Slide 12: Topic #2: RAN4 NTN Architecture
RAN4 shall continue discussion to investigate if (NTN Payload-Feeder Link-NTN Gateway) as a Relay is contradictory with transparent satellite assumption in Rel-17.
  No concern raised so far
RAN4 shall develop appropriate NTN ACLR and ACS based on co-existence studies, to be used by satellite RF on the service link.
  Note: These NTN requirements may be different (or not) from those used in e.g. TS 38.104 for TN.
  No concern raised so far

## Slide 13: Topic #5: HAPS Frequency Bands
RAN4 to study one example band in FR1 for HAPS, from the existing NR bands identified for HAPS deployment.
  Note1: Example band should be used as an example for technical study.
  Note2: Regarding HAPS deployment, more discussion might be needed, which frequency range, whether it is co-channel deployed with terrestrial BS or not.
  No concern raised so far
RAN4 to study coexistence scenarios in order to derive RF requirements used as baseline for HAPS.
  Note: Regarding HAPS deployment, more discussion might be needed, which frequency range, whether it is co-channel deployed with terrestrial BS or not.
  No concern raised so far

## Slide 14
Open issues
This includes issues for which no agreement could be reach during #98-e
for which discussion is postponed to next meetings

## Slide 15: Topic #1: Use Cases and Deployment Scenarios
RAN4 to investigate how much the IAB requirements or a subset can be reused for the VSAT Terminal type in NTN.
  Note1: WI revision might be needed.
  Note2: the IAB proposal is not related to IAB itself, but more to IAB requirements. In the respective contribution is said that Tx Power of VSAT resembles the one of an IAB node/IAB-MT, and is suggested to further discuss/continue discussion of some subset of (potentially common) requirements.
  An agreement could not be reached.
For bands above 6 GHz, “VSAT” UE including fixed/moving platform mounted ones are considered as baseline.
  More discussions are required on this topic.

## Slide 16: Topic #6: NTN UL frequency synchronization requirement
UE shall be able to compensate the frequency offset due to the satellite mobility when generating its UL carrier frequency.
  To be further discussed, this aspect was proposed after the 1st round, from [98e][237] RAN4 RRM list.
The UE modulated carrier frequency shall be accurate to within ±0.1 ppm as observed over a period of 1 ms by the gNB.
  To be further discussed, this aspect was proposed after the 1st round, from [98e][237] RAN4 RRM list.
The UE residual frequency error shall be sufficiently low such that it can be considered included in the tolerated frequency error of ±0.1 ppm already captured in the specification.
  To be further discussed, this aspect was proposed after the 1st round, from [98e][237] RAN4 RRM list.