## Slide 1: Way Forward for NTN Coexistence Study
Moderator, Samsung

## Slide 2: Way Forward – General Aspect
Agreement on scope of coexistence study
For NTN-TN, only adjacent channel cases are considered in RAN4 coexistence study.
For NTN-NTN, only consider adjacent channel cases are considered in RAN4 coexistence study.
Agreement on frequency bands for coexistence study
Using S-band frequency range i.e. 2GHz for co-existence simulation in FR1
Deprioritize FR2 at current stage.

## Slide 3: Way Forward – Scenarios
RAN4 further down-select items based on the table.
Further analysis on which scenario is the worst case between LEO@600km & LEO@1200km.
Cross link interference with NR needs to be considered.
FR1: 2GHz |  |  | Set 1 |  |  | Set 2 |  |  | HAPS
 |  |  | GEO | LEO 600km | LEO 1200km | GEO | LEO 600km | LEO 1200km | 
NR / NB-IoT | Rural |  | X | X | X | X | X | X | FFS
 | Urban macro |  | X | X | X | X | X | X | FFS
 | Dense Urban |  | X | X | X | X | X | X | FFS
 | Indoor |  | X | X | X | X | X | X | 
NTN | GEO | Set 1 | X | X | X | N/A | N/A | N/A | FFS
 | LEO 1200km |  | X | X | X | N/A | N/A | N/A | FFS
 | LEO 600km |  | X | X | X | N/A | N/A | N/A | FFS
 | GEO | Set 2 | N/A | N/A | N/A | X | X | X | FFS
 | LEO 1200km |  | N/A | N/A | N/A | X | X | X | FFS
 | LEO 600km |  | N/A | N/A | N/A | X | X | X | FFS

## Slide 4: Way Forward – Assumptions
Baseline/Starting point of simulation assumptions.
Use Satellite and UE parameters as well as network deployment assumptions in TR 38.821 as the starting point for FR1 coexistence study.
ITU-R studies would also be used as inputs.
NTN UE parameters
Handheld UEs for FR1.
TN UE parameters
The existing RF requirements (i.e. ACS and ACLR for both BS and UE) of TN in the spec (i.e. TS 38.104 and 38.101) shall be reused when doing the coexistence study between NTN and TN.

## Slide 5: Way Forward – Simulation Assumptions
Performance metric
For TN, same criteria as previous study applies, e.g. the throughput loss of victim system should be below 5%. Note that for the throughput of a modem for NTN and TN, it could be referred in section 5.2.7 of TR 38.803.
For NTN, further discussion and evaluation is needed.
Detailed assumptions are captured in R4-2103965 and need further discussion.
Satellite Antenna beam configurations
Start with Earth Fixed beam first, Earth Moving Beams could be further discussed.

## Slide 6: Way Forward – Simulation Assumptions
Further discuss micro work plan on platform calibration with partial simulation assumptions.
For other assumptions, following considerations can be a starting point. However, each item should be checked one by one.
For NTN, other simulation assumptions could refer to section 6.1.1.1 of TR38.821.
For TN, other simulation assumptions for 2GHz could refer to TR36.942.

## Slide 7: Way Forward – HAPS
Frequency bands:
Consider 2GHz FDD & Inputs from operators are encouraged.
Performance metric:
Agree that the adjacent channel requirements for HAPS should be determined based on a 5% throughput degradation in the victim network in HAPS and TN co-existence scenarios.
BS & UE requirements:
RAN4 to study ACLR & ACS requirements on HAPS BS for adjacent channel coexistence with terrestrial IMT systems.
Consider UE requirements as specified in TS 38.101-1.

## Slide 8: Way Forward – HAPS
Detailed assumptions are captured in R4-2103965 and need further discussion.

## Slide 9: Open Issues of HAPS

## Slide 10: Scenarios
Whether coexistence study for HAPS should be prioritized at current stage needs further discussion.
Further discuss following option for coexistence scenarios. (Not exclusive list)
  Consider both densely deployed TN and sparsely deployed TN in HAPS-TN co-existence scenarios.
  To consider wrap-around with 19 sites (3 sectors per site) for TN network.
  FFS if multiple HAPS platform instead of only one is to be considered.
  FFS if uncoordinated operation between two adjacent channel operators for HAPS to HAPS scenario is needed.
HAPS – TN ACI | HAPS may cover a large area with multiple cells. A cellular layout of 19 sites, 57 cells with a certain ISD may be used to model TN | HAPS coverage overlaps spotty TN cells
HAPS-HAPS ACI | FFS | 

## Slide 11: Simulation Assumptions
Further discuss Simulation assumptions for HAPS - TN:
The example table could be a starting point
These parameters are being considered in ITU-R.
Frequency band | Band n1 (UL: 1920-1980 MHz, DL: 2110-2170 MHz) | 
Terrestrial environment | Urban Macro | Rural Macro
Channel bandwidth | 20 MHz | 20 MHz
HAPS altitude | 20 Km | 20 Km
HAPS coverage radius | 100 Km | 100 Km
HAPS and TN coverage center distance | 0, 20, 40 Km | 0, 20, 40 Km
HAPS channel model | NTN urban [7] | NTN rural [7]
HAPS indoor UE percentage | 0% | 0%
TN inter-site distance | 1 Km | 2 Km
TN BS antenna height | 25 m | 35 m
TN BS transmit power | 46 dBm | 46 dBm
TN BS antenna array configuration | 8 x 8 x 2 (M=8, N=8, P=2) 0.5 wavelength spacing | 8 x 1 x 2 (M=8, N=1, P=2) 0.5 wavelength spacing
TN BS antenna downtilt | 10⁰ | 6⁰
TN channel model | UMa model [8] | RMa model [8]
TN BS element gain | 8 dBi | 8 dBi
TN BS element HPBW horizontal/vertical | 65⁰ for H/V | 65⁰ for H/V
TN BS element radiation pattern | As in Table 7.3-1 of [8] | As in Table 7.3-1 of [8]
TN indoor UE percentage | 70% | 50%
Body loss | 4 dB | 4 dB
UE antenna gain | -3 dBi | -3 dBi
UE antenna array | 1 x 1 x 2 (M=1, N=1, P=2) | 1 x 1 x 2 (M=1, N=1, P=2)
UE transmit power | 23 dBm | 23 dBm

## Slide 12: Antenna models
Further discuss antenna models to be used.
An example model and parameters has been proposed as below for further discussion.
Inputs on other options are invited.
Example of HAPS antenna array and cell layout
Number of cells | 7
Antenna array configuration (row x column) | 2 x 2 for 1st layer cell 4 x 2 for 2nd layer cell
Antenna polarization | Linear
Element gain | 8 dBi
Element HPBW horizontal/vertical | for both H/V
Element front-to-back ratio horizontal/vertical | 30 dB for both H/V
Element spacing horizontal/vertical | 0.5 wavelength for both H/V
Antenna panel tilt | for 1st layer cell for 2nd layer cell
Tx power per antenna panel | 46 dBm
Number of cells | 7
Antenna array configuration (row x column) | 2 x 2 for 1st layer cell 4 x 2 for 2nd layer cell
Antenna polarization | 
Element gain | 8 dBi
Element HPBW horizontal/vertical | 
Element front-to-back ratio horizontal/vertical | 30 dB for both H/V
Element spacing horizontal/vertical | 0.5 wavelength for both H/V
Antenna panel tilt | 
Tx power per antenna panel | 46 dBm
Note: This antenna model is based on the parameter currently under consideration in ITU-R and is considered as an active antenna consisting of multiple elements. However, it is also considered that beam forming is to be used to fix the footprint on earth like satellites rather than beam-steering to UE since HAPS would be mainly used for rural areas.

## Slide 13: Appendix

## Slide 14: Contribution list in RAN4#98e
TDoc Number | Title | Company
R4-2100399 | Discussion on frequency band and scenarios for NTN | CATT
R4-2100486 | Simulaiton assumptions for NTN co-existence | CATT
R4-2100487 | Consideration on BS requirement impact for NTN | CATT
R4-2100904 | Simulation assumption for FR1 coexistence study | Samsung
R4-2101105 | Coexistence study on NR to support non-terrestrial networks | Xiaomi
R4-2101812 | General discussion on NTN simulation assumptions | Huawei, HiSilicon
R4-2101859 | NTN FR1 Coexistence Scenarios and Related Core Requirements | THALES
R4-2101880 | Simulations for NTN FR1 Coexistence Cases | THALES
R4-2101934 | NTN - HAPS simulation assumptions for co-existence study | Nokia, Nokia Shanghai Bell
R4-2101935 | NTN - HAPS adjacent channel coexistence | Nokia, Nokia Shanghai Bell
R4-2101964 | Discussion on simulation assumptions for NTN coexistence study | ZTE Corporation
R4-2102174 | NTN Simulations assumptions discussion | Ericsson
R4-2102176 | NTN - BS requirements overview | Ericsson
R4-2102508 | Simulation assumptions for NR NTN co-existence study | Qualcomm Incorporated
Note that R4-2100487, R4-2102176 and part of R4-2101859 were handled in [310] NTN_Solutions_Part1 this time.

## Slide 15: Reference
[1] R4-2103750, “Email discussion summary for [98e][311] NTN_Solutions_Part2”, Samsung
[2] R4-2103965, “Simulation assumption for NTN co-existence study ”, CATT