## Slide 1: WF for NR repeater RF requirements
CMCC
3GPP TSG-RAN WG4 Meeting # 98-e R4-2103882
Electronic Meeting, Jan. 25-Feb. 5, 2021

## Slide 2: Background on NR repeater
RAN#90e approved a new “New WID on NR Repeaters” with RAN4 as the responsible WG.
The objective of the WID is listed as below:
Normative work phase objective [RAN4]
Specify RF and EMC requirements for NR repeaters
Consider FR1 (FDD and TDD) and FR2 (TDD) bands
For the above objective, the leveraging of RF specifications for LTE repeater and IAB should be sought.
It is assumed that the repeater does not perform adaptive beamforming towards the UE.
It is assumed that the TDD repeater meets both BS and UE emission requirements (or the more stringent absolute level in dBm) in all slots.
The following constraint may be considered for TDD repeaters, as needed, to contain the workload associated with this project:
TX EIRP/TRP/power of Repeater not exceeding any UE power class defined in the band
Note: FR1 FDD repeaters testing is assumed to be conducted. This assumption can be revisited in RAN#91.

## Slide 3: WF on classes definition
  FFS on whether to distinguish DL and UL for class definition
  FFS on whether explicitly distinguish classes in specification
    Option 1: Explicitly distinguish repeater classes in the specification. e.g. selection from the set of MA/MR/LA with some modification, if needed, similar as IAB-MT classes definition.
    Option 2: no class is needed

## Slide 4: WF on principle of FDD repeater RF requirements
  NR FDD requirements could follow LTE FDD requirements. However, at least following requirements should be further discussed.
    EVM
    OBUE & adjacent channel emissions
    maximum output power
    out of band gain

## Slide 5: WF on candidate TDD specific conducted requirements
  Candidate TDD specific requirements for further discussion:
    time accuracy
    TDD switching
    REFSENSE
    transmit off requirements
    transient period requirements

## Slide 6: WF on FR1 maximum output power
  FFS on maximum output power requirements, following aspects should be considered:
    Whether to differentiate DL and UL
    Whether to limit the UL power not exceeding any UE power class
    Whether to reuse BS-like approach for DL
    which scenarios require more power, as the repeater gain is limited then increasing the output power does not improve the link only changes the optimum location for the repeater.
    if the repeater uses higher output power than previous simulations (33dBm for LTE repeater), the new simulation may be needed with the new parameters.

## Slide 7: WF on FR1 ALC/AGC mechanism
ALC and AGC play the same role. They are only the different names to regulate repeater’s auto gain control capability
ALC/AGC capability should be maintained
  FFS on whether dedicated requirements is needed for ALC/AGC
  FFS on whether AGC would not interfere with the network power control
  FFS on the detailed AGC mechanism

## Slide 8: WF on FR1 EVM
FFS on EVM requirements, following aspects should be considered
  Aligned with which modulation scheme, 256 QAM or 64 QAM
  whether to improve the EVM beyond what is required for LTE repeater
  how much link EVM degradation is acceptable
  Whether to follow BS or UE spec definition of EVM or something different

## Slide 9: WF on FR1 frequency error
  Frequency error for FR1:
    [±0.01]ppm for RF core requirements

## Slide 10: WF on FR1 ACLR requirements
  FFS on ACLR requirements, following aspects should be considered
  Further check whether the output power in adjacent channel is lower than the noise, if so ACLR with NR adjacent channel may be omitted, as well as with LTE adjacent channel
  If RAN4 does not define ACLR requirements, then alternate tests/requirements may be needed to ensure good coexistence performance.
  Whether the applicable range for ACLR is out of the passband or the carrier

## Slide 11: WF on FR1 OBUE and spurious emission conducted requirements
  BS operating band unwanted emissions and transmitter spurious emissions follow BS specification for appropriate requirements. Further discussion is needed about whether to include extra requirements as follows:
    UE related requirements
    uplink BS receiver protection requirements
    absolute BS ACLR & other equivalent requirements
    Receiver spurious emission for TDD
    Co-existence with other systems in the same geographical area
    Co-location with base station
    the applicable class(es)

## Slide 12: WF on FR1 out of band gain
  FFS on FR1 out of band gain, following aspects should be considered
    whether to identify the minimum coupling loss to any radio transmitter from the repeater, not just the donor BS

## Slide 13: WF on FR1 ACRR
  FFS on ACRR requirements, following aspects should be considered
    the behavior of the repeater if there is another node close by that either creates emissions on an adjacent channel or actually uses an adjacent channel
    co-existence with UTRA/EUTRA rather than NR operating on an adjacent channel

## Slide 14: WF on FR1 output intermodulation
  FFS on output intermodulation, following aspects should be considered
    Whether to refer to BS Tx intermodulation requirements
    Whether to refer to LTE repeater output intermodulation requirements

## Slide 15: WF on FR1 input intermodulation
  FFS on input intermodulation, further discussion whether following scenarios should be considered
    Option 1: UL passband repeater
    Option 2: co-location scenario
    Option 3: co-existence scenario

## Slide 16: WF on FR2 Tx power and ALC requirements
  FFS on FR2 power related requirements, following aspects should be considered
    For FR2, the Tx power is based on declaration or not
    For FR2, not only DL coexistence, but also uplink coexistence should be considered
    For FR2, how the repeater manages its output power levels for FR2

## Slide 17: WF on FR2 frequency error
  [± 0.01] ppm frequency error for FR2 RF requirements

## Slide 18: WF on FR2 EVM requirements
  FFS on whether FR2 EVM Radiated requirements are the same as FR1 conducted requirements

## Slide 19: WF on FR2 OBUE and spurious emission
  BS operating band unwanted emissions and transmitter spurious emissions follow BS specification for appropriate requirements. Further discussion is needed about whether to include extra requirements as follows:
    UE related requirements
    absolute BS ACLR & other equivalent requirements
    Receiver spurious emission for TDD
    the applicable class(es)

## Slide 20: WF on FR2 out of band gain
  FFS on FR2 out of band gain, following aspects should be considered
    UE blocking requirement level within the band
    BS out of band blocking levels for out of band

## Slide 21: WF on FR2 ACLR
  FFS on FR2 ACLR requirements, following aspects should be considered
    Whether it is possible to measure ACLR
    If ACLR is omitted, whether same equivalent requirement is necessary to make sure the same protection for adjacent channel system as BS specification

## Slide 22: WF on FR2 Tx/output intermodulation and input intermodulation requirements
  For FR2, FFS on whether output intermodulation is still needed or not
  For FR2, FFS on whether input intermodulation could be defined based on BS RX intermodulation or based on LTE repeater requirement