## Slide 1: WF on polarization basis mismatch
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25 January – 5 February, 2021
Agenda Item: 12.1.3
R4-2103919

## Slide 2: Background
These open issues about polarization basis mismatch test enhancement methods are further discussed in RAN4#98-e
  Issue 2-1-1: Remaining issues with the TPMI method
  Issue 2-1-2: Proposals related to methods other than TPMI
  Issue 2-2-1: Remaining issues with enhancements related to UL demodulation
The WF focus on the topics of Issue 2-1-1 and 2-1-2

## Slide 3: Remaining issues with the TPMI method
Detailed TPMI method enhancement coverage is FFS
  if TPMI method is applicable for clause 6.2 of TS38.101-2, then 2 port SRS (nrofSRS-Ports = 2) shall be configured
Which TPMI index per test AoA shall be sent by TE is FFS
  Option1: Fixed TPMI index
  Option2: Optimal TPMI index
    Option2-A: TE to configure the UE with SRS resources at each grid point
    Option2-B: TE simply try out all TPMIs and choose best one
  UE vendors are encouraged to study the UE EIRP performance delta between Option1 and Option2
  TE vendors are encouraged to study the feasibility/pros/cons of Option2-A/B compared to Option1
TPMI method enhancement coverage | clause 6.2 of TS38.101-2 (Transmitter power) | Clause 6.1, 6.3 to 6.6 of TS38.101-2 (other Transmitter characteristics)
Rel-15 nonCoherent UEs | No | No
Rel-15 coherent UEs | [Yes] | [Yes]
Rel-16 nonCoherent UEs | No | No
Rel-16 coherent UEs | [Yes] | [Yes]
Rel-16 nonCoherent UEs which support uplink full power transmission | [Yes] | [Yes]
Notes: Qualcomm: TPMI index detail removed. We do not think a TPMI exclusive to coherent UL MIMO capable-UEs is appropriate here. Also on option 2, is the intent that the UE will be asked to send SRS resources at each grid point? This detail should be included by proponent.

## Slide 4: Proposals related to methods other than TPMI (1/2)
About “introduce 2-port CSI-RS”
  Agreement: For any FR2 UE that implements CSI-RS based beam refinement, 2-port CSI-RS can help the UE get a better picture of the channel
  Open issues:
    About “how CSI-RS ports are mapped to TE pols?”
      Option-1: Agree on the principle in RAN4 (Qualcomm,…)
      Option-2: up to TE implementation
    About “simultaneous vs. sequential configuration, and whether sequential is feasible”
      UE vendors are encouraged to study UE EIRP performance impact of simultaneous and sequential configuration, and also feasibility to support sequential configuration
      TE vendors are encouraged to study the feasibility/pros/cons of simultaneous and sequential configuration
    Interested companies are encouraged to provide a suitable CSI-RS configuration to better estimate the feasibility of the method
Notes: Qualcomm: We do not understand what is meant by ‘Sequential CSIRS’. Before agreement on adoption, we would like to evaluate the design (configuration) that enables this format, and how the UE is supposed to know to use non-simultaneous measurements

## Slide 5: Proposals related to methods other than TPMI (2/2)
About “introduce test mode with UE declaration”
  Option-1: support (LGE, Samsung)
  Option-2: object (Qualcomm, Apple, Sony, Ericsson)
About “there is no need to introduce additional test methods for Rel-15 nonCoherent UEs and Rel-16 nonCoherent UEs”
  Option-1: support (Qualcomm, Sony, Ericsson, Huawei)
  Option-2: object