## Slide 1: 3GPP TSG-RAN WG4 Meeting #98-e Electronic Meeting, January 25th – February 5th, 2021
Huawei, HiSilicon
Way forward on NR-U BS demodulation requirements for general part and PUSCH
R4-2103988

## Slide 2: Background
R4-2012611, Way Forward on NR-U BS demodulation requirements, RAN4#96-e, Ericsson
R4-017688, Way forward on NR-U BS demodulation requirements for general part and PUSCH, RAN4#97-e, Huawei, HiSilicon

## Slide 3: General: Test scope
How to handle Rel-15 test requirements for BS supporting NR-U
  Conduct the performance requirements defined for both NR Rel-15 with test applicability rule and NR-U

## Slide 4: General: Specification structure
  Specification structure for PUSCH
    Create separate clauses 8.2.[9] and 11.2.1.[9] in 38.104 and 8.2.[9] in 38.141-1 and 38.141-2 for PUSCH performance requirements with interlace , and 8.2.[10] and 11.2.1.[9] in 38.104 and 8.2.[9] in 38.141-1 and 38.141-2 CG-UCI multiplexed on PUSCH performance requirements with interlace if it is agreed to be introduced
  Specification structure for PUCCH
    Specify interlaced PUCCH requirements in separate clauses 8.3.x and 11.3.1.x in 38.104 and 8.3.x in 38.141-1 and 38.141-2, where x=8, 9, 10, 11
  Specification structure for PRACH
    Create new clause in 38.104 “8.4.2.4 Minimum requirements for PRACH with LRA=1151 and LRA=571”.
    Create new clause in 38.141-1 “8.4.1.7 Test requirement for PRACH with LRA=1151 and LRA=571”.
    Create new clause in 38.141-2 “8.4.1.7 Test requirement for PRACH with LRA=1151 and LRA=571”.

## Slide 5: Agreements for PUSCH
PUSCH performance requirements definition:
  Bandwidth: Define the requirements for single carrier with 20MHz
  Reuse Rel-15 applicability rule for different channel bandwidths with updated wording
Test Applicability rules for PUSCH requirements with different CBW(s)
  Option 1:
    For the subcarrier spacing for testing based on the test applicability rule, the test requirements for 20MHz channel bandwidth shall apply only if the BS supports it (see D.xx in table 4.6-1).
    Unless otherwise stated, for the subcarrier spacing for testing, the tests shall be done only for the widest supported channel bandwidth. If performance requirement is not specified for this widest supported channel bandwidth, the tests shall be done by using performance requirement defined for 20MHz channel bandwidth; The tested interlace shall then be the one closest to the centre in this widest supported channel bandwidth.
  Option 2:Other options not precluded

## Slide 6: Agreements for PUSCH
  PUSCH mapping type and test applicability rule
  Define PUSCH performance requirements for both PUSCH Type A and Type B
  Reuse corresponding NR Rel-15 applicability rules
MCS
  MCS 20
RV sequence
  {0,2,3,1}
  CG-UCI configuration:
  Not configure CG-UCI for PUSCH testing

## Slide 7: Agreements for PUSCH
Performance requirements for CG-UCI multiplexed on PUSCH with interlace allocation
  Introduce performance requirements for CG-UCI multiplexed on PUSCH with interlaced resource allocation and without HARQ-ACK, CSI part 1 and CSI part 2:
    Further discuss the simulation assumptions
    The tests should be based on BS declaration

## Slide 8: Simulation assumptions
Parameters | Value
Transform precoding | Disabled
Antenna configuration | 1T2R Low
SCS and BW | 15kHz: 20MHz; 30kHz: 20MHz
TDD pattern | 7D2S1U S=6D:4G:4U for 30kHz SCS 3D1S1U S=10D:2G:2U for 15kHz SCS
Interlace structure | First single interlace per slot
DM-RS type | type 1 with single-symbol
Number of DMRS symbols | dmrs-AdditionalPosition ‘pos1’ (1+1)
symbols length | 14
start symbol index | 0
Time domain resource allocation type | Type A and B
Frequency domain resource | Full applicable test bandwidth
MCS index | 20
Carrier frequency (GHz) | 4
Propagation condition | TDLA30-10
Guard band | Not configured
PT-RS | Not configured
Timing offset | 0
Frequency offset | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled
Number of HARQ transmissions | 4
RV sequence | {0,2,3,1}
Testing metric | SNR @70% of maximum throughput