## Slide 1: Way Forward on NR TxD & Power Class
vivo
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan - 5 Feb., 2021
R4-2103390

## Slide 2: EVM for Transparent TxD
Proposals:
  Option 1: As in agreed WF R4-2008465
  Option 3: As has been provided in R4-2102917:
    Option 3b.
      where is the
      correlation coefficient of the transmitter noise
      Recommended WF:
  [TBD]

## Slide 3: UE Behavior under Conformance Testing
  Background: Motivation is to guide how to test requirements that require power changes such as relative power control.
  Proposals:
  Option 1a: UE will keep the tx diversity status unchanged in conformance testing.
  Option 1b: Test mode signalling is implemented to instruct UE to keep TX div status unchanged
  Option 2a: TE will detect and sum for every power step and change in condition from declared connector, with no precondition
  Option 2b: TE will detect and sum for every power step and change in condition from declared connector, based on pre-condition that a repeatability of TxD activation/deactivation timing in a UE is maintained can be fulfilled.

## Slide 4: Power Splitting Behavior
Background: Motivation is to guide how to test requirements that require power changes such as relative power control
Question 1: What would be the impact for the requirements and testability with tentative equal power split restriction?
Proposals:
  Option 1: Only allow equal power split between connectors
    Excludes 17+17+20 dBm implementations
    Excludes power control optimizations
  Option 1a: Per instructed as test mode, UE should keep equal power split between connectors in all cases.
  Option 2: Allow any power split between connectors

## Slide 5: Applicability of Transparent TxD Requirement
The applicability of the newly introduced test procedure (if any) and specific requirement (if any) for transparent TxD UE :
•whether or not applicable to UE implementation without transparent TxD
Proposals
  Option 1: Not applicable
  Option 2: Applicable

## Slide 6: Signaling for Transparent TxD
Whether and how RAN4 introduce signalling for transparent TxD:
  Option 1: Introduce some sort of signaling by UE
    Option 1a. Use ModifiedMPRbehavior bits to signal additional relaxations;
    Option 1b: Introducing a new ( per band capability) signalling for TxD together with existing power classes
      Capability reporting for supporting TxD
      [Capability reporting for TxD Enable/Disable status]
    Option 1c: Introducing a new power class (e.g. PC2.5) for TxD
  Option 2: Based on UE vendor declaration.
  Option 3: Using existing signalling to indicate the 2Tx implementation capability.
Recommended WF
  For R15 UEs, UE vendor declaration can be used in testing
  For R16 UEs, new signaling, i.e. 1b, is needed to inform the network of the support of TxD. If the signaling can be made to enable release-independent support of TxD from R15 can be consulted with RAN2

## Slide 7: CDD-related Requirement
For transparent TxD UE, necessity of CDD related requirements, e.g. requirement on TAE+CDD, is need to be further studied:
Proposals
  Option 1: Yes
  Option 2: No.
  Option 2b. No at least for Rel-16
Recommended WF
  Option 2b

## Slide 8: Rel-15 NSA power class
Proposals
  Option 1: The Pcmax for NR is modified according to the declared NR power capability for NSA so that the PHR becomes correct. (Based on R4-2015976 & R4-2015977)
  Option 2: Introduce the Rel-16 defined power class UE capability for Rel-15, and Indication of UE implementation by declaration. (Based on R4-2016479 observation 1)
  Option 3: The Pcmax for NR is modified to use the lower possible power class to decide the lower bound of the configured power. (Based on R4-2016479 observation 3 & R4-2016482, & R4-2102385)
  Option 4: Any other combined/refined revision.
  Option 5: Further revision not needed.
Recommended WF
  [Option 1 or 3]

## Slide 9: Impact of Applicability of TxD to Rel-15 NSA power class
Whether applicability of TxD for Rel-15 would impact the previous Issue for NSA.
Proposals
  Option 1:Yes;
  Option 2: No.
Recommended WF
  TBA

## Slide 10: Power class fall back for SA UL-MIMO in Rel-15
Background & motivation:
  Rel-15: “If UE is scheduled for single antenna-port PUSCH transmission by DCI format 0_0 or by DCI format 0_1 for single antenna port codebook based transmission, the requirements in clause 6.2.1 apply.”
  Rel-16: “If UE is scheduled for single antenna-port PUSCH transmission by DCI format 0_0 or by DCI format 0_1 for single antenna port codebook based transmission, the requirements in clause 6.2.1 apply for the power class as indicated by the ue-PowerClass field in capability signalling.”
Proposals
  Option 1: Rel-15 is the same to Rel-16;
  Option 2: Rel-15 can still have different explanation compared to Rel-16.
Recommended WF
  TBA

## Slide 11: 2Tx MPR and the treatment of Rel-16 TxD CR
Background:
It was agreed the same MPR requirement for TX Diversity and UL MIMO for the same power class (WF R4-2016830 in RAN4#97e).
Two proposals on table for UL-MIMO and no further agreements till now
  R4-2008213 (Huawei) and R4-2008046(Qualcomm), RAN4#95e Summary R4-2008935
    Current CR (R4-2103156) utilize the requirements from R4-2008213 with []
    EVM is not concluded yet with new proposal in this meeting

## Slide 12: 2Tx MPR and the treatment of Rel-16 TxD CR
Proposals:
Option 1: Agree the Rel-16 TxD CR, with MPR requirements and EVM definition in []; Revisit and try to conclude them in next meeting.
Option 2: Agree the Rel-16 TxD CR, remove the MPR requirements and EVM definition; Revisit and try to conclude them in next meeting.
Option 3: Technically endorse Rel-16 TxD CR, with MPR requirements and EVM definition in []; Revisit and try to conclude them in next meeting.
Recommended WF
  Option 3