## Slide 1: Way Forward on MPR evaluation for NR TxD & UL-MIMO
vivo, Skyworks, Huawei, […]
3GPP TSG-RAN WG4 Meeting # #98-bis-e
Electronic Meeting, Apr. 12 -20, 2021
R4-210xxxx

## Slide 2: WF on architecture
PC2 with 2x23dBm PAs => 2Tx NR MPR (High priority)
[PC2 with 2x26dBm PAs => 2Tx NR MPR]
[PC2 with 23+26dBm PAs => 2Tx NR MPR]

## Slide 3: WF: MPR/AMPR evaluation assumptions (1)
RF assumptions:
  4dB post PA losses
  10dB antenna isolation
  Equal power and Equal back-off power split for the two antennas
Usual 3GPP PA calibration for 20MHz QPSK DFT-s-OFDM 100RB0 waveform based on 4dB post PA losses and 1dB MPR.
  For 26dBm PA: 29dBm at 31dB ACLR
  For 23dBm PA: 26dBm at 30dB ACLR
RF impairments:
  Image and carrier leakage is 28dB for up to 64QAM, image is 35dB for 256QAM
  CIM3 is 60dB and CIM5 is 70dB
  Measurements/simulation is used where two PA are coupled at their outputs recreating the 10dB antenna isolation assumption with the Reverse IMD
  To recreate the effect of CDD the two signal on each antennas can simply have a small delay between each other (a fraction of CP)

## Slide 4: WF: MPR/AMPR evaluation assumptions (2)
Requirements for back-off evaluation:
  Emission requirements (ACLR/SEM/spurious emissions of the targeted power class) are checked by summing the power of the two transmit paths
  EVM is checked for the agreed composite EVM equation but with P1 and P2 assumed equal. EVM should be checked especially for inner at high order modulations where RIMD will further degrade the in channel noise floor.
  Whether IBE is checked per antenna or as the sum should be clearly stated
  MPR is provided in the form of back off of total power versus power class nominal power level
EVM budget for PA:
  QPSK 10%
  16QAM 8%
  64QAM 4%
  256QAM 1.8%

## Slide 5: WF: MPR/AMPR evaluation assumptions (3)
Evaluation scenarios:
  Both CP-OFDM and DFT-s-OFDM waveforms are evaluated
  Since simulation may not be available, at least some worst case corners are evaluated for inner/outer and edge allocations
  Since it has the tighter requirements and highest PSD the lowest valid SCS should be used.
  All modulation orders should be checked:
    Pi/2 BPSK (no shaping), QPSK, 16QAM, 64QAM, 256QAM (for 256QAM mostly EVM with proper image level)
  Channel BW configurations should cover the entire channel bandwidth range:
    At least 5, 20, 50, 100MHz channel bandwidths (depends on the supported CBW of the operating band)