## Slide 1: WF on increasing UE maximum power high limit
Qualcomm Incorporated, OPPO, Nokia
R4-2105342
3GPP TSG-RAN WG4 #98bis-e
April 12th ‒ 20th, 2021
Electronic Meeting

## Slide 2: Background
Increasing UE maximum output power has been seen as beneficial
  Proliferation of PC2 bands, band combinations, DC configurations
  Introduction of PC 1.5 in Band n41 and ongoing work item for n77, n78, and n79
UE’s with two PA’s for the same band are more common now
  UL MIMO, TxD
  Configurations such as 23+23, 23+26, 26+23, 26+26 have been discussed
For a UE with two Tx paths capable of delivering 23 dBm (antenna port referred) and 26 dBm, the UE is potentially able to reach a maximum output power of 27.8 dBm. Generalizing, a UE with X dBm and Y dBm Tx paths can potentially deliver 10log(10X/10+ 10Y/10) dBm total maximum output power.

## Slide 3: Way Forward
It is agreed to study feasibility to enable the increase of maximum output power for those UE’s able to do so
Options for further evaluation
  Remove PPowerClass from PCMAX_H
  Replace PPowerClass with sum or modified sum
    in both PCMAX_H and PCMAX_L, or
    only in PCMAX_H if still this UE reports PC for CA or
    in both PCMAX_H and PCMAX_L and relax PCMAX_L by the sum - MAX(PC for Band A, PC for Band B) if the UE doesn’t report PC for CA(R4-2104572)
  Define a new power class
  Power boosting
  Other options are not precluded

## Slide 4: Possible impacts by increasing UE maximum power high limit
The following issues shall be solved before agreeing to enable the increase of maximum output power
  1) Possible impact to regulations
  2) Possible impact to 3GPP specifications
  3) Possible need for signaling
  4) Possible impact to SAR and whether existing mechanisms such as duty cycle need to be enhanced
  5) Possible impact on RAN4 requirements, such as MPR, emissions, coexistence
  6) MSD