## Slide 1: Way forward on the introduction of 25 MHz in band n5
AT&T
­­­3GPP TSG-RAN WG4 Meeting #98bis-e R4-2105362
Electronic Meeting, 12th – 20th Apr., 2021

## Slide 2: Background
Murata, Apple, MediaTek, Qualcomm, and Skyworks provided contributions with n5 25MHz REFSENS proposals
  All companies provided REFSENS proposals based on TX/RX 25MHz/25MHz
  Four companies provided contributions with REFSENS proposals based on TX/RX 20MHz/25MHz
    MediaTek provided REFSENS proposals for TX/RX 20MHz/25MHz during second round comments
Summary of REFSENS proposals for TX/RX 20MHz/25MHz from companies based on middle-case and best-case scenarios, respectively
UL Channel BW and REFSENS UL configurations for n5 25MHz can be confirmed
Possible impacts on A-MPR evaluated for coexistence with B26, adjacent Public Safety service in DL (851-859MHz), and Band n28
  No impact based on 20MHz UL Channel BW limitation
Possible impact on MPR evaluated
  No impact

## Slide 3: WF on UL Channel BW and A-MPR
Issue 4-1: UL channel BW restricted to 20MHz
Issue 4-3: A-MPR
Observations:
  Concerns raised related to 25MHz TX BW:
    A-MPR required for coexistence with B26
    A-MPR required for coexistence with adjacent Public Safety service in DL (851-859MHz)
    One company raised concern that A-MPR required for coexistence with Band n28
    Large MSD impact and link budget issues
  Concerns are avoided with UL channel BW restricted to 20MHz
WF
  Introduce asymmetric UL/DL CBW with UL BW limited to 20MHz, with the condition that REFSENS values would be acceptable
  No A-MPR required
  Status check at RAN4 #99-e after REFSENS confirmation

## Slide 4: WF on MPR
Issue 4-2: MPR for 25MHz channel BW
Observations:
  All contributing companies on this topic confirmed that delta MPR is not needed.
WF
  Based on relative channel BW, delta MPR is not needed.

## Slide 5: Way Forward on REFSENS
Issue 4-4: UE REFSENS
Observations:
  REFSENS proposals for TX/RX 20MHz/25MHz from companies based on middle-case and best-case scenarios, respectively
  REFSENS proposals for TX/RX 20MHz/25MHz based on middle-case scenario from four companies relatively aligned.
WF
  Further discussion required if MSD estimation is based on best-case or middle-case scenario
  Agree to UL configuration for n5 25MHz as in the next table:
  The asymmetric CBW and default Tx-Rx frequency separation specification is FFS
  Further discussion required for REFSENS for n5 TX/RX 20MHz/25MHz at the next meeting. Possible options:
    Option 1: If middle-case scenario is confirmed, REFSENS set to Murata/Skyworks values
    Option 2: Further discussion to understand large discrepancy and evaluate suitable REFSENS based on findings
    Option 3: Take average value
    Option 4: Others …

## Slide 6: References
R4-2104657, “REFSENS of n5 for 25MHz channel bandwidth”, Murata Manufacturing Co Ltd, 3GPP TSG-RAN WG4 Meeting #98-bis-e
R4-2104881, “Discussion and proposal for n5 with 25MHz CBW”, Apple Inc., 3GPP TSG-RAN WG4 #98-bis-e
R4-2104890, “MSD calculation for band n5 with 20 MHz UL BW”, Apple Inc., 3GPP TSG-RAN WG4 #98-bis-e
R4-2104959, “n5 REFSENS supporting 25MHz CBW”, MediaTek Inc., 3GPP TSG-RAN WG4 #98-bis-e
R4-2107320 + Revised R4-2107320, “n5 25MHz”, Qualcomm Incorporated, 3GPP TSG-RAN WG4 #98-bis-e
R4-2107323, “n5 25MHz REFSENS, A-MPR”, Skyworks Solutions Inc., 3GPP TSG-RAN WG4 #98-bis-e