## Slide 1: WF on the introduction of 50MHz channel BW in band n3
Ericsson, China Telecom, China Unicom
R4-2105363
3GPP TSG-RAN WG4 Meeting # 98-bis-e
Electronic Meeting, 12-20 April, 2021

## Slide 2: UE RF: MPR and A-MPR
When introducing 50MHz channel BW in band n3:
  No MPR is needed
  No A-MPR is needed

## Slide 3: UE RF: REFSENS – RB allocation
RB allocation:
  Following options have been proposed for this meeting:
  With:
  - Note 1: From TS 38.1010-1
  - Note x: For Band 3, for 50 MHz channel bandwidth, in the case of 15 kHz SCS, the UL resource blocks shall be located at Rbstart 165, in the case of 30 kHz SCS, the UL resource blocks shall be located at Rbstart 75, and in the case of 60 kHz SCS, the UL resource blocks shall be located at Rbstart 39.
  Companies are encouraged to bring UL config proposal at next meeting, considering:
    Shifting the RB allocation to eliminate CIM3.
    Keep consistency with existing bands and use RB allocation closest to DL.
SCS | RB allocation |  | 
 | Option 1 | Option 2 | Option 3
15 | 501 | 50x | 48
30 | 241 | 24x | 
60 | 101 | 10x | 

## Slide 4: UE RF: REFSENS limits
REFSENS values:
  Following limits have been proposed for this meeting (with corresponding RB allocation option# from previous slide):
  Companies are encouraged to bring analysis for REFSENS at next meeting, considering CIM3 and CIM5 impacts.
SCS | Option 1 | Option 3
15 | -81.1 | -79.4
30 | -81.2 | 
60 | -81.4 | 

## Slide 5: References
R4-2106284, Discussion on RefSens for Band n3 50MHz CBW, China Telecom
R4-2106285, Draft CR to 38.101-1 Introduce 50MHz CBW for Band n3 , China Telecom
R4-2106286, Draft CR to 38.104 Introduce 50MHz CBW for Band n3 , China Telecom
R4-2106482, Adding 50 MHz CBW for NR band n3, Huawei, HiSilicon
R4-2107321, n3 50MHz, Qualcomm
R4-2105185, Email discussion summary for [98-bis-e][112] NR_bands_R17_BWs, Moderator (Ericsson)