## Slide 1: WF on UE REFSENS for 35 MHz and 45 MHz
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2105364 Electronic Meeting, 12th – 20th April, 2021

## Slide 2: Summary of REFSENS proposals from companies
Company | n2 |  | n3 |  | n8 |  |  | n25 |  |  |  | n71 |  | 
 | 35 | 45 DL/40 UL | 35 | 45 | 35 DL/20 UL |  |  | 35 | 45 DL/40 UL |  |  | 35 DL/20 UL |  | 
 |  |  |  |  | worst | Mid | Best |  | worst | Mid | Best | worst | Mid | Best
Murata |  |  | -86 | -84.2 | -64 | -79.5 | -85.2 | -85.4 | -77.4 | -81.5 | -82.8 | -69.1 | -85.2 | -87.7
Mediatek |  |  |  |  | -68.7 | -78 | -86 |  |  |  |  | -69.8 | -78 | -87
Qualcomm | -83.6 | -78.6 | -85.2 | -80.2 | -70.7 | -78.5 | -84.8 | -81.7 | -76.4 |  |  | -71.2 | -82.7 | -84.9
Huawei |  |  | -86.1 | -82 | -71.5 |  |  |  |  |  |  | -71 |  | 
Apple |  |  |  |  |  | -76.7 | -85.1 |  |  |  |  |  | -77 | -85.4
Skyworks | -83.2 | -80.6 | -87.5 | -81.8 |  | -79.2 |  | -81.7 | -79.1 |  |  |  | -80.8 | 
Average | -83.4 | -79.6 | -86.2 | -81.3 | -68.7 | -78.4 | -85.3 | -81.7 | -77.6 | -81.5 | -82.8 | -70.3 | -80.7 | -86.3
Note 1: It is the average of companies REFSENS values larger than the agreed REFSENS value of smaller channel bandwidth.

## Slide 3: WF for n2, n25 35MHz REFSENS
  Two Antenna Port Reference Sensitivity QPSK PREFSENS for n2 and n25 35 MHz
  Uplink Configuration for Reference Sensitivity
Operating Band | SCS kHz | 35 MHz (dBm)
n2 | 15 | -83.6
 | 30 | -83.7
 | 60 | -83.8
n25 | 15 | -81.7
 | 30 | -81.8
 | 60 | -81.9
Operating Band | SCS kHz | 35 MHz (dBm) | Duplex Mode
n21 | 15 | 401 | FDD
 | 30 | 201 | 
 | 60 | 101 | 
n251 | 15 | 401 | FDD
 | 30 | 201 | 
 | 60 | 101 | 
NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1) |  |  | 

## Slide 4: WF for n2, n25 45MHz REFSENS
  Two Antenna Port asymmetric 40MHz Uplink / 45MHz Downlink Reference Sensitivity QPSK PREFSENS and Uplink configuration table
Operating band / SCS / Channel bandwidth / Channel allocations / REFSENS/ Duplex mode |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | Channel bandwidth (DL) (MHz) | Channel bandwidth (UL) (MHz) | FC (DL) (MHz) | FC (UL) (MHz) | UL allocation (LCRB) | REFSENS (dBm) | Duplex Mode
n2 | 15 | 45 | 40 | 1967.5 | 1890.0 | 401 | -79.6 | FDD
 | 30 |  |  |  |  | 201 | -79.7 | 
 | 60 |  |  |  |  | 101 | -79.8 | 
n25 | 15 | 45 | 40 | 1972.5 | 1895.0 | 401 | -77.6 | FDD
 | 30 |  |  |  |  | 201 | -77.7 | 
 | 60 |  |  |  |  | 101 | -77.8 | 
NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1) |  |  |  |  |  |  |  | 

## Slide 5: WF for n3 35MHz and 45 MHz REFSENS
  Two Antenna Port Reference Sensitivity QPSK PREFSENS for n3 35 MHz and 45 MHz
  Uplink Configuration for Reference Sensitivity
Operating Band | SCS kHz | 35 MHz (dBm) | 45 MHz (dBm)
n3 | 15 | -86.2 | -81.3
 | 30 | -86.3 | -81.4
 | 60 | -86.4 | -81.5
Operating Band | SCS kHz | 35 MHz (dBm) | 45 MHz (dBm)
n3 | 15 | 501 | 501
 | 30 | 241 | 241
 | 60 | 101 | 101
NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1). |  |  | 

## Slide 6: WF for n8 and n71 REFSENS
  Two Antenna Port asymmetric 20MHz Uplink / 35MHz Downlink Reference Sensitivity QPSK PREFSENS and Uplink configuration table
Operating Band | SCS kHz | Channel bandwidth (DL) (MHz) | Channel bandwidth (UL) (MHz) | FC (DL) (MHz) | FC (UL) (MHz) | UL allocation (LCRB) | REFSENS (dBm)
n8 | 15 | 35 | 20 | 942.5 | 897.5 | 25 | [-78.4]
 | 30 |  |  |  |  | 10 | [-78.5]
 | 60 |  |  |  |  |  | 
n71 | 15 | 35 | 20 | 634.5 | 680.5 | 25 | [-80.7]
 | 30 |  |  |  |  | 10 | [-80.8]
 | 60 |  |  |  |  |  | 
[NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1)] |  |  |  |  |  |  | 

## Slide 7: To be further investigated
For asymmetric Uplink /Downlink scenarios
  Option 1
    To add a new entry in "Table 5.3.6-1: FDD asymmetric UL and DL channel bandwidth combinations" for bands n8, n25 and n71.
    The impact of each UL-DL scenario on the default Tx-Rx frequency separation.
  Option 2
    To state that the REFSENS requirement is met for a specific duplex spacing in the general REFSENS section
  Other options are not excluded

## Slide 8: Refrens
R4-2104656 REFSENS of n8, n71, n25 for 35_45MHz channel bandwidth Murata Manufacturing Co Ltd.
R4-2104811 REFSENS evaluation of n8 and n71 for 35MHz channel bandwidth Mediatek India Technology Pvt.
R4-2104888 UL channel location for MSD calculation for bands n8 and n71 Apple
R4-2106283 Draft CR to 38.101-1 Introduce band specific requirements for 45MHz CBW for Band n1 China Telecom
R4-2106483 UE REFSENS for 35 MHz and 45 MHz Huawei, HiSilicon
R4-2106906 FR1 REFSENS table split and simplification Apple
R4-2107337 35-45MHz REFSENS for n2 n3 n8 n25 n71 Skyworks Solutions Inc.
R4-2107339 35MHz and 45MHz REFSENS Qualcomm Incorporated