## Slide 1: WF on PC2 n34 and n39 for NR
Moderator (CMCC)
3GPP TSG-RAN WG4 Meeting # 98-bis-e R4-2105386
Electronic Meeting, Apr. 12-20, 2021

## Slide 2
Issue 1-1-1: UE MOP and Tx power tolerance for n34 of Power class 2
Proposals
  Option1: The MOP and Tolerance for single antenna port are to be specified as 26dBm ±2 dB for band n34 of power class 2, and The MOP and Tolerance for UL MIMO are to be specified as 26dBm +2/-3 dB for n34 of power class 2.
  Option2: The power tolerance for PC2 for n34 is +2/-3. Regardless of single antenna port or UL MIMO case.
Issue 1-1-2: MPR and A-MPR
Agreement
  No changes to 1Tx PC2 MPR and A-MPR requirements for n34.
Issue 1-1-3: Release independent issue
Agreement
  The n34 power class 2 can be supported form Rel-15 by release independent manner.
WF on PC2 n34

## Slide 3
Issue 2-1-1: UE MOP and Tx power tolerance for n39 of Power class 2
Proposals
  Option1: The MOP and Tolerance for single antenna port are to be specified as 26dBm ±2 dB for band n39 of power class 2, and The MOP and Tolerance for UL MIMO are to be specified as 26dBm +2/-3 dB for n39 of power class 2.
  Option2: The power tolerance for PC2 for n39 is +2/-3. Regardless of single antenna port or UL MIMO case.
Issue 2-1-2: MPR and A-MPR
Agreement
  No changes to 1Tx PC2 MPR requirements for n39.
  Companies are encouraged to evaluate 1Tx PC2 NS-50 A-MPR at May RAN4 meeting.
Issue 2-1-3: Release independent issue
Agreement
  The n39 power class 2 can be supported form Rel-15 by release independent manner.
WF on PC2 n39

## Slide 4: Reference
[1]R4-2105014 Discussion on the PC2 UE RF requirements of NR n34, CMCC
[2]R4-2105015 Draft CR on PC2 UE RF requirements of n34 in Rel-17 TS 38.101-1, CMCC
[3]R4-2105016 Discussion on the PC2 UE RF requirements of NR n39, CMCC
[4]R4-2105017 Draft CR on PC2 UE RF requirements of n39 in Rel-17 TS 38.101-1, CMCC
[5]R4-2106548 Discussion on HP UE for Band n34, Xiaomi
[6]R4-2106549 Discussion on HP UE for Band n39, Xiaomi