## Slide 1: WF on Open issues for BCS4 (other than MSD)
T-Mobile USA, […]
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic Meeting, April 12th – 20th, 2021
R4-2105490

## Slide 2: Background
The BCS4 Work Item was approved at RAN#90
RAN4 has been making progress on BCS4, but there are some open issues that need to be resolved.

## Slide 3: Way Forward
Which type of band combination can BCS4 apply to?
  Proposal 1: inter-band and intra-band NR-CA, inter-band and intra-band NR-DC and SUL
Should BCS4 apply to all combinations, or on a per request basis?
  Proposal 2: It depends on whether or not we can get a generic solution to MSD. If MSD has to be worked per combination, then the support for BCS4 would need to be indicated in the tables
If it is decided that BCS4 needs to be indicated in the tables, what should the format be?
  Proposal 3: A single row as follows:
NR CA configuration | Uplink CA configuration | NR Band | Channel bandwidth (MHz) (NOTE 3) |  |  |  |  |  |  |  |  |  |  |  |  | Bandwidth combination set
 |  |  | 5 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 
CA_nXA-nYC | CA_nXA-nYA | nX | 5 | 10 | 15 | 20 |  |  |  |  |  |  |  |  |  | 0
 |  | nY | 5 | 10 | 15 | 20 | 25 | 30 |  |  |  |  |  |  |  | 
 |  | See nX channel bandwidths in Table 5.3.5-1 and nYC channel bandwidths in Table 5.5A.1-1. |  |  |  |  |  |  |  |  |  |  |  |  |  | 4

## Slide 4: Way Forward
  How should BCS4 be handled if there are both BCS4 and a traditional BCS(s) in the WID
    Proposal 4: For the same band combination, in case of both BCS0/1/2/3 and BCS4 exist in the WID, TP and draft CRs for BCS4 is enough, and BCS0/1/2/3 combinations are completed by default after BCS4 combinations TP/draft CR are approved.
  What text should be adopted for BCS4?
    Proposal 5:
    The configuration tables for CA describe Bandwidth Combination Sets. Bandwidth Combination Set 4 (BCS4) contains all possible defined channel bandwidths for each CC in the combination. The fact that BCS4 contains all channel bandwidths for each band does not alter if a channel bandwidth is mandatory or optional for a given band. Bandwidths which are identified as optional for the current version of the specification in Table 5.3.5-1 are still optional even with BCS4. The channel bandwidths the UE supports for each band and the maximum bandwidth for the band in the band combination are indicated in the UE capabilities. Other UE capabilities regarding bandwidths in the band combination are FFS. Support for BCS4 for a given band combination is indicated by a single row in the table.

## Slide 5: Way Forward
  Is any new signalling needed for BCS4?
    R4-2107327 explained how if there is new Rel-17 signalling needed for BCS4, then BCS4 cannot be release independent. For example, if there is new signalling for minimum channel BW, if the UE reports a minimum channel bandwidth that it supports for a BCS4 band combination, then a Rel-15 or Rel-16 gNB will ignore the new IE and will assume incorrectly that the UE supports all of the the lower channel BWs.
    Proposal 6: RAN4 will proceed with the introduction of BCS4 with no new signalling so it is release independent to Rel-15. RAN4 will continue to discuss the need for new signalling. If it is determined that new Rel-17 signalling like minimum channel bandwidth is needed, then RAN4 will introduce BCS5 which will be similar to BCS4 except that the new signalling will apply to BCS5, but not to BCS4.