## Slide 1: WF on gNB positioning measurement requirements
Ericsson
3GPP TSG-RAN WG4 Meeting # 98bis-e
Electronic Meeting, April 12-20, 2021
Agenda: 5.5.2.3
R4-2105755

## Slide 2: General: Beam sweeping during gNB measurement
gNB accuracy requirements do not mandate gNB RX beam sweeping
FFS: whether to capture the above agreements in the specification
Candidate options:
  Option 1:
    gNB accuracy requirements do not mandate gNB RX beam sweeping is captured only in the WF.
  Option 2:
    gNB accuracy requirements do not mandate gNB RX beam sweeping is included in the accuracy side conditions.

## Slide 3: General: Samples for gNB accuracy requirements
Default assumption is to define the gNB accuracy requirements based on single sample/shot measurement assumption
  FFS if multiple shots are used for lowest SRS BW group per SCS in case performance is not satisfactory.

## Slide 4: RoAoA side conditions for 1-O and 2-O gNB types
Following side condition is included in the gNB requirement:
  “gNB positioning measurement requirements apply for the same RoAoA as OTA reference sensitivity requirements for 1-O and 2-O BS”.

## Slide 5: SRS-RSRP: SRS BW grouping for accuracy requirements
gNB accuracy requirements shall be defined for group of SRS BWs
  grouping of SRS BWs will be decided based on link simulation results
Candidate options:
  Option 1:
Option 2:
    For SINR +3dB, one set of accuracy for all SRS BWs and for all combinations of comb+symbol
    For SINR -13dB,
      two sets of requirements, one for 24≤RB_num<[64] and the other for [64]≤RB_num.
SRS bandwidth in RB | SRS-RSRP measurement accuracy [dB] | 
 | Ês/Iot ≥ -13dB | Ês/Iot ≥ +3dB
24 ≤ BW ≤ 40 | TBD | TBD
40 ≤ BW ≤ 84 | TBD | TBD
88 ≤ BW ≤ 168 | TBD | TBD
176 ≤ BW ≤ 272 | TBD | TBD
SRS bandwidth in RB | SRS-RSRP measurement accuracy [dB] | 
 | Ês/Iot ≥ -13dB | Ês/Iot ≥ +3dB
32 ≤ BW ≤ 40 | TBD | TBD
44 ≤ BW ≤ 84 | TBD | TBD
BW ≥ 88 | TBD | TBD
Note 1: In tables 1 and 2, lower bound of BW ranges can be updated based on simulation results
Table 1: FR1
Table 2: FR2

## Slide 6: SRS-RSRP: Impact of SRS SCS on accuracy
SRS-RSRP accuracy is agnostic to SRS SCS within the same FR

## Slide 7: SRS-RSRP: Impact of SRS symbol and comb size on accuracy
FFS: whether SRS-RSRP accuracy is agnostic to SRS symbols and comb size or not will be decided based on further simulation with updated simulation assumptions.

## Slide 8: SRS-RSRP: Propagation condition for meeting accuracy
SRS-RSRP measurement accuracy shall be defined under AWGN

## Slide 9: SRS-RSRP: RF margin for SRS-RSRP accuracy for different gNB types
FFS: RF margin for different gNB types
Candidate options:
Option 1:
  RF calibration margin differs between gNB type 1-C and other gNB types:
    X=2.5dB for gNB type 1-C
    X=4dB for gNB type 1-H, 1-O and 2-O
Option 2:
  RF margin needs further discussion
    Investigate RF margin for different gNB types (1-C, 1-H, 1-O and 2-O)

## Slide 10: gNB Tx-Tx: SRS BW grouping for accuracy requirements
gNB accuracy requirements shall be defined for group of SRS BWs
  grouping of SRS BWs will be decided/updated based on link simulation results
SRS bandwidth in RB | SRS SCS [kHz] | gNB TOA measurementaccuracy [Tc] | 
 |  | Ês/Iot ≥ -13dB | Ês/Iot ≥ +3dB
24 ≤ BW ≤ 40 | 15 | TBD | TBD
40 ≤ BW ≤ 84 |  | TBD | TBD
88 ≤ BW ≤ 168 |  | TBD | TBD
176 ≤ BW ≤ 264 |  | TBD | TBD
48 ≤ BW ≤ 84 | 30 | TBD | TBD
88 ≤ BW ≤ 168 |  | TBD | TBD
176 ≤ BW ≤ 272 |  | TBD | TBD
32 ≤ BW ≤ 40 | 120 | TBD | TBD
44 ≤ BW ≤ 84 |  | TBD | TBD
88 ≤ BW |  | TBD | TBD
Note 1: 60kHz SCS can be added based on the simulation results
Note 2: Lower bound of BW ranges can be updated based on simulation results

## Slide 11: gNB Rx-Tx: Impact of SRS SCS on accuracy
SRS-RSRP accuracy depends on SRS SCS

## Slide 12: gNB Rx-Tx: Impact of SRS symbol and comb size on accuracy
FFS: whether SRS-RSRP accuracy is agnostic to SRS symbols and comb size or not will be decided based on further simulation with updated simulation assumptions.

## Slide 13: gNB Rx-Tx: RF margin for gNB Rx-Tx accuracy for different gNB types
gNB Rx-Tx time difference accuracy is defined as: ± (X+Z) Tc.
Where:
  X is numerical value derived from the link simulation results
  Z accounts for RF margin and is declared by manufacturer.
    Z depends on gNB type (1-C, 1-H, 1-O, 2-O)

## Slide 14: UL RTOA measurement accuracy requirements
Agreements in GTW:
  Do not define UL RTOA performance requirements in Rel-16 NR Positioning.