## Slide 1: WF on RRM requirements for spectrum WIs
Ericsson
3GPP TSG-RAN WG4 Meeting # 98bis-e
Electronic Meeting, April 12-20, 2021
Agenda: 7.25.5, 7.27.3, 7.39.2
R4-2105784

## Slide 2: RRM requirements for 35MHz and 45MHz
Introduction of 35 MHz and 45 MHz channel bandwidths does not have any impact on RRM core requirements.
Introduction of 35 MHz and 45 MHz channel bandwidths does not have any impact on RRM performance requirements including RRM test cases.

## Slide 3: RRM performance requirements for band n262 for PC3
Min SSB_RP/CSI-RS_RP for conditions for measurements at RX beam peak direction for UE power class 3 for band n262
Min SSB_RP/CSI-RS_RP for conditions for measurements for spherical coverage direction for UE power class 3 for band n262
No. | Condition for requirements | Minimum SSB_RP [dBm] (SCS=120 kHz) | Minimum CSI-RS_RP [dBm] (SCS=60 kHz)
1 | Intra-frequency/inter-freqyuency measurements for cell re-selection | -103.6 | N/A
2 | Intra-frequency measurements in RRC connected state | -106.6 | N/A
3 | Inter-freqyuency measurements in RRC connected state | -104.6 | N/A
4 | SSB based L1-RSRP | -103.6 | N/A
5 | CSI-RS based L1-RSRP | N/A | -106.6
6 | RRC connection release with redirection | -104.6 | N/A
No. | Condition for requirements | Minimum SSB_RP [dBm] (SCS=120 kHz) | Minimum CSI-RS_RP [dBm] (SCS=60 kHz)
1 | Intra-frequency/inter-freqyuency measurements for cell re-selection | -90.5 | N/A
2 | Intra-frequency measurements in RRC connected state | -93.5 | N/A
3 | Inter-frequency measurements in RRC connected state | -91.5 | N/A
4 | SSB based L1-RSRP | -90.5 | N/A
5 | CSI-RS based L1-RSRP | N/A | -93.5
6 | RRC connection release with redirection | -91.5 | N/A

## Slide 4: RRM requirements for band n262 for PC1, 2 and 4
Core requirements:
  The FR2 band group foAgreement on RRM band grouping for the remaining UE power classes (PC1, PC2 and PC4) for band n262 is based on RF group agreements on their REFSENS requirements.
  RRM core requirement discussion postponed to RAN4#99-e.
Performance requirements:
  The minimum received signal level (SSB_RP or CSI-RS levels) for RX for beam peak direction and for spherical coverage direction as part of the side conditions for the remaining UE power classes (PC1, PC2 and PC4) for band n262 will be defined in sections B.1 and B.2 of TS 38.133 after the RF group has agreed on the corresponding UE RF requirements (UE REFSENS and EIS spherical coverage).
  RRM performance requirement discussion postponed to RAN4#99-e.

## Slide 5: RRM requirements for FR2 FWA PC5 for band n259
Core requirements:
  The FR2 band group for PC5 for n259 will be defined in Table 3.5.3-1 of TS 38.133 after the RF group has agreed on the UE RF requirements (UE REFSENS) for FR2 FWA power class 5 with maximum TRP of 23 dBm for band n259.
  RRM core requirement discussion postponed to RAN4#99-e.
Performance requirements:
  The minimum received signal level (SSB_RP or CSI-RS levels) for RX for beam peak direction and for spherical coverage direction as part of the side conditions will be defined in sections B.1 and B.2 of TS 38.133 after the RF group has agreed on the UE RF requirements (UE REFSENS and EIS spherical coverage) for FR2 FWA power class 5 with maximum TRP of 23 dBm for band n259.
  RRM performance requirement discussion postponed to RAN4#99-e.