## Slide 1: 3GPP TSG-RAN WG4 Meeting #98-bis-e Electronic Meeting, 12 – 20 April, 2021
Intel
WF on R17 NR MG enhancements –NCSG
R4-2105792

## Slide 2
Agreements in the 1st round/GTW
Agreements in the 2nd round
Remaining open after 1st round discussion

## Slide 3: Scenarios and use cases
The use cases of NR NCSG can be
  Eliminate/reduce interruption rate and interruption length/duration due to measurements on [deactivated Scell, Scell with dormant BWP or unused RF chain
  FFS on
    intra-frequency measurements with MG,
    inter-frequency measurements with MG,
    inter-RAT measurements,
Per-CC gap is not considered for NCSG
NCSG patterns shall be defined for both synchronous and asynchronous operations
  FFS on RAN4 needs to define separate NCSG patterns for sync and async scenarios

## Slide 4: NCSG pattern
The general NCSG design principle :
  Option 1. Define NCSG patterns for All 26 MG patterns in Rel16
  Option 2 Define NCSG patterns for subset of the legacy MG patterns in [TS38.133 v16.5.0]
  FFS on which subset of legacy MG patterns
The NCSG gap patterns are defined based on the absolute RF retuning time or not?
  Option 1: NO, based on a generic interrupted duration [FFS]
    Option1-1: ML=MGL-VIL1-VIL2
    Option1-2: ML=legacy MG window length
  Option 2: Yes, based on the RF retuning time (RRT). ML=MGL-RRT1-RRT2
    FFS on the length of RRT
Support both per FR and per UE NCSG patterns in Rel17

## Slide 5: NCSG configuration
Only NW explicit configuration for NCSG is considered in Rel17

## Slide 6: Impacts on RRM requirements due to NCSG
FFS on Interruption requirements
  Option 1: The interruption requirements in TS38.133 and TS36.133 shall be revisited
  Option 2: Existing interruption requirements for SCell activation/deactivation can serve as starting point for the study of VIL requirements
  Option 3: the interruption is proposed as following
  Option 4: RAN4 to further discuss the condition, capability and impacts to measurement requirements for UE to use NCSG to control interruptions due to measurement on deactivated SCC or Scell in dormancy
FFS on CSSF when NCSG is configured
FFS on the existing measurement mode requirements (effective MGRP, data scheduling depends on gap configuration) can be the baseline
FFS on Per-UE or Per-FR capability support
  Option 1:per UE and per FR NCSG for RRM measurement needs the specific UE capability.
  Option 2: No additional NCSG capability for per-UE and per-FR differentiation is needed
  Others
SCS | Synchronous |  | Asynchronous | 
 | interruption length before measurement | interruption length after measurement | interruption length before measurement | interruption length after measurement
15KHz SCS | 1 slot | 1 slot | 2 slots | 2 slots
30KHz SCS | 2 slots | 2 slots | 3 slots | 3 slots
60KHz SCS | 3 slots | 3 slots | 4 slots | 4 slots
120KHz SCS | 6 slots | 6 slots | 7 slots | 7 slots

## Slide 7: Measurement applicability
FFS on whether NCSG can be configured simultaneously with legacy gap pattern
  Option 1. Yes.
    FFS on how to apply the measurement requirements (e.g. CSSF) under this assumption
  Option 2. In the first phase of the WI , No
    FFS on how to apply the measurement requirements (e.g. CSSF) under this assumption
FFS on RF combination limitation
  Option 1. UE is not expected to measure 2 inter-freq/RAT layers in parallel even if UE reports the support of NCSG to both corresponding bands
  Others
FFS on Rx beam limitation
  Option 1. : NW needs to be informed that the inter-frequency measurements with NCSG is CBM or IBM with serving cells in FR2.
  Option 2: NCSG in FR2 should be deprioritized in current stage.
  Others
FFS on scheduling and measurement restriction
  Option 1: When NCSG is configured then during the ML the existing scheduling restriction requirements defined in TS 38.133 shall also apply
  Others

## Slide 8: Signaling
FFS on How to consider the relation between NCSG and ‘NeedForGap’?
  Option 1 :The “NeefForGap” signaling structure can be reused for NR NCSG as a start point
  Option 1a :Rel-17 NCSG capability is reported on top of existing RAN2 ‘NeedForGap’ signaling structure with a new component ‘NCSG’.
  Option 1b: Extend the Rel-16 NeedForGap ignaling for UE to indicate
    Need for normal MG, or
    No need for normal MG but NCSG, or
    No need for either normal MG or NCSG
  Option 2 :Don’t reuse Rel-16 ‘NeedForGap’ signaling for NCSG
  Option 3: Let RAN2 decide NCSG signaling details and any relation between NCSG and ‘NeedForGap’ based on RAN4 technical input on NCSG pattern design
  Option 4 : FFS when the NCSG pattern design as well as NCSG applicability and UE capability support are finalized
Note: RAN4 tries to reach consensus on what needs to be signalled for NCSG support. The final signaling design is still up to RAN2 decision.

## Slide 9: Specification impacts
Decision of the specification section(s) for specifying the NCSG patterns is deferred until reasonable level of agreements on NCSG concept and patterns are agreed by RAN4