## Slide 1: WF on NR-U BS wideband operation testing
Nokia, Nokia Shanghai Bell
R4-2106005
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic Meeting, 12 April – 20 April, 2021

## Slide 2: Background (1/4)
This WF summarizes agreements from RAN4#98-bis-e meeting on NR-U BS wideband operation testing. Following contributions were submitted:
[1] R4-2106308, Discussion on test configurations for wideband NR-U operation, Nokia, Nokia Shanghai Bell
[2] R4-2106311, Draft CR to TS 38.141-1 – Test configurations for NR-U BS conformance tests, Nokia, Nokia Shanghai Bell
[3] R4-2106312, Draft CR to TS 38.141-2 – Test configurations for NR-U BS conformance tests, Nokia, Nokia Shanghai Bell

## Slide 3: Background (2/4)
Specific emission mask is specified in the RAN4 BS core specifications TS 38.104, for one and two non-transmitted channels, as well as the masks are dependent on configured transmission bandwidth
The introduction of non-transmitted channels and an adaptive emission mask means new test requirements need to be defined.
The new requirements specified in the core specifications for NR-U including those related to the non-transmitted channels has to be verified during the conformance testing.
Figure 1: Wideband case for 4x20MHz with both a 1x20MHz non-transmitted channel between transmitted channels and also a non-transmitted channel at the edge of the wideband channel

## Slide 4: Background (3/4)
NRTC3 can be used for non-contiguous spectrum operation where there may be also one, two or more non-transmitted 20 MHz channels between two transmitted 20 MHz channels as shown in Fig. 1 and 2. However, NRTC3 cannot be used for the BS in case where there is only one 40 MHz transmitted sub-block within the BS channel bandwidth as shown in Fig. 3. As a result, a new/modified TC needs to be defined to ensure the NR-U BS will meet the OBUE masks in this case.
Figure 2: Wideband case for 3x20 MHz with a 1x20 MHz non-transmitted channel between transmitted channels of the wideband channel

## Slide 5: Background (4/4)
NRTC1 can be used for contiguous spectrum operation where there are one or more contiguous non-transmitted 20 MHz channels for 60 MHz or 80 MHz channel bandwidth as shown in fig. 3:
Figure 3: Wideband case for 4x20 MHz with a 2x20 MHz non-transmitted channel on the edge of the wideband channel

## Slide 6: WF on NR-U BS wideband operation testing
Agreements:
  Option 1:
  To define modified TC for band n46 and n96 for NRTC1 and NRTC3 where the one 40 MHz transmitted sub-block is placed at one edge of the NR-U BS CBW, and the one 40 MHz transmitted sub-block is placed at another edge, in order to provide a more demanding TC for the BS OBUE tests.
  Option 2:
  No new test configurations for in-carrier BS OBUE requirements.
  Option 3:
  new TBD test configurations for NR-U in-carrier BS OBUE requirements.