## Slide 1: WF on CQI reporting requirements for inter-cell interference MMSE-IRC
Ericsson
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic meeting, 12 – 20 April 2021
Agenda item: 8.14.1
Document for: Approval
R4-2106117

## Slide 2: Open Issues
Issue 1: Whether to define CQI reporting requirements with inter-cell interference scenario
Option 1: Yes
Option 2: Need further discussion

## Slide 3: Open Issues (If Issue 1 is agreed)
Issue 2: Interference covariance estimation granularity for CQI reporting
Option 1: the interference covariance can be estimated and averaged among multiple PRBs, and the exact PRB number for interference covariance averaging needs further discussion
Option 2: Up to UE implementation
For information: if we follow the agreements in UE demodulation requirements, interference covariance estimation granularity up to UE implementation
  Interested companies can further check the results for per PRB bundle size or per PRB and per slot basis

## Slide 4: Open Issues (If Issue 1 is agreed)
Issue 3: Interference model for CQI reporting
Option 1: As the starting point, model one inter-cell interferer with DIP of -0.41dB and static propagation condition
Option 2: Align with assumptions for demodulation requirements

## Slide 5: Open Issues (If Issue 1 is agreed)
Issue 4: Test metric for CQI reporting
Option 1: Reuse the LTE test metric as a starting point, which includes:
  1) the relative increase of the throughput obtained when the transport format is that indicated by the reported CQI subject to an interference model compared to the case with a white Gaussian noise model, and
  2) when transmitting the transport format indicated by each reported wideband CQI index subject to an interference source with specified DIP, the average BLER for the indicated transport formats shall be greater than or equal to 2%.
Option 2: Need further discussion
  For static condition, test metric 2) in Option 1 may not work. In LTE, these requirements were defined for fading conditions where this may make more sense.