## Slide 1: Way Forward on MMSE-IRC for intra-cell inter-user interference
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #98-bis-e
Electronic Meeting, 12th – 20th Apr. 2021
Agenda item: 8.14.2
R4-2106118
Document for: Approval

## Slide 2: Inter-user interference modeling for phase I evaluation

## Slide 3: Inter-user interference modeling for phase I evaluation
Paired UE number
  Under 2Tx and 4Tx with random PMI for target UE, use 1 target UE + 1 interference UE as starting point for initial simulation
  For scenario of Tx more than 4, other options not precluded
  Interested companies can bring analysis on scenarios of interference UE more than 1
Rank for target and interference PDSCH
  Option 1: Rank 1 only for target UE and interference UE
  Option 2: Cover both rank 1 and rank 2 per UE
    Option 2A: [1+1], [2+2] for target UE and interference UE
    Option 2B: [1+1], [2+1] for target UE and interference UE
    Option 2C: [1+1], [1+2] for target UE and interference UE
    Note: Rank 2 only for 4RX case

## Slide 4: Inter-user interference modeling for phase I evaluation
Correlation between the propagation channel of the paired UEs
  Ensure Low correlation between the co-scheduled UEs
Antenna configuration
  For Rx antenna number
    Cover both 2Rx and 4Rx
  For Tx antenna number
    Using 2Tx and 4Tx with random PMI for target UE as starting point for initial simulation
    Other options not excluded
    Interested companies can bring analysis with 8Tx and 16Tx cases with following PMI for target UE

## Slide 5: Inter-user interference modeling for phase I evaluation
Codebook Type
  Option 1: Type I Single Panel only
  Option 2: Cover Type I Single Panel and Type II codebook
    Option 2A: For 2Tx and 4Tx, use Type I SP codebook. Type II precoder can also be applied for 4Tx

## Slide 6: Inter-user interference modeling for phase I evaluation
PMI selection and precoding matrix generation
  Option 1: Random based target UE PMI selection
    Option 1A: Random selection based precoder generation with QRD orthogonalization processing as below
    Option 1B: Random PMI selection for the target UE, and select the precoder for the interference UE to ensure orthogonality
    Option 1C: Random PMI selection for both target and interference UE, with ensuring the selected PMI matrix shall not be identical to the precoding matrix applied for the UE under test
    Option 1D: Randomly select precoder from codebooks corresponding to number of MIMO layers equal to total number of MU MIMO layers (i.e. serving Rank + interference Rank) and take several columns from this precoder for serving UE signal and remaining columns for interference UE signal.
  Option 2: Feedback-based target UE PMI selection
    Option 2A: If the feasibility can be confirmed by the TE vendor, use ZF precoding based on the reported PMI from the target UE, and the randomly generated PMI from the interference UE(s)
    Option 2B: Feedback-based PMI selection for the target UE, select the precoder for the interference UE to ensure the orthogonality
    Option 2C: Feedback-based PMI selection for target UE, and random PMI selection for interference UE, with ensuring the selected PMI matrix shall not be identical to the precoding matrix applied for the UE under test
  Option 3: Fixed precoding matrix for one or both co-scheduled UEs
  TE vendors’ feedback on the feasibility of the above options:
    Keysight: 1A and 2A are of less feasibility. The preferences are in this order 3, 1C, 1B, 2B.
    R&S: 1A and 2A is very complex and not really feasible. Preference in order 3 > 1C >> 1B.
    Anritsu: Need more time to study.

## Slide 7: Inter-user interference modeling for phase I evaluation
PRB bundling size and precoding granularity
  For 2Tx and 4Tx
    Option 1: Per 2 PRBs for frequency domain and per slot for time domain
    Option 2: Per 4 PRBs for frequency domain and per slot for time domain
  For more than 4Tx(if introduced):
    Option 1:
      Wideband for 8Tx for target and paired UEs.
      For 16Tx, use subband precoding if it is feasible for TE to calculate ZF precoding matrix per subband
    Other option not precluded
MCS for interfering PDSCH
  Random 16 QAM signal generation

## Slide 8: Inter-user interference modeling for phase I evaluation
DMRS ports for 1 target and 1 interfering UE scenario
  Option 1: only consider rank 1 transmission
    Option 1A: DMRS port 0 for target UE, DMRS port 1 for the interference UE, i.e., same CDM group
    Option 1B: DMRS port 0 for target UE, DMRS port 2 for the interference UE, i.e., different CDM groups
  Option 2: consider both rank 1 and rank 2 transmission
    With [2,2] transmission for target UE and interference UE
      DMRS port 0/1 for target UE, DMRS port 2/3 for the interference UE
    With rank [1,2] or rank [2,1] transmission for the target UE and interference UE
      Option 2A: DMRS port 0 (and 1) for target UE, port 2 (and 3) for the interference UE, i.e., use different CDM groups for the target and interference UEs
      Option 2B:
        For rank [1,2], DMRS port 0 for target UE, DMRS port 1 and 2 for the interference UE
        For rank [2,1], DMRS port 0 and 1 for target UE, DMRS port 2 for the interference UE

## Slide 9: Inter-user interference modeling for phase I evaluation
DMRS ports for 1 target and more than 1 interfering UE scenario (if introduced) (Further apply the agreement of rank)
  For rank 1 transmission,
    Option 1: DMRS port 0 for target UE, DMRS port i for the i-th interference UE (i = 1, 2,...)
  For rank 2 transmission,
    with same rank number per UE,
      Option 1: DMRS port 0/1 for target UE, DMRS port 2i and 2i+1 for the i-th interference UE e.g. use different CDM group for the target and interference UEs

## Slide 10: Inter-user interference modeling for phase I evaluation
DMRS type and DMRS additional position
  DMRS Type 1 with 1 additional DMRS
Ratio of PDSCH EPRE to DM-RS EPRE
  0 dB and -3 dB when the number of DM-RS CDM groups without data is 1 and 2 respectively
Whether to use same DMRS pattern and the same sequence for all co-scheduled UEs
  Option 1: Use the same following DMRS configuration for all co-scheduled UEs
    Same DMRS type
    Same DMRS additional position
    Same scrambling ID
    Same cell ID
  Option 2: Different scrambling id for different CDM groups
  Option 3: No restriction for simulation

## Slide 11: Reference receiver for phase I evaluation

## Slide 12: Reference receiver for phase I evaluation
Candidate Receiver
  Prioritize MMSE-IRC processing with serving signal demodulation for initial simulation
  Other options are not precluded
    Option 1: MMSE-IRC processing with joint (serving + interference) signal demodulation
      , where
Interference estimation for cases with 2 DMRS CDM group
  Option 1: For cases with 2 DMRS CDM groups, the interference should be estimated based on the REs occupied by both of the two DMRS CDM groups
  Option 2: Not to consider this scenario
  Option 3: Up to UE implementation and cannot be specified as simulation assumption

## Slide 13: Reference receiver for phase I evaluation
Interference estimation granularity
  Option 1: Per PRB and per slot based interference covariance matrix estimation
  Option 2: Same with the PRB bundling size
  Option 3: Up to UE implementation
Whether to introduce network assistance to assist the receiver
  FFS on whether to introduce network assistance and if so how to assist the receiver

## Slide 14: PDSCH parameters for phase I evaluation

## Slide 15: PDSCH parameters for phase I evaluation
SCS
  15kHz SCS for FDD
  30kHz SCS for TDD
Channel bandwidth
  Option 1
    For FDD 15kHz SCS: Cover 10MHz and 50MHz CBW
    For TDD 30kHz SCS: Cover 40MHz and 100MHz CBW
  Option 2:
    For FDD 15kHz SCS: Cover 10MHz
    For TDD 30kHz SCS: Cover 40MHz
  Option 3:
    For FDD 15kHz SCS: Cover 10MHz and 40MHz CBW
    For TDD 30kHz SCS: Cover 40MHz and 100MHz CBW
TDD configuration
  7D1S2U(6D+4G+4U) for 30kHz TDD

## Slide 16: PDSCH parameters for phase I evaluation
MIMO correlation for each UE
  Cover XP High, XP Medium, XP low and ULA low for phase I evaluation, and make further down-selection based on results
Propagation condition
  Cover both TDLA30-10 and TDLC300-100 in phase I, and decide whether down-selection or adjustment is needed based on the simulation results
MCS for target UE
  Cover QPSK MCS 4, 16QAM MCS 13, and 64QAM MCS 19 for initial simulation
    Rank 1: QPSK, 16QAM
    Rank 2: 16QAM, 64QAM
  Other options are not preclude
PDSCH mapping type
  Type A

## Slide 17: PDSCH parameters for phase I evaluation
PDSCH Resource Allocation
  Time Domain
    Starting symbol 2 and duration 12 as baseline
  Frequency Domain
    Full PRB allocation as baseline
HARQ Process Number
  4 for FDD 15kHz SCS and 8 for TDD 30kHz SCSMCS for target UE
SSB configuration
  SSB position in burst: first SSB in Slot#0; SSB periodicity: 20ms.
  The slot #0 in every 20 ms is not scheduled for PDSCH transmission

## Slide 18: PDSCH parameters for phase I evaluation
TRS, NZP CSI-RS and ZP CSI-RS Configuration
  For TRS and ZP CSI-RS, reuse the Rel-15 assumptions for PDSCH demodulation requirement.
  For NZP CSI-RS,
    Reuse the Rel-15 general assumptions for PDSCH demodulation requirement and extend the configuration for more than 4 ports
    The configuration should be extended if 8Tx or 16Tx is used
Performance evaluation metrics
  Measure the 70% max throughput performance of the target UE
  Evaluate the gain of MMSE-IRC over MMSE under the same simulation setup as baseline
  Interested companies also encouraged to bring analysis for performance difference between the case with and without co-scheduled UE