## Slide 1: WF on 1024QAM BS RF requirements
R4-2106121
Moderator (Ericsson)

## Slide 2: Agreements
0 dB RE power control dynamic range should be reused for 1024-QAM
Power back-off for 1024QAM (independent of 256QAM backoff) will be enabled. Details of how to specify are for the conformance phase
The following parameters were identified as needing more consideration for EVM.
  Wider bandwidths
  30kHz SCS (as well as 15kHz SCS)
  Spectral Utilization
  CFR (Crest Factor Reduction)
  TX linearity (in particular PA non-linearity)
  Effects in the digital domain
  I/Q compression

## Slide 3: WF for further discussions
Phase noise
  Option 1: Phase noise is of importance due to e.g. Bands up to 4.9GHz where it may be greater and should be considered in the EVM link budget
  Option 2: Phase noise is not of significance when deriving EVM for 1024QAM in FR1 as it is small compared to the other factors (mentioned on page 2)
BS class
  Option 1: Do not define 1024QAM RF requirements for the wide area BS class
  Option 2: Define 1024QAM RF requirements for all BS classes
Link level simulation assumptions
  Use parameters in R4-2104726 as a basis for link level parameters, but use a wider bandwidth

## Slide 4: Work split for BS CR drafing
Spec number | Responsible
38.104 | Huawei
38.141-1 | ZTE
38.141-2 | Ericsson
37.145-1 | CATT
37.145-2 | Nokia