## Slide 1: Way forward on analysis and framework of triple beat issue of 3CC UL with contiguous intra band UL CA
Qualcomm Inc., …
R4-2105335
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic meeting, 12 – 20 Apr. 2021

## Slide 2: Background: RAN and RAN4 agreements
RAN agreements in [6] Guidelines for Combinations Not for Block Approval and relevant to this WF:
UL CA with three or more non-contiguous CCs (feature not yet defined) including
  Inter-band UL CA consisting of intra-band non-contiguous UL CA
RAN4 agreements this meeting and relevant to this WF:
All companies agree that MSD related to triple beat of FR1 intra-band contiguous UL CA with an additional FR1 UL band needs to be analyzed for 2 and 3 band inter-band cases.
MSD related to triple of FR1 intra-band contiguous UL CA part with a FR1 UL in a second band needs to be analyzed
Develop a framework for such analysis

## Slide 3: WF: Handling of 3ULCC cases with intra-band UL CA part
The different cases for which triple beat analysis applies is further discussed:
  Applies to EN/NE-DC, NR CA, and NR-DC.
  Applies to both LTE and NR intra-band UL CA.
  FDD band + intra-band UL for 2 band only.
  Applies to triple beat product falling in a 3rd DL band with simultaneous Tx/Rx of 3rd DL band with the 2 UL bands
  3rd order triple beat mainly but assess the need to investigate higher orders up to 5th order.
  Look at PC3 and PC2.
  Both MSD and band protection should be assessed.
Study at least one example for framework.
  Examples flagged in [1]: DC_2C_n71A, DC_3C_n5A, DC_7C_n5A, DC_28A_n7B, DC_8A_n79C, DC_3A_n41C.
Develop a framework for such analysis with associated requirement tables

## Slide 4: WF: Handling of 3ULCC cases with intra-band UL CA part
Analysis of MSD related to triple of FR1 intra-band contiguous UL CA part with a FR1 UL in a second band for 2 and 3 band inter-band combinations.
  UL configuration to use.
  MPR applicability
  Power sharing
  Correction Factors
Recommendation for the identifying flagged cases [1].
  For MSD:
  For Band Protection:
Priority is for 3CC cases.
4CC cases not precluded

## Slide 5: WF: Handling of 3ULCC cases with intra-band UL CA part
Example Screening for MSD cases: 28A_n7B, 2C_n71A, 3C_n5A, 7C_n5A, and 8A_n79C
Screening can apply to 4CCs with contiguous blocks on each band.
IMD3/IMD5 could coincide with triple beat(s) although not shown here but discussed in [5
Combo | FDD/TDD_Band | ULCA_BW Band | ULCA_BW_max | FDD_BW_max | FDD/TDD Duplex | Issue (1/0)
3A_n7B | 3 | n7 | 50 | 20 | 95 | 0
28A_n7B | 28 | n7 | 50 | 20 | 55 | 1
1A_n7B | 1 | n7 | 50 | 20 | 190 | 0
1C_n3A | n3 | 1 | 40 | 40 | 95 | 0
2C_n41A | n41 | 2 | 40 | 100 | 0 | 0
2C_n71A | n71 | 2 | 40 | 20 | 46 | 1
3C_n1A | n1 | 3 | 40 | 50 | 190 | 0
3C_n5A | n5 | 3 | 40 | 20 | 45 | 1
3C_n7A | n7 | 3 | 40 | 50 | 120 | 0
3C_n28A | n28 | 3 | 40 | 30 | 55 | 0
3C_n41A | n41 | 3 | 40 | 100 | 0 | 0
3C_n77A | n77 | 3 | 40 | 100 | 0 | 0
3C_n78A | n78 | 3 | 40 | 100 | 0 | 0
3C_n79A | n79 | 3 | 40 | 100 | 0 | 0
7C_n1A | n1 | 7 | 40 | 50 | 190 | 0
7C_n3A | n3 | 7 | 40 | 50 | 95 | 0
7C_n5A | n5 | 7 | 40 | 20 | 45 | 1
7C_n28A | n28 | 7 | 40 | 30 | 55 | 0
7C_n78A | n78 | 7 | 40 | 100 | 0 | 0
8A_n79C | 8 | n79 | 200 | 20 | 45 | 1
39C_n41A | n41 | 39 | 40 | 100 | 0 | 0
40C_n78A | n78 | 40 | 40 | 100 | 0 | 0
41C_n3A | n3 | 41 | 40 | 50 | 95 | 0
41C_n77A | n77 | 41 | 40 | 100 | 0 | 0
41C_n78A | n78 | 41 | 40 | 100 | 0 | 0
41C_n79A | n79 | 41 | 40 | 100 | 0 | 0
42C_n28A | n28 | 42 | 40 | 30 | 55 | 0
42C_n3A | n3 | 42 | 40 | 50 | 95 | 0
Band X_UL
Band Y UL
Band X_DL
ULCAMBW
ULCAMBW
Duplex
TripleBeat
IMD3

## Slide 6: References:
[1] R4-2107345 Inter-band ULCA with more than 2CCs, Qualcomm Incorporated, R4#98bis-e
[2] R4-2106908 FR1 CA/DC band combinations not for block approval, Apple, R4#98bis-e
[3] R4-2104818 Handling of Inter-band UL Configuration Including NR Intra-band ULCA, Skyworks Solutions Inc., R4#98bis-e
[4] R4-2104507 DraftCR for NR inter band CA DC combinations for 2DL with up to 2 bands UL, Verizon Denmark, R4#98bis-e
[5] R4-2103097 Way forward on introduction of NR intra-band UL CA as UL configuration in an inter-band combination, Skyworks Solutions Inc., RAN4#98e
[6] RP-210892 WF on guidelines for Rel-17 FR1 CA/DC band combinations approval handling, Apple Inc., Skyworks Solutions Inc., RAN#91e