## Slide 1: WF on REFSENS Table Split and Simplification
Apple
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic Meeting, April 12th – 20th, 2021
R4-2105365

## Slide 2: Background
Due to the gradual introduction of brand new FR1 channel bandwidths, the REFSENS table based on the current format in TS 38.101-1 Table 7.3.2-1 has expanded substantially in horizontal direction and gone beyond the word document page width which has caused REFSENS requirements virtually unreadable in both Rel-16 and Rel-17 specifications as illustrated below where band numbers have become invisible.

## Slide 3: Background
To mitigate the current FR1 REFSENS table readability issue and accommodate more potential new channel BWs in future, splitting REFSENS table based on FDD bands and TDD bands has been proposed in this meeting [1].
The proposed approach in [1] by splitting the REFSENS table has demonstrated the effectiveness in reducing the table width which also received full positivity during the first-round email discussions.
The idea behind this table split approach is that
  FDD band channel BWs are only limited to 50 MHz and below while REFSENS are not fully scalable with channel BW.
  TDD bands are taking all possible channel BWs, but the REFSENS are scalable with channel BW and can be specified with equation-based representation to substantially reduce the table width.
This WF proposes RAN4 to adopt this new REFSENS table format starting from Rel-17.

## Slide 4: Way Forward
FR1 REFSENS table in TS 38.101-1 Table 7.3.2-1 is modified based on the split table format proposed in [1] starting from Rel-17.
Add a note in REFSENS table for TDD bands to indicate that “NRB” in REFSENS formula is the maximum transmission bandwidth configuration as defined in Table 5.3.2-1.
Companies are encouraged to verify the equation-based REFSENS formula for TDD bands in [1].
Companies are also encouraged to further simplify the REFSENS table for FDD/SDL bands potentially with equation-based REFSENS representation.

## Slide 5: References
[1] R4-2106906 “FR1 REFSENS table split and simplification”, Apple