## Slide 1: WF on n262 UE RF
Nokia, Nokia Shanghai Bell
RAN4#98-Bis-e R4-2105370
e-Meeting, 12-20 Apr. 2021

## Slide 2: Sub-topic 1-1: Minimum Peak EIRP for PC1, PC2, and PC4
  Way-forward:
    Agree on the average in RAN#99e for inputs available by then.
      Averaging method is FFS, whether mW or dBm average is used, or whether extreme values are included or not.
power class | Qualcomm | Vivo | Sony | Ericsson | Nokia | Intel | Average made over mW [dBm]
 | R4-2104492 | R4-2104517 | R4-2104696 | R4-2104696 | R4-2104712 | R4-2102906 | 
PC1 | 33.6 | 33.6 | 35 | 35 | 34 | 29.5 | 33.8
PC2 | 22.6 | 22.6 | 24 | 24 | 23 |  | 23.3
PC4 | 29.6 | 27.6 | 29 | 29 | 28 |  | 28.7

## Slide 3: Sub-topic 1-2: EIRP spherical coverage for PC1, PC2, and PC4
Gain drop (dB) (min peak EIRP – EIRP special coverage) |  | PC1 | PC2 | PC4
 |  | @85th %ile | @60th %ile | @20th %ile
Band | n257 | 8.0 | 11.0 | 9.0
 | n258 | 8.0 | 11.0 | 9.0
 | n259 |  |  | 
 | n260 | 8.0 |  | 12.0
 | n261 | 8.0 | 11.0 | 9.0
  Way-forward:
    It is further discussed what gain drop is specified for n262 in RAN4#99e.
      Possible option: Reuse a gain drop of an existing band (e.g., n260) for consistency with the work already done.

## Slide 4: Sub-topic 2-1: REFSENS for 50 MHz channel and -1 dB target SNR
power class | Qualcomm | Vivo | Sony | Ericsson | Nokia | Intel | Average made over mW [dBm]
 | R4-2104492 | R4-2104516 | R4-2104695 | R4-2104695 | R4-2104712 | R4-2102907 | 
PC1 | -92 | -92 | -94.7 | -94.7 | -91.5 | -90.7 | -92.3
PC2 | -86.5 | -86.5 | -87.7 | -87.7 | -86 |  | -86.8
PC4 | -91.5 | -91.5 | -89.7 | -89.7 | -91 |  | -90.6
  Way-forward:
    Agree on the average in RAN#99e for inputs available by then.
      Averaging method is FFS, whether mW or dBm average is used, or whether extreme values are included or not.

## Slide 5: Sub-topic 2-2: EIS spherical coverage for PC1, PC2, and PC4
Gain drop (dB) (-REFSENS + EIS special coverage) |  | PC1 | PC2 | PC4
 |  | @85th %ile | @60th %ile | @20th %ile
Band | n257 | 8.0 | 11.0 | 9.0
 | n258 | 8.0 | 11.0 | 9.0
 | n259 |  |  | 
 | n260 | 8.0 |  | 12.0
 | n261 | 8.0 | 10.5 | 9.0
  Way-forward for RAN4#99e:
    For n262, it is further discussed whether the same gain drop as EIRP is specified for EIS.

## Slide 6: Sub-topic 3-1: Side conditions for n262 (PC3)
Way-forward for RAN4#99e:
  Confirm the following side conditions for SSB and CSI-RS as proposed in R4-2104889.
    Minimum SSB_RP = -88.5 [dBm/SCSSSB]
    Minimum CSI-RS_RP conditions = -88.5 [dBm/SCSSSB]