## Slide 1: 3GPP TSG-RAN WG4 Meeting # 98-bis-e Electronic Meeting, 12 – 20 April, 2021
ZTE, [Apple], …
WF on new CA BW class denotation and definition
R4-2105396

## Slide 2: Background(1/4)
In RAN#91-e meeting, an objective of introducing new FR2 CA BW classes and related Rx requirements to support of contiguous downlink aggregated channel BW up to 1600MHz has been approved and included in the revised WID on NR RF enhancements for FR2 [1].
Considering that 16 CA BW classes have already been introduced for intra-band contiguous CA in TS 38.101-2, the remaining letters for CA BW class will soon be used up. How to denote the increasing CA BW classes have been discussed during RAN4#98-bis-e meeting [2,3,4].
Some companies raised concerns on two-letter format, since it may cause some confusions. For example, double letter has already been used for intra-band contiguous EN-DC notation. And some special letters of combination such as “CA”, “DC” may be confused with “CA_”, “DC_” , etc.

## Slide 3: Background(2/4)
In [2], the following rules for CA BW classes have been proposed.
  Prefer to use the symbol of Capital letter + lowercase letter due to the rest of letters are not enough
  Consider below some ordering rules to name the new bandwidth classes for intra-band contiguous CA:
      Option 1: It could first use the remaining letters, then use Aa, Ab in order when the letters are run out.
      Option 2: Reserve the remaining letters which could be used to extend new bandwidth classes or new fallback groups in the future, then apply below methods naming the new bandwidth classes:
        Option 2a: Using Aa, Ab, Ac names the new bandwidth classes directly.
        Option 2b: Using the last name of each fallback group + lowercase letter names the new bandwidth classes, i.e., Fa, Fb, Fc and Ma, Mb, Mc.
        Option 2c: Using the last name of each fallback group + lowercase letter names the new bandwidth classes, lowercase letter coming from the same group represents the increment of the number of CCs based on the number represented by the last letter. For example, Fa means 4+1 CCs, Fd means 4+2 CCs, Ma means 8+1 CCs, Mg means 8+2 CCs, and so on.

## Slide 4: Background(3/4)
In [3], it is proposed to continue using the next available capital letter in English alphabets for the new FR2 CA BW classes before they are run out.

## Slide 5: Background(4/4)
In [4], two capital letters are chosen to denote the new NR CA bandwidth class for FR2.

## Slide 6: Way Forward (I)
For new CA BW class denotation in FR2
  Companies are encouraged to share their views on the following options in the next meeting.
    Option 1. Use two letter format.
    Option 2. Stay with single letter and solve the 26 letter limitation when needed.
    Option 3. Use letter + number format
  Evaluate Pros and Cons for each option.
  Note that any other options are not precluded.

## Slide 7: Way Forward (II)
For new CA BW class definition in FR2
  Four new CA BW classes in fallback group 2 will be introduced to support aggregated channel BW up to 1600 MHz.
    For aggregated channel BW range, the following two options are considered which will be down-selected in next RAN4 meeting.
      Option 1: (R4-2107266)
      Option 2: (R4-2106907)
CA BW Class | Aggregated Channel BW | Number of CC | Fallback Group
 | 800 MHz < BWChannel_CA ≤ 1000 MHz | 5 | 2
 | 1000 MHz < BWChannel_CA ≤ 1200 MHz | 6 | 2
 | 1200 MHz < BWChannel_CA ≤ 1400 MHz | 7 | 2
 | 1400 MHz < BWChannel_CA ≤ 1600 MHz | 8 | 2
CA BW Class | Aggregated Channel BW | Number of CC | Fallback Group
 | 750 MHz ≤ BWChannel_CA ≤ 1000 MHz | 5 | 2
 | 950 MHz ≤ BWChannel_CA ≤ 1200 MHz | 6 | 2
 | 1150 MHz ≤ BWChannel_CA ≤ 1400 MHz | 7 | 2
 | 1350 MHz ≤ BWChannel_CA ≤ 1600 MHz | 8 | 2

## Slide 8: Reference
[1] RP-210914, Revised WID Further enhancements of NR RF requirements for frequency range 2 (FR2), Nokia, Nokia Shanghai Bell.
[2] R4-2105101, Introducing new bandwidth classes for FR2 CA, Xiaomi.
[3] R4-2106907, New FR2 CA BW classes, Apple
[4] R4-2107266, On FR2 CA bandwidth class, Huawei, HiSilicon