## Slide 1: WF on A-MPR for PC2 n39
Huawei, HiSilicon, Apple, Nokia
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, 19 – 27 May 2021
Agenda Item: 8.34
R4-2107738

## Slide 2: Background
In support of PC2 for n39, the A-MPR for n39 NS_50 needs to be updated.
For CBW <= 20MHz, additional power back-off may also be needed for protecting the same frequency ranges as in NS_50.
References:
  R4-2109259, PC2 A-MPR for NS_50 on n39, Nokia, Nokia Shanghai Bell
  R4-2111014, Considerations for PC2 n39 and A-MPR results, Apple
  R4-2107828, AMPR for n39 NS_50 PC2, Huawei, Hisilicon

## Slide 3: Way Forward for CBW > 20MHz
The A-MPR regions and values in the tables on the right are the merged results based on the contributions submitted to this meeting.
Interested companies can bring new simulation results and proposals in future meetings.
The tables shown serve as the starting point for further discussion.
Companies are encouraged to perform further check and RAN4 is expected to decide the A-MPR in the next meeting.
Channel Bandwidth (MHz) | RBstart*12*SCS (MHz) | LCRB*12*SCS (MHz) | A-MPR
25 MHz | ≤ LCRB*12*SCS – 5 | > 5 | A7
 | ≤ 6.3 | ≤ 1.44 | A8
 | > 8.28 | > max (21.6 – RBstart*12*SCS, 0), <RBstart*12*SCS+5 | A4
 | >1.8, ≤6.12 | > 1.44, ≤ 3.6 | A9
 | > LCRB *12*SCS – 5, ≤ 5.04 | > 1.44 | A6
30 MHz | ≤ LCRB*12*SCS – 5 | >5 | A7
 | ≤ 7.56 | ≤ 1.44 | A8
 | >1.8, ≤7.56 | > 1.44, ≤ 3.6 | A9
 | ≤ 1.8 | >1.44, <RBstart*12*SCS+5 | A6
 | > 10.8 | > max (26.64 – RBstart*12*SCS, 0), <RBstart*12*SCS+5 | A4
40 MHz | ≤ 4.32 | > 0 | A1
 | > 4.32, ≤ 12.96 | ≤ 10.8 | A3
 | > 4.32, ≤ 18 | > 10.8 | A2
 | > 18, ≤ 31.68 | > max (31.68 – RBstart*12*SCS, 0) | A6
 | > 31.68 | > 0 | A1
NOTE 1: The A-MPR values are specified in Table 6.2.3.19-2. |  |  | 
Modulation/Waveform |  | A1 (dB) | A2 (dB) | A3 (dB) | A4 (dB) | A6 (dB) | A7 (dB) | A8 (dB) | A9 (dB)
 |  | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner
DFT-s-OFDM | Pi/2 BPSK | ≤ [11.5] | ≤ [8] | ≤ [4] | ≤ [2.5] | ≤ [2.5] | ≤[4.5] | ≤ [2.5] | ≤ [1]
 | QPSK | ≤ [11.5] | ≤ [8] | ≤ [4] | ≤ [2.5] | ≤ [2.5] | ≤ [5.5] | ≤ [2.5] | ≤ [1]
 | 16 QAM | ≤ [11.5] | ≤ [8] | ≤ [4] | ≤ [2.5] | ≤ [2.5] | ≤ [5.5] | ≤ [3] | ≤ [1.5]
 | 64 QAM | ≤ [11.5] | ≤ [8] | ≤ [4] |  |  | ≤ [5.5] |  | 
 | 256 QAM | ≤ [11.5] | ≤ [8] |  |  |  | ≤ [5.5] |  | 
CP-OFDM | QPSK | ≤ [12.5] | ≤ [9] | ≤ [5.5] | ≤ [4] | ≤ [4.0] | ≤ [7] | [2] | [2]
 | 16 QAM | ≤ [12.5] | ≤ [9] | ≤ [5.5] | ≤ [4] | ≤ [4.0] | ≤ [7] |  | 
 | 64 QAM | ≤ [12.5] | ≤ [9] | ≤ [5.5] | ≤ [4] |  | ≤ [7] |  | 
 | 256 QAM | ≤ [12.5] | ≤ [9] |  |  |  | ≤ [7] |  | 

## Slide 4: Way Forward for CBW <= 20MHz
FFS whether to modify the ASE requirements signalled by NS_50 to include CBW <= 20MHz
  If needed, define A-MPR regions/values for CBW <= 20MHz
Companies are encouraged to bring simulation results or other justifications together with proposals.