## Slide 1: WF on A-MPR revision for both NS_33 and NS_52
Huawei, HiSilicon, LGE
3GPP TSG-RAN WG4#99-e R4-2107745
Electronic Meeting, May 19 – 27, 2021

## Slide 2: Background
Some issues for NS_33 and NS_52 are identified based on the contribution [1].
  For NS_33, as RAN1 update the RB allocation rules, the allowed RB allocation can be found as below. The AMPR requirements for missing allocation (12, 24, 36 and 48) should be added in RAN4.
  For NS_52, AMPR value for region 1 is too stringent to meet the ASEM requirement. Furthermore, the specified emissions limits in the latest FCC regulation [2] are not what RAN4 specified in clause 6.5E.2.3.2 from TS 38.101-1.
In this meeting, RAN4 need to further discuss this issue and how to address them.

## Slide 3: WF for NS_33
Proposal 1: It’s proposed to update the AMPR requirements for NS_33 PSSCH/PSCCH (at Fc =5860MHz) as below.
Carrier frequency [MHz] | Resources Blocks (LCRB) | Start Resource Block | A-MPRBase (dB) |  | 
 |  |  | QPSK/16QAM | 64QAM | 256QAM
5860 | ≥ 10 and ≤ 15 | 0 | ≤ 24 |  | 
 |  | ≥ 1 and ≤ 3 | ≤19 |  | 
 | ≥ 10 and ≤ 15 | ≥ 26 and ≤ 38 | ≤6 |  | 
 | ≥ 10 and ≤ 15 | ≥ > 38 | 7≤6 |  | 
 | ≥ 10 and ≤ 20 | ≥ 12 and ≤ 14 | ≤11 |  | 
 |  | ≥ 15 and ≤ 19 | ≤9.5 |  | 
 |  | ≥ 20 and ≤ 25 | ≤8.0 |  | 
 | > 15 and < 25 | ≥ 25 | ≤ 8 |  | 
 | ≥ 10 and ≤ < 340 | ≥ 4 and ≤7 | ≤ 16 |  | 
 |  | ≥ 8 and ≤ 11 | ≤ 13.5 |  | 
 | ≥ 20 and ≤ <340 | ≥ 0 and ≤ 3 | ≤ 22 |  | 
 | ≥ 25 and <340 | ≥ 16 and ≤ 21 | ≤ 9.5 |  | 
 |  | ≥ 22 and ≤ 27 | ≤ 8.0 |  | 
 | ≥ 245 and ≤ 40 | ≥ 12 and ≤ 15 | ≤ 12 |  | 
 | ≥ 40 and ≤ 45 | 0 and 1 | ≤ 19 |  | 
 |  | ≥ 2 and ≤ 5 | ≤ 16 |  | 
 |  | ≥ 6 and ≤ 11 | ≤ 13.5 |  | 
 | ≥ 50>45 | ≥ 0 | ≤ 16 |  | 
NOTE 1: A-MPRstep =1.2 dB is applied for RBstart 0 and 1 and A-MPRstep =0.7 dB is applied for all other RBstart NOTE 2: Applicable for Channel Bandwidth = 10 MHz |  |  |  |  | 

## Slide 4: WF for NS_52
Revise the current AMPR value as 15dB for NS_52 region 1 and analyze the status of FCC regulation about the use of the 5.850-5.925 GHz Band until Aug. RAN4 meeting.

## Slide 5: References
# | TDoc | Title | Source
1 | R4-2110400 | Discussion on Rel-16 NR V2X AMPR value for both NS_33 and NS_52 | Huawei, HiSilicon
2 |  | https://www.federalregister.gov/documents/2021/05/03/2021-08801/use-of-the-5850-5925-ghz-band | 
3 |  |  |