## Slide 1: WF on simultaneous Rx/Tx for the inter-band combinations having more than two bands
Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May 19-27, 2021
R4-2107843

## Slide 2: Background
Inter-band CA combinations with more than 2 bands can contain multiple band pairs with different simultaneous Rx-Tx capabilities
  E.g. Band combination A+B+C,
    A+B+C does not support simultaneous Rx/Tx
    A+B and A+C supports simultaneous Rx-Tx but B+C does not support simultaneous Rx-Tx
Current CA capability includes a single bit per combination for simultaneous Rx-Tx support
  Capability applies across all band pairs within a band combination
  It may not be possible to signal the simultaneous Rx-Tx capability per band pair within a band combination with more than 2 bands
Network should be aware of the exact UE capabilities for scheduling decisions

## Slide 3: Way Forward
CA capability signaling should be able to indicate support of simultaneous Rx-Tx for all band pairs within a higher order CA combination
Send an LS to RAN2 to inform them about this RAN4 agreement
  Signaling details (whether new signaling is needed or existing signaling can be reused) should be left to RAN2