## Slide 1: WF on default DC location and offset signalling
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting # 99-e R4-2107858
Electronic Meeting, May. 19-27, 2021

## Slide 2: Background
This WF is generated based on each of the topics belonging to topic #2 DC location in the below t-doc.
  R4-2107665: Email discussion summary for [99-e][139] NR_RF_FR2_req_enh2_Part_3
    This is the summary for the 1st round during the meeting
  Note that “2-x” in this WF refers to a corresponding sub-topic in the references.

## Slide 3: Factors affecting and exception applicability
Factors(topic 2-1/2-4)
  For FR1, UL configured or activated outermost CCs or BWPs
  For FR2, UL or DL configured or activated outermost CCs or BWPs
  For both FR1 and FR2, some UEs may further optimize the DC location based on inner CCs or BWPs if necessary
DC location when the exception needs to be granted(topic 2-2).
  For FR1, anywhere between the configured outermost UL CCs for intra-band NC UL CA whose signalling is absent for dualPA-Architecture IE
  For FR2, any configured UL or DL CCs
    The above holds unless a necessity of including a gap in-between configured CCs is confirmed.

## Slide 4: Handling of dualPA capability (topic 2-5)
No more discussion is necessary
  Current RAN2 specification has # of PAs information, i.e., secondPA-TxDirectCurrent-r16, dedicated to UL DC location reporting is sent within UplinkTxDirectCurrentTwoCarrierList IE apart from dualPA-Architecture for CA/DC configurations
    Where secondPA-TxDirectCurrent-r16 is defined as “The uplink Tx Direct Current location used by the UE with the second PA for the UEs which support dual PA for this uplink carrier aggregation” in TS38.331.

## Slide 5: Signaling(topic 2-3)
Way of indication of DC location
  Option 1: Defined as offset from the default DC location
    The definition of the default is FFS
    Encouraged to study if the outermost CCs or BWPs aspect can be merged or not
    Other ideas are not precluded.
  Option 2:Function of outermost CC or BWP
      Detail function definition is FFS
  Other solutions are not precluded
Signalling details
  Leave the below details to RAN2
    How often and/or how quickly the DC location needs to be signalled and its timing