## Slide 1: WF on Waveform configuration, parameters for link simulations and agreements
Qualcomm, ...
3GPP TSG-RAN WG4#99-e Meeting R4-210XXXX
Electronic Meeting, 19th Jan –27th May, 2021

## Slide 2: Background
In RAN#91-e a new SID was approved to investigate ways to increase the UL power using shaped pi/2 BPSK waveforms [1].
To obtain results that can be compared across companies there should be general agreement on things such as waveform configuration, link simulation parameters, PA configuration, target output power and EVM equalizer spectral flatness

## Slide 3: Issue 1-1-1: Waveform configuration
R4-2109749 and R4-2109371 submitted to RAN4#99-e presented waveform parameters that can be used to analyze candidate PAs .
Recommended parameter list in table 1 is derived by merging tables from contributions referenced above
Recommended WF based on company inputs
  Use parameter list given in table1
Parameter | Value
Pulse shaping filter | Filter configuration conforms to 38.101-1 Rel-16
Waveform | DFTS OFDM with pi/2 BPSK with Rel-16 DMRS
PRB/LCRB | Full sweep of all possible combinations of RB starting locations and RB lengths
# of DMRS symbols/slot | 2
# of data symbols/slot | 12
BW | [10, 15, 20, 30, 40, 50, 60, 80, 90, 100] MHz
SCS | [15, 30, 60] kHz 30 kHz mandatory 15, 50 kHz optional
Table 1: Recommended Parameter list
Notes: Company comments
Nokia: Try to reduce the number of cases to be simulated
  SCS: 30 kHz mandatory, [15 60] kHz optional

## Slide 4: Issue 1-2-1 Pulse shaping filter characteristics
Comments from 1st round can be grouped into options as follows:
  Companies that wanted to use 2 tap filter as per 38.101-1, section 6.4.2.4.1 (IITH, IITM, CEWIT, Reliance Jio, Tejas Networks)
  Companies that wanted to use 2 & 3 tap filters as per 38.101-1, section 6.4.2.4.1 (QCOM, Nokia)
  Companies that wanted to use general filters defined as per 38.101-1, section 6.4.2.4.1 (Huawei, Nokia)
Recommended WF based on company inputs
  Initial study to focus on filter configurations defined as per 38.101-1, section 6.4.2.4.1
  Interested companies can do subsequent studies that focus on other filter configurations
Notes:   Company inputs:
  vIITH, IITM, CEWIT, Reliance Jio, Tejas Networks Proposed Modification:
    Use any filter configuration that conforms to the current 38.101-1 specification for the current phase of study till we reach an agreement on the exact filter to be used
  Nokia: We propose to use general filters defined as per 38.101-1, section 6.4.2.4.1

## Slide 5: 1-3-1 Parameters for Link simulations
Parameter | Value
Pulse shaping filter | Filter configuration conforms to 38.101-1
Channel model | TDL-C300ns, TDL-A30, TDL-D30
MCS Code rate | 0 1/8, 1/4, 1/3, 1/2, 2/3
Waveform | DFTS OFDM with pi/2 BPSK filtered by same filter as for Rel-16 DMRS
# of DMRS symbols/slot | 2
# of data symbols/slot | 12
# of RBs | 2, 4, 6, 8, 10 [2, 4, 8, 16, 64]
TX/RX configuration | 1TX/4RX
BW | 100 MHz
UE speed | 3 km/h
SCS | 30 kHz
HARQ configuration | No retransmissions
R4-2109749 and R4-2109371 submitted to RAN4#99-e presented link level simulation parameters that can be used to evaluate candidate filters .
Recommended parameter list in table 1 is derived by merging tables from contributions referenced above
Recommended WF based on company inputs
  Use parameter list given in table2
Table 2: Recommended Parameter list
Notes: Company inputs
IITH, IITM, CEWIT, Reliance Jio, Tejas Networks Proposed Modification:
  We should only stick to MCS tables already defined in NR for pi2BPSK. At the present time we need not introduce new MCS and therefore new code rates should not be introduced into the study.
Nokia:
  For channel model, we think that two different type of models is enough  We propose to use TDL-C300ns, TDL-A30. TDL-D30 could be defined as optional
  For # of BW we propose to cover also wider BWs. Based on that we propose the following set
    [2, 4, 8, 16, 32, 64] RBs

## Slide 6: 1-4-1 Target output power
Comments from 1st round can be grouped as follows:
  Companies that wanted to limit study to PC2 (Huawei)
  Companies that wanted to make study of PC2 mandatory and higher powers optional (Nokia)
  Companies that wanted to study PC2 first and then discuss higher powers (Apple)
  Companies that wanted to study higher output powers up to 32 dBm (QCOM, IITH, IITM, CEWIT, Reliance Jio, Tejas Networks)
Options
  Start study with PC2 and re-evaluate higher output power targets later
  Study output power up to 32 dBm
  Each company picks between options 1 & 2
Recommended WF based on company inputs
Initial study to focus on PC2 performance
Interested companies can subsequently study higher output powers
Notes: Company inputs
IITH, IITM, CEWIT, Reliance Jio, Tejas Networks Proposed Modification:
  First we remark that CP-OFDM already meets PC2 requirements. There is no benefit in studying pi2BPSK performance for the current PC2 spec which is already defined. The RAN plenary has clearly mandated to study the potential of pi2BPSK in maximizing the transmit power. The initial exercise itself should start with higher power levels and every company can report what is the power level they can achieve. Therefore we take 32 dBm as a target for this study.
Nokia: for comparison purposes all companies should at least provide results for Option1

## Slide 7: 1-4-2 PA architecture
Comments from 1st round can be grouped as follows:
  Study only 1 PA designs (Huawei, Nokia, Apple)
  Study multi-PA designs after evaluating single PA designs (Apple)
  Study 1 PA and multi-PA designs (QCOM, IITH, IITM, CEWIT, Reliance Jio, Tejas Networks)
Options
  Study only 1 PA designs
  Study multi-PA designs
  Each company picks between options 1 & 2
Recommended WF based on company inputs
All companies to initially study 1 PA designs
Interested companies can subsequently study multi-PA designs
Notes: Company inputs
IITH, IITM, CEWIT, Reliance Jio, Tejas Networks Proposed Modification:
  We can study multi-PA designs after evaluating single PA designs. This is inline with Apple’s suggestion.
Nokia: for comparison purposes all companies should at least provide results for Option1

## Slide 8: 1-5-1 EVM equalizer spectral requirements
No change required per agreement on 1-2-1
  For initial studies where filters conforming to 38.101-1, section 6.4.2.4.1 are analyzed current EVM equalizer spectral requirements remain unchanged
  Subsequent studies using other filter configurations modifications to EVM equalizer spectral requirements can be considered
Notes: Company inputs
IITH, IITM, CEWIT, Reliance Jio, Tejas Networks Proposed Modification:
    Use the EVM equalizer spectral requirements that conforms to the current 38.101-1 specification for the current phase of study till we reach an agreement on the exact filter to be used and thereby redefine the EVM equalizer if required.
Nokia: agree with the Recommended WF

## Slide 9: References
[1] RP-210910, New SID: Optimizations of pi/2 BPSK uplink power in NR, RAN#91e, Mar. 2021