## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e R4-2108647 Electronic Meeting, May. 19 – 27, 2021
CATT…
WF on NTN RF aspects

## Slide 2: Frequency error
RAN4#98-bis-e agreement: The mean value of basic measurements of UE modulated carrier frequency shall be accurate to within ±0.1 ppm observed over a period of 1ms of cumulated measurement intervals compared to the carrier frequency received from the gNB.
Note: The gNB refers to RAN3 NTN architecture.
The additional frequency error introduced by NTN payload, feeder link Doppler compensation error and NTN-Gateway is negligible.

## Slide 3: Network side
Take the RF requirement in 38.104 as the starting point for NTN network side.
Same temperature operating condition is assumed for [NTN BS] as that for TN BS
  Assuming the temperature control system in satellite can ensure similar operating condition for NTN payload to that for TN BS
Companies are invited to contribute on the following points in RAN4#100e meeting
  The following figure might be used as starting point for further discussion.
  Which [NTN BS] types is the baseline for R17 specification.
    Candidates include, BS type 1-C, BS type 1-H, BS type 1-O. Additional prefix for [NTN BS] type is FFS.
  How to define [NTN BS] classes?
    Further discuss whether and how to differentiate into different [NTN BS] classes and the corresponding criteria.
  Whether and how to consider EVM distortion for NTN intra-gNB (refer to RAN3 architecture): FFS

## Slide 4
[1] R4-2108701, Email discussion summary for [99-e][314] NTN_Solutions_Part3, Moderator (CATT)