## Slide 1: WF on NeedForGap measurements
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021
Agenda item: 5.1.7.3
Document for: Approval
R4-2108220

## Slide 2: Background
In Rel-16 TEI, RAN2 has introduced NeedForGapsInfoNR capability for NR measurement as follow.
The related requirements for NeedForGap are not defined in Rel-16.
NeedForGapsInfoNR information element -- ASN1START -- TAG-NeedForGapsInfoNR-START NeedForGapsInfoNR-r16 ::= SEQUENCE { intraFreq-needForGap-r16 NeedForGapsIntraFreqlist-r16, interFreq-needForGap-r16 NeedForGapsBandlistNR-r16 } NeedForGapsIntraFreqlist-r16 ::= SEQUENCE (SIZE (1.. maxNrofServingCells)) OF NeedForGapsIntraFreq-r16 NeedForGapsBandlistNR-r16 ::= SEQUENCE (SIZE (1..maxBands)) OF NeedForGapsNR-r16 NeedForGapsIntraFreq-r16 ::= SEQUENCE { servCellId-r16 ServCellIndex, gapIndicationIntra-r16 ENUMERATED {gap, no-gap} } NeedForGapsNR-r16 ::= SEQUENCE { bandNR-r16 FreqBandIndicatorNR, gapIndication-r16 ENUMERATED {gap, no-gap} } -- TAG-NeedForGapsInfoNR-STOP -- ASN1STOP

## Slide 3: Agreements
‘NeedForGap’ in Rel-16 is only applied in NR SA.

## Slide 4: Work Scope
Potential new objective - NeedForGap for NR-SA only
  Limited to SSB based measurements configured via measurement objects
  Study whether the additional interruption is allowed when UE reporting ‘no gap’
    Further define the interruption length, occasion and ratio, if the interruption is allowed
  Study the related requirements, such as CSSF, measurement period, scheduling restriction etc.
  RAN4 to further consider the relation with other UE capabilities, such as NCSG etc.
  Decide if it is feasible that the UE requirements are defined in R16 or release independent from Rel-16.

## Slide 5: The definition of ‘no gap’
How to understand ‘no gap’ for UE capable of ‘NeedForGap’ and reporting ‘no gap’ in intra-frequency measurements?
  Option 1: No gap and no interruption.
  Option 2: No gap but limited interruption.
How to understand ‘no gap’ for UE capable of ‘NeedForGap’ and reporting ‘no gap’ in inter-frequency measurements?
  Option 1: No gap and no interruption.
  Option 2: No gap but limited interruption.

## Slide 6: Interruption
If interruption is allowed for UE capable of ‘NeedForGap’ and reporting ‘no gap’ in measurements,
  How long about each interruption length in ‘NeedForGap’ measurements?
    Option 1: 0.5 ms for FR1, 0.25ms for FR2
    Option 2: 1ms
    Option 3: other values
  FFS the interruption occasions
  FFS the overall interruption ratio(missing ACK/NACK) in ‘NeedForGap’ measurements

## Slide 7: Measurement requirements
FFS CSSF of measurements with ‘no gap’ in ‘NeedForGap’ reporting
FFS measurement period of ‘NeedForGap’ measurements
FFS scheduling restriction of ‘NeedForGap’ measurements

## Slide 8: Relation with ‘NCSG’
How to consider the relation of ‘NeedForGap’ and ‘NCSG’ in Rel-17?
  Signaling
    Note 1: Can we agree to follow the agreements in Rel-17 NCSG and skip this discussion in ‘NeedForGap’?
    Note 2: This issue is also discussing in Rel-17 NCSG WI.
  FFS UE behaviour
FFS to avoid the contradiction or double effort to discuss ‘NeedForGap’ in Rel-16 TEI with the on-going ‘NCSG’ in Rel-17.

## Slide 9: Release Independency
Signaling for ‘NeedForGap’ has defined in Rel-16 (TS 38.331).
FFS: If measurement requirements for ‘NeedForGap’ are defined in Rel-16
If measurement requirements for ‘NeedForGap’ are defined in Rel-17, then whether the measurement requirements will be release independent from:
  Option 1: Rel-16
  Option 2: Rel-17