## Slide 1: WF on further RRM enhancement for NR and MR-DC – HO with PSCell
vivo, …
R4-2108344
3GPP TSG-RAN4 Meeting #99-e
Electronic Meeting, 19th – 27th May, 2021
Agenda item: 9.9.2.2
Document for: Approval

## Slide 2: Agreements in the 1st round
Tprocessing includes both software processing time and RF warm up time.
It depends on RAN2 reply whether RACH processing can be performed in parallel or not and it can be further discussed
Considering the reply LS from RAN2, RRC processing delay for HO with PSCell is:
  NR SA to EN-DC : 50ms
  EN-DC to EN-DC: 20ms
  NE-DC to NE-DC: 16ms
  NR-DC to NR-DC: 16ms
  Note: RRC processing delay is defined in RAN2 specification.
PCC could be scheduled for UE when Pcell HO is completed but PSCell addition is not completed

## Slide 3: Agreements in the 2nd round
PCell HO and PSCell addition, except RACH procedure, are performed in parallel for at least some of procedures
  FFS condition of parallel processing in Issue 2-2-1a

## Slide 4: Open issues – sub-topic 2-1
Issue 2-1-1: Scenarios for RRM requirement of HO with PSCell
  Option 1 (CMCC, CATT, OPPO, Ericsson, Qualcomm, Intel, Docomo, NEC, vivo, Nokia)
    RAN4 concludes that RRM requirements are needed for the additional scenarios for HO with PSCell. It is up to RAN plenary decision whether to extend the scope the WID.
      from NR SA to NE-DC (newly added)
      from NR SA to NR-DC (newly added)
      from LTE SA to EN-DC (newly added)
  Option 2 (Apple, Xiaomi, MTK)
    The extension of WI scope should be discussed in RAN plenary.

## Slide 5: Open issues – sub-topic 2-1
Issue 2-1-2: NR-DC and NE-DC mode in HO with PSCell
  Option 1(CATT, Qualcomm, Huawei): In R17 RAN4 only considers:
    FR1+FR2 NR-DC for HO with PSCell from NR-DC to NR-DC,
    FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
  Option 2 (CMCC, Apple, Xiaomi, Ericsson, Huawei, Intel, NEC, vivo, Nokia):
    FR1+FR2 NR-DC and FR1+FR1 NR-DC for HO with PSCell from NR-DC to NR-DC
      Note: the baseline PSCell addition requirement for FR1+FR1 NR-DC would be discussed in TEI16.
    FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC.
  Recommended WF (OPPO, Docomo, MTK)
    FR1+FR2 NR-DC for HO with PSCell from NR-DC to NR-DC is supported.
    FR1+LTE NE-DC for HO with PSCell from NE-DC to NE-DC is supported.
    FR1+FR1 NR-DC for HO with PSCell from NR-DC to NR-DC is FFS
      the baseline PSCell addition requirement for FR1+FR1 NR-DC would be discussed in TEI16.
    FR2+LTE NE-DC for HO with PSCell from NE-DC to NE-DC is FFS.

## Slide 6: Open issues – sub-topic 2-1
Issue 2-1-2a: Requirements for Rel-16 FR1+FR1 NR-DC
  Option 1:
    Limited set of RRM requirements, i.e., PSCell addition requirements, are specified
      The requirements are discussed in TEI16.
  Option 2:
    Full set of RRM requirements:
      Note: The requirements are specified under what agenda/WI?

## Slide 7: Open issues – sub-topic 2-2
Issue 2-2-1a: Condition of parallel processing
  Option 1:
    If SMTC of target unknown PSCell is configured in targetcellSMTC-SCG-r16, sequential processing shall be assumed; otherwise, parallel processing shall be assumed
  Option 2:
    Parallel processing shall always be assumed.
  Note: other options are not precluded
Issue 2-2-1b: Whether requirements for sequential processing are needed if parallel processing is only possible under certain condition
  Option 1: yes
  Option 2: no
    Option 2a: no, but the applicability condition shall be clarified in the spec (e.g., no requirement applies when such configuration happens).

## Slide 8: Open issues – sub-topic 2-2
Issue 2-2-2: Parallel processing for HO with PSCell
  Option 1a (QC, Nokia, ZTE, CATT, Ericsson, vivo, Apple, OPPO, Docomo, MTK, NEC):
    PCell HO and PSCell addition, without considering RA procedures and Tprocessing, are performed in parallel independently.
  Option 1b (Intel):
    Tsearch, Tmargin, T∆ can be processed in parallel for both Pcell HO and PSCell addition. Tsearch is the time required to search the target cell. T∆ is time for fine time tracking and acquiring full timing information of the target cell. Tmargin is time for SSB post-processing.
  Option 1c (Huawei):
    Based on the parallel processing assumption
    Whether to consider additional delay for searching procedure depends on whether to include FR1+FR1 NR-DC case
  Option 2b (MTK, Intel):
    RAN4 to specify the delay requirement for HO with PSCell based on the assumption that some of procedures should be able to be performed in parallel.
    FFS what kinds of components in the overall delay requirement, e.g., Tprocessing, will have dependency between Pcell and PSCell.

## Slide 9: Open issues – sub-topic 2-2
Issue 2-2-3: UE SW processing and RF warm-up(if needed) time for HO with PSCell
  Option 1 (CATT): The value of processing time of handover and the PSCell addition can be reused separately. And Tprocessing for HO with PSCell including UE SW processing and RF warm-up time should be the maximum of the processing time of handover and the processing time of the PSCell addition.
  Option 3 (Apple, Xiaomi):
    For sequential processing for HO with PSCell, the total UE processing time for HO with PSCell is the sum of UE processing timing of HO and UE processing timing of PSCell addition.
    For parallel processing for HO with PSCell, the total UE processing time for HO with PSCell could be the maximum one between UE processing timing of HO and UE processing timing of PSCell addition
    the UE processing time for HO with PSCell is:
UE processing margin (Tprocessing) | Target Pcell and PSCell is in the same FR as old serving cell | Target Pcell and/or target PSCell is in the different FR from old serving cell
Sequential processing | 40ms | 60ms
Parallel processing | 20ms | 40ms

## Slide 10: Open issues – sub-topic 2-2
Issue 2-2-3: UE SW processing and RF warm-up(if needed) time for HO with PSCell
  Option 4 (Huawei): UE processing time is the maximum value of Pcell HO and PSCell addition, and FFS whether to extend the processing time for NR SA to EN-DC and the value if needed.
  Option 5 (Ericsson): For software processing for PSCell, the following values are to be used.
    0ms, when source and target PSCells are the same same NR or LTE cell,
    20ms, when source and target PSCells are different NR cells in same FR,
    40ms, when source and target PSCells are different NR cells in different FRs,
    [40ms], when there is no source PSCell i.e. when it is a matter of PSCell addition.
  Option 6 (Nokia):
    The UE processing time in HO with PSCell can be 20ms if source & target Pcell is in same frequency range and source & target PSCell in same frequency range, 40ms otherwise.
    No additional RF retuning interruption should be defined during HO with PSCell.
  Option 8 (MTK, OPPO): The overall Tprocessing for HO with PSCell should be max(Tprocessing for PCell HO, Tprocessing for PSCell addition) +10ms
  Option 10 (Qualcomm, vivo, MTK, NEC):
    Extending the UE processing time for NRSA to EN-DC joint handover by [FFS]ms and [FFS] can be 10ms as the starting point, i.e. Tprocessing = [30]ms.
    For NRDC to NRDC, the UE processing time to be 20ms without FR mode switch on PSCell; otherwise, the UE processing time shall be 40ms as the legacy PSCell change requirement.

## Slide 11: Open issues – sub-topic 2-2
Issue 2-2-5: Ending point of the delay requirement for HO with PSCell
  Option 1 (CATT, CMCC, Ericsson, Intel, NEC, vivo, Nokia): Waiting for RAN2 response for order of random access carried out towards PCell and PSCell.
  Option 2 (Xiaomi, OPPO, DoCoMo, vivo): The ending point of HO with PSCell is the timing when UE is capable to transmit PRACH preamble towards target PSCell.
  Option 3 (Apple): the ending point of the delay requirement for HO with PSCell is:
    if sequential processing is used, the timing when UE shall be capable to transmit PRACH preamble towards target PSCell
    if the parallel processing is used, the later timing between “timing when UE shall be capable to transmit PRACH preamble towards target Pcell” and “the timing when UE shall be capable to transmit PRACH preamble towards target PSCell”
  Option 4 (Huawei, QC, MTK):
    Define delay requirements for HO and PSCell addition/change separately with the ending points defined as Pcell PRACH and PSCell PRACH respectively. No need to define overall delay requirement.

## Slide 12: Open issues – sub-topic 2-2
Issue 2-2-6: Optimisation for the case when PSCell is not changed during HO with PSCell
  Option 1 (ZTE, CATT, Apple, OPPO, Ericsson, vivo): For UE which is already configured with DC, the UE’s behavior is same when the configured PSCell is same as the original one or not.
  Option 2 (Nokia): If the target PSCell is same as source PSCell, UE should have known the timing, then it is no need for fine time tracking for target PSCell.

## Slide 13: Open issues – sub-topic 2-2
Issue 2-2-8: Delay requirement design if parallel processing is assumed
  Option 1 (CATT):
    If parallel processing is assumed and having order limit of PRACH, the delay requirement can be defined as:
      Delay = RRC processing time + max(Tprocessing for handove, Tprocessing for addition) + max(Tinterrupt –Tprocessing for handove , Tconfig_PSCell – TRRC_delay –Tprocessing for addition–TPSCell_ DU) + TPSCell_ DU
    If parallel processing is assumed and having not order limit of PRACH, the delay requirement can be defined as:
      Delay = RRC processing time + max(Tinterrupt , Tconfig_PSCell – TRRC_delay)
  Option 2 (CMCC):
    Delay for HO with PSCell is maximum (PSCell addition delay, HO delay)
      PSCell addition delay= TRRC_delay + Tprocessing + Tsearch + T∆ + TPSCell_ DU + 2 ms
      HO delay = TRRC_delay +Tinterrupt = TRRC_delay +Tsearch + TIU + Tprocessing + T∆ + Tmargin ms
  Option 3 (Nokia):
    The delay requirements for HO with PSCell can be described as: DHO_with_PSCell = TRRC_delay + Tsearch + Tprocessing + T∆ + Tmargin +TFFS. Where TFFS is the delay in acquiring the first available PRACH occasion in the target cells.
      The cell searching time in HO with PSCell can be the maximum searching time of target PCell and PSCell.
Delay requirements for parallel processing are discussed after there is conclusion on the other issues in sub-topic 2-2.

## Slide 14: Open issues – sub-topic 2-2
Issue 2-2-9: Delay requirement design if sequential processing is assumed
  Option 1 (CATT):
    If sequential processing is assumed, the delay requirement can be defined as:
      Delay = RRC processing time + max(Tprocessing for handove, Tprocessing for addition) + (Tinterrupt –Tprocessing for handove) + (Tconfig_PSCell – TRRC_delay –Tprocessing for addition)
  Option 2:
    Other options are not precluded.
Delay requirements for sequential processing are discussed after there is conclusion on other issues in sub-topic 2-2.

## Slide 15: Open issues – sub-topic 2-3
Issue 2-3-2: Interruption requirement for HO with PSCell
  Option 1 (CATT, Xiaomi, Huawei, vivo, Docomo): No interruption requirement should be defined during HO with PSCell
  Option 2 (MTK, Ericsson, CATT, Intel, Nokia): No new interruption requirement for HO with PSCell is needed. Interruption in legacy handover delay requirement can still be applied for the PCell
  Option 3 (Apple, OPPO, Huawei): Interruption in legacy handover delay requirement can be applied for Pcell. No interruption is defined on PSCell.
    If sequential processing is used for HO with PSCell, UE may have an interruption on new PCell due to the PSCell addition.
    If parallel processing is used for HO with PSCell, no need to define interruption requirement.
  Option 5 (NEC): RAN4 to postpone the discussion on interruption uncertainty (TIU) till reply LS from RAN2 is received.
  Option 6 (Qualcomm): Depending on RAN2 LS reply.

## Slide 16: Open issues – sub-topic 2-4
Issue 2-4-1: 2 step and 4 step RACH for HO with PSCell
  Option 1a (ZTE, Nokia, vivo): Include both 2-step RA and 4-step RA into the new requirements made for handover with PSCell. No need to mention 2-step or 4-step in HO with PSCell requirements.
  Option 1b (NEC, Ericsson, ZTE, Nokia): RAN4 to define both 2-step and 4-step RACH requirements for handover with PSCell.
  Option 2 (Apple, Xiaomi, OPPO, MTK): for requirement of HO with PSCell, RAN4 starts the discussion with 4 step RACH first and FFS on 2 step RACH.
  Option 3 (CATT, Qualcomm): Waiting RAN2 response and conclusions of other issues for 2 step and 4 step RACH.

## Slide 17: Open issues – sub-topic 2-4
Issue 2-4-3: RACH occasion on NR-U CC for HO with PSCell
  Option 1 (Ericsson): RAN4 to further study whether RA for spCell on unlicensed carrier with CCA shall be prioritized over RA for spCell on licensed carrier, once CCA is successful.
  Option 2 (CATT, Apple, OPPO, Qualcomm, Huawei, MTK): The NR-U scenario is out of scope of this WID, no need to discuss.
  Option 3 (vivo): Discuss in RAN plenary.