## Slide 1: WF on single RB High PSD
Nokia
3GPP TSG-RAN WG4 Meeting # 99
Electronic Meeting, 19 – 27 May 2021
Agenda Item: 6.3.2.1
R4-2108563

## Slide 2: Background
Contributions on the use of high PSD test model with single RB allocation at band edge for IAB transmitter unwanted emission test (Note 1, 2) have been discussed in RAN4#99-e but no agreement could be reached in the 1st round discussion except to ‘Decouple the discussion on test configuration and single RB High PSD proposal’:
[1] R4-2110140 Discussion on IAB test configurations with TPs to 38.176-1 and 38.176-2 Nokia, Nokia Shanghai Bell
[2] R4-2111174 IAB Common test issue on test model-Conducted Ericsson
[3] R4-2111205 IAB Common test issue on test model-OTA Ericsson
[4] R4-2111398 Discussion on Test models and Test configurations Huawei
The Way Forward from the 1st round discussion is summarized in the following slide.
Note 1: the IAB transmitter unwanted emission core requirements shall apply for all transmission bandwidth configurations from full RBs allocation to single RB allocation.
Note 2: the use of lower PSD test model with single RB allocation is proposed for IAB transmitter total power dynamic range (TPDR) test in R4-2111174 and R4-2111205.

## Slide 3: Way forward on use of single RB high PSD TM
Use test model with full RBs allocation at band edge for IAB transmitter unwanted emission test to proceed the TPs in this meeting.
Companies are encouraged to discuss the issue of single RB high PSD TM for unwanted emission in future RAN4 meetings in maintenance phase with following candidate options for consideration:
Option 2: Only use test model with full RBs allocation at band edge for IAB transmitter unwanted emission test, with a clear statement in the specification that single RB allocation with high PSD should not be scheduled for IAB-MT.
Option 4: Also use test model with single RB allocation with a higher PSD declared by the vendor to be supported for single RB transmission at band edge at least for IAB transmitter operating band unwanted emission test, where the single RB allocation with high PSD would be more likely to impact.