## Slide 1: WF on Repeater Classes and Types
CMCC
3GPP TSG-RAN WG4 Meeting # 99-e R4-2108627
Electronic Meeting, May 19-27, 2021

## Slide 2: WF on repeater classes for DL (access link)
Tentative agreement: at least 2 classes as the baseline for at least FR1
  Also introduce for FR2 if there is any differentiation in DL related requirements between the scenarios/classes. If no requirement differentiation between scenarios, no need for FR2 downlink scenarios/classes.
Further discuss on
  how to differentiate the 2 (or 3) classes
    Option 1: use the same approach as BS/IAB class definition with deployment scenario (e.g. Local Area, Medium Range, Wide Area)
    Option 2: Other option.
  whether a 3rd class is also needed depending on whether FR1 (or FR2).

## Slide 3: WF on repeater Classes for FR1 FDD UL (backhaul link)
Tentative agreement: at least 2 classes as the baseline
Further discuss on
  how to differentiate the 2 classes
    Option 1: use the same approach as IAB class definition with deployment scenario description (e.g. planned/unplanned with a subset of WA/MR/LA)
    Option 2: other option.
  Whether the same principle of how to define/differentiate class also apply for FR1 TDD UL
  whether a 3rd class is also needed.

## Slide 4: WF on repeater Classes for FR2 UL (backhaul link)
Further discuss on
  Whether to limit all repeater’s output power not exceeding PC1level
    Option 1: yes, introduce a single maximum Tx power level equal to PC1
    Option 2: no, introduce two classes, one class with maximum power limited by PC1 and the other without power limit
  how to define class
    Option 1: Similar approach to IAB; i.e. formal class definition (e.g. MR) with deployment scenario description (e.g. planned/unplanned)
    Option 2: class is implicitly defined by power level. (e.g. exceeding PC1, not exceeding PC1)

## Slide 5: WF on relationship between repeater classes for DL and UL TX
  Tentative agreement: UL and DL (TX) classes(or what definition/differentiation will be used) are decoupled.
  Further discuss if receiver requirements also need to be differentiated.

## Slide 6: WF on repeater types
  Tentative agreement: Introduce types 1-C and 2-O
  further discuss if 1-H or 1-O is also needed or at least try to have some decision criteria for introduction of 1-H