## Slide 1: WF for FR2 HST Demodulation
Samsung
3GPP TSG-RAN WG4 Meeting #99-e
Electronic,19th May– 27th May, 2021 Agenda Item: 9.8.5
R4-2108637 Document for: Approval

## Slide 2: Background
      Agreed WFs for FR2 HST WI in previous meetings
  R4-2017828, “WF on NR support for HST in FR2”, Samsung. RAN4#97-e meeting
  R4-2103240, “WF on Deployment Scenario and UE RF Requirement for FR2 HST”, Samsung. RAN4#98-e meeting
  R4-2106100, “WF on FR2 HST Deployment scenario Analysis”, Samsung, RAN4#98b-e meeting
  R4-2106101,”WF on Channel Modeling for FR2 HST”, Nokia, RAN4#98b-e meeting
  R4-2106102, “WF on Demodulation requirement for FR2 HST”, Samsung, RAN4#98b-e meeting

## Slide 3: UE demodulation requirements

## Slide 4: Test Scope
Doppler frequency for PDSCH requirement
  Doppler frequency for PDSCH requirement in Bi-directional deployment scenario, if Bi-directional deployment scenario is introduced
    Option 1: 9722Hz targeting 350km/h at 30GHz
    Option 2: 7000Hz with the smallest RS range of frequency offset estimation
  Doppler frequency for PDSCH requirement in Uni-directional deployment scenario, if Uni -directional deployment scenario is introduced
    9722Hz targeting 350km/h at 30GHz
Whether to introduce PDSCH requirement with HST single-tap channel
  Do not define PDSCH requirement with HST single-tap channel

## Slide 5: Test Scope
PDSCH requirement for Uni/Bi-directional scenario in scenario A and scenario B
  Option 1: Define PDSCH requirement with Uni/Bi-directional scenario for both A and B, Define the test applicability rule to reduce the test effort
  Option 2: Define requirements for both scenario A/B, and Uni/Bi-directional deployment, and not define any applicability between
  Option 3 : Consider output of FR2 HST deployment scenario discussion whether to cover scenario A
  Option 4 : RAN4 define two test cases for HST FR2
    Test 1: HST single tap (Uni-directional) with scenario A
    Test 2: DPS (Uni-directional) with scenario B
    If RAN4 agree to consider both Uni-directional and Bi-directional deployment, either test 1 or 2 apply Bi-directional model

## Slide 6: Test Scope
DPS transmission scheme
  Option 1:
    Define PDSCH requirement with DPS scheme 1a in Uni-directional scenario for scenario A. FFS scheme 1b
    Define PDSCH requirement with DPS scheme 1a and 1b in Uni-directional scenario for scenario B, FFS the number of TCI state configured
    Define PDSCH requirement with DPS scheme 1a in Bi-directional scenario for scenario A and scenario B. FFS scheme 1b
  Option 2: Define both DPS transmission scheme 1a and 1b for both Bi-directional and Uni-directional deployment
    Option 2a : RAN4 define both scheme 1a and 1b if the performance is same, but define the same applicability rule as Rel-16 HST, i.e., if a UE declared supporting > 1 TCI states, the UE will pass scheme 1b and skipped scheme 1a test cases, and if a UE only support 1 TCI state, the UE need to pass scheme 1a and skip scheme 1b test cases.

## Slide 7: Test Setup for PDSCH
RS configuration
  Assumption of RS for frequency offset tracking is up to UE implementation, FFS the RS configuration for PDSCH requirement as
    Configure SSB every 20ms
    Configure TRS every 10ms
    Configure PTRS with KPT-RSS=2 and LPT-RS=1
DMRS configuration
  1+1+1 DMRS configuration for DPS scheme
CBW
  Option 1: 100MHz CBW
  Option 2: 200MHz CBW
  Option 3: Align the CBW configuration for PDSCH and PUSCH
UE frequency error
  Do not consider extra UE frequency error for demodulation tests in FR2 HST WI
    Impact of UE frequency error can be included in companies’ impairment results when RAN4 sets the UE demodulation requirement for FR2 HST

## Slide 8: BS demodulation requirements

## Slide 9: Test Scope
PUSCH requirement
  Introduce PUSCH requirement with Doppler frequency as 19444Hz targeting 350km/h at 30GHz
  Do not introduce PUSCH requirement with Doppler frequency as 14444Hz targeting 260km/h at 30GHz, if no issue with supporting 350km/h was identified

## Slide 10: Test Scope
PUSCH requirement for Uni/Bi-directional RRH deployment scenarios in scenarios A and B
  Option 1
    Define PUSCH requirement with Uni-directional RRH deployment scenario only in scenario A. If both scenarios are introduced for PUSCH requirements, define the test applicability rule to reduce the test effort with only one of them will be selected for testing based on manufacture of declaration.
    If both scenarios A and B for bi-directional RRH deployment scenario are introduced for PUSCH requirements, define the test applicability rule to reduce the test effort with only one of them will be selected for testing based on manufacture of declaration
  Option 2
    RAN4 to define different sets of requirements for Scenario A and Scenario B
    If it is decided that single HST conditions are not sufficient for HST FR2, then to define both PUSCH demodulation requirements for Uni- and bi-directional RRH deployment scenarios
  Option 3: Define test cases for scenario A only
  Option 4: Define requirements for both scenario A/B and Uni/Bi-directional deployment, and not define any applicability rule between them. Manufacture declaration can be used and the case will be tested only when BS vender declares to support it.

## Slide 11: Test Setup for PUSCH requirements
RS configuration
  Option 1: 1 DMRS +PTRS (L=1,K=2)
  Option 2: 2 DMRS+ PTRS (L=1,K=2)
  Option 3: 3 DMRS +PTRS (L=1,K=2)
    Option 3a: If companies have strong concern about DMRS 1+1, create an applicability rule that only one DMRS configuration shall be tested by manufacture declaration
CBW
  Option 1: 100MHz, and 50MHz with test applicable rule
  Option 2: 200MHz, and 50MHz with test applicable rule
  Option 3: 100MHz only
  Option 4: 200MHz only
MCS
  Option 1: MCS 16
    Option 1a: Additional margin can be considered for performance requirement definition to allow different implementation if needed
  Option 2 : both MCS 16 and MCS 17
    Define requirements with MCS17 up to BS declaration support
  Option 3: Configure highest MCS that remains below 20dB SNR, i.e, MCS20
  Further discuss how to guarantee 64QAM operation
  Further discuss how to not preclude any possible BS implementations (with pre and post FFT FOC)
Length of data symbol
  Option 1 : 9
  Option 2 :10

## Slide 12: Test Setup for UL timing adjustment
Waveform
  CP-OFDM
CBW
  Align CBW for UL adjustment and PUSCH demodulation
    Option 1: 100MHz, and 50MHz with test applicable rule
    Option 2: 200MHz, and 50MHz with test applicable rule
    Option 3: 100MHz only
    Option 4: 200MHz only
    PUSCH resource allocation
  Option 1
    Moving UE: 0~32 for 100 MHz CBW, FFS 0~15 for 50 MHz CBW
    Stationary UE: 33~65 for 100MHz CBW, FFS 16~31 for 50MHz CBW
  Option 2: Align CBW for UL timing adjustment and PUSCH demodulation
    Moving UE: 0~32 for 100 MHz CBW
    Stationary UE: 33~65 for 100MHz CBW
  Option 3
    Moving UE: 0~65 for 200 MHz CBW
    Stationary UE: 66~131 for 200 MHz CBW
RS configuration
  Option 1: 1 DMRS+PTRS (L=1,K=2)
  Option 2: 2 DMRS+PTRS (L=1,K=2)
  Option 3: 3 DMRS+ PTRS (L=1,K=2)

## Slide 13: Test Setup for UL timing adjustment requirement
PUSCH mapping type
  Type B
Length of PUSCH allocation
  Align with PUSCH for UL timing adjustment
    Option 1: 10
    Option 2: 9
  MCS
  Align with PUSCH for UL timing adjustment
    Option 1: MCS16
      Option 1a: Additional margin can be considered for performance requirement definition to allow different implementation if needed
    Option 2: both MCS16 and MCS17
      Define requirements with MCS17 up to BS declaration support
    Option 3:Align MCS for UL timing adjustment and PUSCH demodulation requirement, configure highest MCS that remains blow 20dB SNR, i.e., MCS20

## Slide 14: Test Setup for UL timing adjustment requirement
SRS bandwidth configuration
  Option 1
    Option 1a
      C_SRS =11, B_SRS =0 for 40RB, with 100 MHz CBW
      C_SRS = 5, B_SRS=0 for 20RB, with 50 MHz CBW
    Option 1b
      C_SRS =9, B_SRS =0 for 32RB, with 100 MHz CBW
    Option 1c
      C_SRS =17, B_SRS =0 for 64RB, with 100 MHz CBW
      C_SRS = 9, B_SRS=0 for 32 RB, with 50 MHz CBW
  Option 2: C_SRS=33, B_SRS=0 for 132RB with 200MHz CBW
SRS Transmission comb: KTC=2
SRS Transmission periodicity : KSRS=10
Slots in which sounding RS is transmitted
  The last symbol in slot#3 in radio frames for 120KHz SCS
Test Parameters for timing offset
  Option 1:
    A: 1.25 us
    Δw: 1.04 s-1
  Option 2: FFS on A =2.5 us
Test Parameters for timing offset
  Option 1
    [Δt-(TA-31)x16*8Tc]
  Note: The timing different can be updated with taken into account the output of possible enhancements for timing adjustment command discussion in RRM session

## Slide 15: Test setup for PRACH
Frequency offset
  19444Hz with 350km/h at 30GHz carrier frequency
Test Preamble Configuration for Ncs
  Ncs =0 as baseline
Timing offset configuration
  Option 1: Reuse Rel-15 FR2 timing offset configuration for PRACH, i.e., 0.8us
  Option 2: Update the timing offset configuration based on the largest expected cell radius, i.e., derived from scenario B
    Note
      Scenario A (Ds=700m, Dmin=10m), cell radius = 700m
      Scenario B (Ds=700m, Dmin=150ms), cell radius = 716ms
Timing error tolerance
  0.07us for AWGN, as a default value for 120KHz SCS

## Slide 16: Testability

## Slide 17: Testability issues for FR2 HST UE
Option 1: Do not discuss any testability issue aspects in HST FR2 WI unless it is captured in WID
Option 2 : Assume static UE and single Probe
Option 3: Combine RRM and Demod requirements as a single feature to support HST FR2 operation

## Slide 18: Observations (information)
RS configuration to enable 350km/h for PDSCH
  Observation 1 (R4-2109216)
    When UE is served by one RRH the Doppler frequency trajectory is continuous and there are no problems to track it by TRS
    To performance switching from one RRH to another UE needs to handle frequency jump which is different for different deployments scenarios. For unidirectional it can be up to max Doppler frequency and in bidirectional up to double max Doppler frequency
  Observation 2 (R4-2110720)
    Maximum Doppler frequency based on TRS is 14000Hz if we do not assume frequency error
    Assuming zero frequency error, the range of maximum Doppler frequency estimation based on TRS is 14kHz
    In a bidirectional deployment, if Fc=30GHz and the train speed is 350 Km/h, a UE using TRS processing for frequency offset tracking will experience a maximum Doppler shift larger than 19kHz when switching between RRHs pointed in opposite directions, outside of the TRS range and the impact on performance is potentially unbounded.
    Using both SSB and TRS for UE Frequency Offset Tracking does not solve the problem of the maximum Doppler shift larger than TRS FO estimation range, if the first resource received at the UE after the switch to a new RRH is TRS and not SSB
    Combining different resources (with different spectral characteristics as in the case of SSB and TRS) for FOT requires a dedicated UE implementation
    Feasibility of supporting maximum speed of 350km/h in downlink using TRS (4 symbol interval) and SSB for frequency offset tracking under bi-directional RRH deployment, assumes an increased complexity in the UE implementation of FOT schemes compared to a baseline UE implementation
  Observation 3 (R4-2110643)
    Maximum Doppler frequency based on TRS is 14000Hz if we do not assume frequency error
    Maximum Doppler frequency based on TRS is 11,000Hz if we assume frequency error of 0.1ppm at 30GHz.

## Slide 19: Observations (information)
PUSCH requirement for Uni/Bi-directional RRH deployment scenarios in scenarios A and B
  Observation 1 (R4-2109806)
    Similar performance can be achieved for both bi-directional and un-directional deployment scenario in scenario A
    Similar performance can be achieved for Uni-directional scenario in scenario A and B
    Better performance can be achieved for bi-directional scenario in scenario B compared with Uni-directional scenario
  Observation 2 (R4-2111067)
    The difference in SINR values corresponding to 30% and 70% of PUSCH maximum TPut with the same test configuration in Scenario A and Scenario B is less than 0.3 dB.
    Scenario B looks to be slightly less challenging because the same relative TPut levels can be achieved at a bit lower SINR
    The difference in SINR values corresponding to 30% and 70% of PUSCH maximum TPut with the same test configuration in Uni- and bi-directional deployments is less than 0.1 dB
    The Uni-directional and bi-directional scenarios are fundamentally different from the Doppler trajectory point of view

## Slide 20: Observations (information)
RS configuration for PUSCH
  Observation 1 (R4-2109806)
    The overhead of 1DMRS +PTRS (L=1, K=2) configuration is the smallest compared with other RS configuration schemes
    With 1 DMRS+PTRS (L=1, K=2) configuration, better performance can be achieved in terms of maximum throughput compared with other RS configurations
  Observation 2 (R4-2110730)
    The performance difference is negligible for PUSCH configured with PT-RS +(1+0) DM-RS and PT-RS + (1+1) DM-RS symbols
  Observation 3 (R4-2110532)
    There is negligible performance difference between DMRS 1+1 and DMRS 1+1+1.
    There is about 1.2dB performance degradation between DMRS 1 and the others due to large residual frequency offset using PTRS only for frequency offset estimation
  Observation 4 (R4-2111067)
    There is no significant difference in the demodulation performance between the cases with only one and two DM-RS per slot when PT-RS is present. We can expect a similar behaviour when two additional DM-RS symbols are used
    It is practical to use at least one additional DM-RS symbol per slot in real implementation where fast fading is inevitably present. Moreover, in HST FR1 PUSCH requirements two additional DM-RS symbols are used

## Slide 21: Contributions List in RAN4#99-e
T-doc No. | Title | Company
R4-2109216 | View on DL demodulation requirements for HST FR2 | Intel Corporation
R4-2109217 | View on UL demodulation requirements for HST FR2 | Intel Corporation
R4-2109749 | Discussion on Reference Signal for UL and DL | ZTE Corporation
R4-2109750 | Discussion on UE Demodulation Requirements for FR2 HST | ZTE Corporation
R4-2109805 | View on demodulation requirement for Rel-17 FR2 HST | Samsung
R4-2109806 | View on BS demodulation requirement for Rel-17 FR2 HST | Samsung
R4-2109807 | View on UE demodulation requirement for Rel-17 FR2 HST | Samsung
R4-2110530 | Discussion on BS demodulation requirements for FR2 HST | Huawei, HiSilicon
R4-2110531 | Discussion on UE demodulation requirements for FR2 HST | Huawei, HiSilicon
R4-2110532 | Discussion on general issues for NR FR2 HST demodulation requirements | Huawei, HiSilicon
R4-2110643 | UE demodulation requirements for HST FR2 | Ericsson
R4-2110720 | Maximum UE velocity and RS configuration for FR2 HST UE Demod Performance Test | Qualcomm Incorporated
R4-2110730 | BS demodulation requirements for HST FR2 | Ericsson
R4-2111067 | On HST FR2 BS Demodulation Requirements | Nokia, Nokia Shanghai Bell
R4-2111108 | On HST FR2 DM-RS Configuration in UL Direction | Nokia, Nokia Shanghai Bell

## Slide 22: Reference
[1] R4-2108454, “Email discussion summary for [99-e][329] NR_HST_FR2_Demod”, Samsung