## Slide 1: WF on FR1 TRP TRS
vivo
3GPP TSG-RAN WG4 Meeting #99-e R4-2108620
Electronic Meeting, May 19-27, 2021
Agenda item: 9.2.1
Document for: Approval

## Slide 2: General
Workplan for FR1 TRP TRS WI
  The workplan of FR1 TRP TRS WI is approved in [R4-2108624]
TR 38.824 for FR1 TRP TRS OTA test methods
  TR skeleton is approved in [R4-2108625]
Coordination with RAN5
  LS to RAN5 on MU work is approved in [R4-2108622]
  How to coordinate with RAN5 is also captured in the LS
UE type for FR1 TRP TRS testing
  Smartphone is selected as 1st priority for FR1 TRP TRS WI
Head and Hand phantoms for FR1 TRP TRS OTA test methods
  LS to CTIA for coordination on phantoms for OTA testing is approved in [R4-2108622]

## Slide 3: FR1 OTA test methods
Use scenarios for test methods
  Talk mode using head & hand phantom for narrow devices between 56 mm and 72 mm and for wide devices with a width >72 mm and <92 mm.
  Browsing mode using hand phantom for narrow and wide phones
  Free Space for devices not used in talk or browsing mode
Measurement distance for FR1 TRP TRS test system
  The effective antenna approach defined in TR 38.827 for RTS method should be adopted for FR1 TRP TRS testing, the minimum range length is suggested to be 1.2 m.
Large bandwidth impacts
  A MU element related to frequency flatness needs to be considered for FR1 TRP TRS test system
SA test system
  For FR1 SA, the test system and test procedure for LTE can be reused as much as possible

## Slide 4: Power configuration for EN-DC (1)
Power splitting between LTE and NR
  For EN-DC OTA testing, the fixed-power-splitting approach should be configured, the following options can be considered:
    Option 1: UE transmit LTE and NR with a 50%-50% equal power splitting under EN-DC mode.
      Option 1a: exact 50%-50% power splitting with fixed 50% power for each RAT, e.g. for PC3, 20 dBm LTE and 20 dBm NR
      Option 1b: rough 50%-50% power splitting with only fixed 50% power for LTE, e.g., for PC3, 20dBm LTE and no upper power limit setting for NR
    Option 2: UE transmit a significant different power for LTE and NR under EN-DC mode
      Option 2a: maximum power for NR and minimized power for LTE (stable LTE connection should be confirmed with, e.g. 10dBm UL power)
      Option 2b: maximum power for LTE and minimized power for NR (stable NR connection should be confirmed with, e.g. 10dBm UL power)
    Option 3: other configuration is not precluded
Special OTA test method for DPS function
  RAN4 further discuss whether it is necessary to develop OTA test method to quantify the DPS function of FR1 UEs.

## Slide 5: Power configuration for EN-DC (2)
Tx configuration for TRP and TRS
  Given maximum Tx should be configured for both TRP and TRS, RAN4 need to decide whether same Tx configurations should be used for TRP and TRS:
    Option 1: EN-DC Tx Power splitting for TRP and TRS testing should be the same.
    Option 2: EN-DC Tx power splitting for TRP and TRS should be different.
For EN-DC, whether two RATs need to be measured
  FFS whether both LTE and NR should be measured under EN-DC mode.
  Clarification from RAN Plenary on whether LTE measurement under EN-DC mode is within the scope of the WID is helpful.
  This topic is related to the Tx power configuration of EN-DC, suggest to make decision on EN-DC power splitting first

## Slide 6: UE configuration with multi-antenna
Tx antenna switching
  Option1: Function Off. This is traditional way for OTA testing.
    Potential vendor declaration and test mode FFS
    Minimum requirement shall be satisfied by the antenna with the best TRP performance
  Option 2: Function On. How to test the TRP at this condition is FFS.
Rx antenna switching
  RAN4 further study how to treat the UE with Rx antenna switching.

## Slide 7: Test Time Reduction
Reduce EN-DC combinations
  RAN4 should define a mechanism on testing time reduction of EN-DC combinations.
Reduce SA test time
  Test time reduction techniques are desired for SA test methods.
  Companies are encouraged to share views on how to reduce the FR1 OTA testing time

## Slide 8: Co-operation between RAN4 and RAN5 on this WI
How to draft Annex B: Measurement Uncertainty for TR 38.834
  RAN5 is responsible for MU assessment of the test methods, and RAN5 can send LS to RAN4 with the endorsed TPs in the attachment for TR 38.834.
  Once RAN4 receives the LS, the Editor can implement the RAN5 endorsed Text Proposals (TPs) directly for this RAN4 TR.

## Slide 9: Next Steps
  SA and EN-DC test setup and calibration procedure
  Ripple test procedure for SA and EN-DC test system
  Detailed configure power for EN-DC (fixed-power-splitting approach)
  Methodology on how to reduce TRP TRS testing time
  How to configure UE with TX/Rx switching
  How to develop head&hand phantoms
  How to configure the test parameters for each band (e.g. center frequency, bandwidth, RBs..)
  Test procedures for SA and EN-DC