## Slide 1: WF on MSD due to triple beat of intra-band UL CA UL + FDD UL configurations
Qualcomm Inc., Skyworks Inc., …
R4-2107803
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021

## Slide 2: Background
Band combinations with 3 ULCCs were analyzed in [1]
3 active UL CCs create triple beat distortion and can lead to RX de-sensitization.
Suspect band combinations from [1][2] that were detected to create triple beat distortion are highlighted and shown in table on the right ->
3A_n7B
28A_n7B
1A_n7B
1C_n3A
2C_n41A
2C_n71A
2A_n77(2A)
3A_n41C
3C_n1A
3C_n5A
3C_n7A
3C_n28A
3C_n41A
3A_n77(2A)
3A_n78(2A)
3C_n77A
3C_n78A
3C_n79A
7C_n1A
7C_n3A
7C_n5A
7C_n28A
7C_n78A
8A_n79C
25A_n41C
30_n77(2A)
39C_n41A
40C_n78A
41C_n3A
41C_n77A
41C_n78A
41C_n79A
42C_n28A
42C_n3A
66_n77(2A)

## Slide 3: Background - detection
The detection mechanism for the 1st order triple beat is shown below from [2]
    Duplex Offset is the duplex offset of the victim FDD band
    ULCAMBW is the non-contiguous 2 tone allocation spacing
    TXMBW and RXBW is the FDD victim band TX transmission measured BW and the RX DL channel BW respectively
Band X_UL
Band Y UL
Band X_DL
ULCAMBW
ULCAMBW
Duplex
TripleBeat
1st order TripleBeat
2nd order TripleBeat
3rd order TripleBeat
ULCAMBW
ULCAMBW
ULCAMBW

## Slide 4: Background - analysis
Triple beat distortion occurs at RX and TX and is a 3rd order non-linearity that is mainly α (TX22TX1) and is more prominent for non-contiguous RB allocations.
For TX
    Both forward and reverse triple beat products can occur at the transmitter
    It was shown that the triple beat distortion at the ULCA transmitter path is dominant for TX due to 2:1 variation with ULCA output power
    PCB isolation from FDD band PA to ULCA band PA will affect forward TX distortion
    ULCA Filter rejection and antenna isolation will affect the reverse TX distortion
For RX
    RX path filter rejection for both TX bands and the 3rd order non-linearity specification determines the RX triple beat distortion
Power Back-off
    For ULCA band, the power is backed off to meet the general emission requirements or CA_NS_04 requirement.
      this can be a function of tone spacing.
    For FDD band, the power is backed off to meet the NS_01 requirement
    Backed off power must meet the power class requirement
    Worst case triple beat will occur with equal power on the 3ULCCs if both power class and emission requirements are met.

## Slide 5: WF: Example Analysis PC3 capable bands
Tentatively agree on the following MSD values for the following band combinations for power class 3.
Further verify power back off to meet power class and emission requirements
  ie. DC_3A_n77(2A), DC_3A_n78(2A) are at MSD = [0]dB, pending further verification for back-off and RX linearity
Further check if triple beat can land in a 3rd DL carrier other than duplex offset of FDD carrier
Back-off can be applied per carrier as indicated or per band.

## Slide 6: WF: Framework for specification
Mainly consider the 1st order triple beat α (TX22TX1) of 3rd order non-linearity -> this is shown in the table as triple beat order 1. Detection ->
Further check the 2nd order triple beat α (TX24TX1) of 5th order non-linearity -> this would be shown in the table as triple beat order 2. Detection ->
  This may come into play for higher TX power for power class 2 capable bands
  Neglect the 3rd order triple beat α (TX26TX1) of 7th order non-linearity. Detection ->
Verify MSD test points including RB positions and consider following framework for specification.
  If FDD victim TX band allocation is fully allocated, then RB positions in table are chosen so that ULCA tone spacing is at the duplex offset
  Tone spacing and RB positions also chosen for least amount of back-off to meet emission requirements
NR or E-UTRA Band / Channel bandwidth / NRB / MSD |  |  |  |  |  |  |  | 
EN-DC Configuration | EUTRA or NR band | UL Fc (MHz) | UL/DL BW (MHz) | UL LCRB | DL Fc (MHz) | MSD (dB) | Duplex mode | Triple beat order
DC_3A-n41C | 3 | 1782.5 | 5 | 25 | 1877.5 | [12.7] | FDD | 1
 | n41C | 2555 2635 | [80] [80] | [1 (RBstart=88)] [1 (RBstart=128)] | 2555 2635 | N/A | TDD | N/A
DC_25A-n41C | 25 | 1912.5 | 5 | 25 | 1992.5 | [5.4] | FDD | 1
 | n41C | 2545 2595 | 90 100 | 1 (RBstart=150) 1 (RBstart=122) | 2545 2595 | N/A | TDD | N/A
DC_8A-n79C | 8 | 912.5 | 5 | 25 | 957.5 | [0] | FDD | 1
 | n79C | 4545 4645 | 100 100 | 1 (RBstart=212) 1 (RBstart=60) | 4545 4645 | N/A | TDD | N/A

## Slide 7: References:
[1] R4-2107627 Triple beat and 3ULCC MSD, Qualcomm Incorporated, R4#99-e
[2] R4-2111016 MSD Due to NR Intra-band ULCA IMD within Inter-band Combinations, Skyworks, R4#99-e
[3] R4-2105335 Way forward on analysis and framework of triple beat issue of 3CC UL with contiguous intra band UL CA , Qualcomm Inc., R4#98bis-e
[4]