## Slide 1: Way forward for MSD improvement
T-Mobile USA, …
3GPP TSG-RAN WG4 Meeting # 98-bis-e R4-2107808
Electronic Meeting, Apr. 12-20, 2021

## Slide 2: Background
MSD is defined to allow flexible architecture options
Operators have found and confirmed that sensitivity degradation in real world UEs can be 20 dB better than MSD in the specs [1]
If sensitivity degradation is small single digits, operators might safely ignore it, but if it is >20 MHz, then the network may want to avoid problematic configurations for those UEs, or deploy an intelligent scheduler schedule around problematic allocations for UEs with high sensitivity degradation in some combinations.
With no UE capability differentiation, the operators will have a choice to either need to ignore the MSD which would impact UEs with high sensitivity degradation, or avoid the problematic combinations or allocations for all UEs, negating the performance improvements of the UEs with low sensitivity degradation.

## Slide 3: Proposal
Proposal 1: RAN4 to introduce a new UE capability bit to allow a UE indicate support for improved MSD
Proposal 2: RAN4 will choose a (preferably low single digit) improved MSD value that a UE could declare support for a given combination with a new capability bit
  RAN4 could either define a single improved MSD value for all the types of MSD, or it could choose one level for harmonics, one level for harmonic mixing, one level for cross-band isolation and one value for Intermods.
Proposal 3: The new capability would be signalled per UL/DL band combination

## Slide 4: References
[1] R4-2111492, “MSD and real-world implications,” T-Mobile USA, Deutsche Telekom, Verizon, CHTTL, AT&T, Dish Network