## Slide 1: WF on Tx power tolerance for PC2 n34 and n39
Moderator (CMCC)
3GPP TSG-RAN WG4 Meeting # 99-e R4-2107829
Electronic Meeting, May. 19-27, 2021

## Slide 2
Issue 1-1-1: UE MOP and Tx power tolerance for n34/n39 of Power class 2
Proposals
  Option1:
    The MOP and Tolerance for single antenna port are to be specified as 26dBm ±2 dB for band n34/n39 of power class 2
    The MOP and Tolerance for UL MIMO are to be specified as 26dBm +2/-3 dB for band n34/n39 of power class 2
  Option2: The power tolerance for PC2 for n34/n39 is +2/-3dB. Regardless of single antenna port or UL MIMO case.
  Option3: PC2 n34/n39 MOP lower tolerance should be +2/-2 dB.
Agreement:
Option2: The power tolerance for PC2 for n34/n39 is +2/-3dB. Regardless of single antenna port or UL MIMO case.
  PC2 n34 and n39 Tx tolerance for 1PA can be re-evaluated in the future

## Slide 3
Thanks