## Slide 1: WF on release independent for simultaneous Rx/Tx CHTTL, Huawei
3GPP TSG-RAN WG4 Meeting #99-e R4-2107842
Electronic Meeting, May.19th – May.27th 2021

## Slide 2: Background
The release independent issue for simultaneous Rx/Tx capability was discussed during RAN4#99e email thread #134.
  Issue 1-4-1: Specify/change the simultaneous RxTx capability only in the Rel-17 spec in this WI and keep the capability indication unchanged for Rel-15/Rel-16 band combinations to avoid NBC issue
  Option 1: Yes.
  Option 2: No
    During the first round email discussion, 4 companies supported option 1, meanwhile 4 companies supported option 2, and one company was open to option 2.
  Issue 1-4-2: Follow the normal release independent manner for a band combination introduced in Rel-17 with indication of the simultaneous Rx/Tx capability
  Option 1: Yes.
  Option 2: No
    During the first round email discussion, two companies supported option 1, two companies asked for clarification on the “normal release independent manner”, one company commented that there is nothing to do in Rel.17.

## Slide 3: WF on release independent for simultaneous Rx/Tx
WF for issue 1-4-1:
  At least in the Rel.15 RAN4 specifications, the indication of mandatory/optional simultaneous Rx/Tx capability support for each combination should remain unchanged.
WF for issue 1-4-2:
  For the FDD-TDD and TDD-TDD band combination introduced in Rel.17 38.101-1, 38.101-2, 38.101-3, the simultaneous Rx/Tx capability affiliated to the band combination is considered as release independent from Rel.15 if the band combination is mandatory to support simultaneous Rx/Tx in Rel-17.
    For example: A band combination is specified as mandatory support of simultaneous Rx/Tx in Rel-17. If Rel-15 or Rel-16 UE wants to support this band combination with release independent manner, it shall support simultaneous Rx/Tx.

## Slide 4: Reference
[1] R4-2111448, On principles for deciding simultaneous Rx/Tx capability, Huawei,
[2] Email discussion summary for [98-bis-e][134] Simultaneous_RxTx