## Slide 1: 3GPP TSG-RAN WG4 Meeting # 99-e Online meeting, 19-27 May, 2021
Xiaomi
WF on CA BW classes
R4-2107859

## Slide 2: Agreement
Granularity for new CA BW classes in FR2
  Define new CA BW classes with 100 MHz granularity.
  Fallback group 2 (FBG2) (200MHz)
  Will be introduced with 200MHz CC to support aggregated channel BW up to 1600 MHz:
CA BW Class | Aggregated Channel BW | Number of CC | Fallback Group
R | 800 MHz < BWChannel_CA ≤ 1000 MHz | 5 | 2
S | 1000 MHz < BWChannel_CA ≤ 1200 MHz | 6 | 
T | 1200 MHz < BWChannel_CA ≤ 1400 MHz | 7 | 
U | 1400 MHz < BWChannel_CA ≤ 1600 MHz | 8 | 

## Slide 3: Way Forward (1)
Additional fallback groups in FR2
  Options:
  Option 1: Introduce fallback group 1 (FBG1) (400 MHz)
  Option 2: Introduce fallback group 3 (FBG3) (100 MHz):
  Tentative agreements:
  Introduce FBG1 with 400 MHz CC’s
  FFS for FBG3 with 100 MHz CC’s
CA BW Class | Aggregated Channel BW | Number of CC | Fallback Group
 | 1200 MHz < BWChannel_CA ≤ 1600 MHz | 4 | 1
CA BW Class | Aggregated Channel BW | Number of CC | Fallback Group
 | 800 MHz < BWChannel_CA ≤ 900 MHz | 9 | 3
 | 900 MHz < BWChannel_CA ≤ 1000 MHz | 10 | 
 | 1000 MHz < BWChannel_CA ≤ 1100 MHz | 11 | 
 | 1100 MHz < BWChannel_CA ≤ 1200 MHz | 12 | 
 | 1200 MHz < BWChannel_CA ≤ 1300 MHz | 13 | 
 | 1300 MHz < BWChannel_CA ≤ 1400 MHz | 14 | 
 | 1400 MHz < BWChannel_CA ≤ 1500 MHz | 15 | 
 | 1500 MHz < BWChannel_CA ≤ 1600 MHz | 16 | 

## Slide 4: Way Forward (2)
Denotation for new CA BW class in FR2
  Options:
  Option 1: Use single alphabets for now and come up with additional (two letters, apostrophe) until they run out.
  Option 2: Use two letters already now.
  Status analysis
  There are only remaining 9 (except N) capital letters can be used for new CA BW classes in FR2. But at least 4 CA BW classes in FBG2 and 8 CA BW classes in FBG3 will be introduced in this meeting.
  Issue
  No matter choose Option1 or Option2, how to use additional denotation for new CA BW class in FR2 still need discuss.
  Tentative agreement:
  Option 1
  FFS for two letter denotation if FBG 3 agree to introduce.

## Slide 5: Reference
[1] R4-2109528, Considerations on new CA BW class notation, ZTE Corporation.
[2] R4-2110161, New FR2 CA BW classes, Apple.
[3] R4-2110185, Discussion on FR2 new CA BW class denotation and definition, Xiaomi
[4] R4-2111381, On FR2 CA bandwidth class, Huawei, HiSilicon
[5] R4-2107665, Email discussion summary for [99-e][139] NR_RF_FR2_req_enh2_Part_3, Moderator (Qualcomm)