## Slide 1: WF on remaining issues for system parameters in NRSL_enh_Part1
Agenda item: 9.14.3
Source: LG Electronics
3GPP TSG-RAN WG4 Meeting #99-e R4-2108001
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Background
In RAN4 #99-e meeting, RAN4 treated as follow issues in 2nd round
  Issue 1-1-1: Operating bands & CBW for SL enhancement
  Issue 1-1-3: Channel raster & sync. Raster in licensed band
    Tentative agreements: RAN4 agreed as following tentative agreement based on 1st round
    Option 1: Keep the previous RAN4 agreement to follow the Channel raster & synch. Raster of NR Uu for SL enhancement in Rel-17.

## Slide 3: WF: TR38.785 spec. structure
Issue 1-1-1: Operating bands & CBW for SL enhancement
Proposals
  Option 1: All operating band & CBW can be captured in section 7. But the related RF requirements and coexistence evaluation is described in the different sections in TR38.785.
  Option 2: same section will be used according to SL enh. operation
    In section 5.1, PC2 V2X UE, the operating band and the related RF requirements will be captured.
    In section 5.2, Intra-band con-current operating band and the related RF requirements will be captured
    In section 7, SL enh operating band will be captured. Section 8 and section 9 will be captured the Tx and Rx requirements for SL enhancement.
Agreement
  Option 2
    Editor can change the TR accordingly
Notes: CATT: From CATT point of view, we do not have strong views. Option 1 is normal way to capture the normal band in TS and TR. We still think if company has concern on Option 1. We can add some note for it.
Xiaomi: prefer Option 1. We can accept Option 2.
Vivo: for Option 2, why we should put band definition in RF section. This TP does not follow option 2. band combination is defined in section 7 rather section 5. If we go with Option2, we should change the existing TR.
LGE: it is important to pick which band to support which service. When we capture all the band in section 7, there is no distinction. We prefer to capture them in the same section. TP can be revised.

## Slide 4: WF: System parameters
Issue 1-1-3: Channel raster & sync. Raster in licensed band
  Tentative agreements in 1st round: Keep the previous RAN4 agreement to follow the Channel raster & synch. Raster of NR Uu for SL enhancement in Rel-17.
Proposals
  Option 1: Channel raster for SL enhancement follows that for NR Uu. But, sync raster for SL enhancement follows that for NR V2X
  Option 2: Both Channel raster & synch raster for SL enhancement follows that for NR Uu.
Agreement
  Option 2
Notes: LGE: most companies support Option 2.
CATT: we are OK with option 2. n14 is also operating in coverage scenario.
Vivo: for Option 2, we have concern, which adopt channel and sync raster. But we had agreed TP where we do not consider sync raster. There is no need for sync raster for SL enhancement.
Xiaomi: to Vivo, in last meeting, AT&T agreed that there will be only PC5 public safty scenario. That is reason to agree no sync. But with n14 in-coverage, we have new scenario and we need sync raster.
LGE: we have new scenario and should consider both rasters.

## Slide 5: Reference
[1] R4-2107668, “RAN4#99-e_summary_142_NRSL_enh_Part1,” Moderator (LG Electronics)